## Slide 1: SA2: Analysis on UDM/AUSF Discovery (Agenda 6.5.4)
NEC, Nokia, Ericsson
S2-186078

## Slide 2: SA3 LS [S3-181494] to SA2, CT1 and CT4
  1. Overall Description:
    SA3 had discussion on AUSF/UDM selection and SUCI parameters and would like to bring the attention of CT1, CT4 and SA2 few points on this.
    1) AUSF/UDM selection: In networks where multiple UDMs are deployed, a parameter in addition to the MNC+MCC is necessary for the selection of the correct UDM instance and routing the authentication request. SA3 expects this parameter to be in the clear for the proper routing. SA3 would like remind that AUSF/UDM selection/routing based on range value in the encrypted MSIN field is not feasible.
    2) SUCI parameters: The new encrypted subscription identity SUCI needs special attention from various WGs. SUCI contains fields to represent e.g., Encryption Algorithm/Curve identifier, Ephemeral Public key, Encrypted MSIN, MSIN MAC etc. For a complete list of parameters please refer to CR S3-181495, TS 33.501 Annex C.3.4. In addition to these fields, MCC, MNC and the UDM instance selection parameter need to be represented.

## Slide 3: Problem statement
How should NF Consumer discover the right AUSF group, right UDM Group when UE provides the SUCI only?
Is SUPI sufficient to find a UDM/AUSF instance?

## Slide 4: Principles for AUSF/UDM Discovery (1/3)
CT4 agreement on the SUCI format (C4-184575):
CT4 Routing Indicator, consisting of four decimal digits. It contains 1 to 4 digits assigned by the home network operator and provisioned in the USIM, that allow together with the MCC and MNC to route network signalling with SUCI to AUSF and UDM instances capable to serve the subscriber. If there are less than 4 digits in the Routing Indicator, one or more "0" digits shall be inserted at the left side to fill the 4 digits coding of Routing Indicator;
When SUPI is available, Routing ID is not needed for UDM Discovery nor AUSF Discovery
Routing ID is configured by the operator in the UE. Routing ID helps hide network topology from the UE.
Any AUSF instance within an AUSF Group can process the same group of UE(s) as agreed for the definition of AUSF Group as in S2-183996; Any UDM instance within an UDM Group can process the same group of UE(s) as agreed for the definition of UDM Group as in S2-183996;

## Slide 5: Principles for AUSF/UDM Discovery (2/3)
    6. Routing ID <-> AUSF Group ID; Routing ID <-> UDM Group ID mapping is expected to be stored within the network by the operator e.g. via OA&M in the NRF or during NF Registration with the NRF.
    7. Standards should allow Routing ID and Group ID to change independent of each other;
    8. Routing ID change could be periodic to ensure end user’s privacy and impact UE configuration but Group ID change (e.g. it can be frequent or infrequent dependent on operator deployment) shall not impact UE configuration (i.e. not require re-configuration whenever an operator tries to reconfigure their subscribers from one UDM/AUSF instance to another for whatever reason).
    9. For instance, Subscriber migration from one AUSF Group to another AUSF Group, one UDM Group to another UDM Group should not require re-configuration of SUCI in the UE.
    10. Also, AUSF and UDM Groups may be independent of each other in actual deployment. Standards need not enforce strict direct correlation.

## Slide 6: Principles for AUSF/UDM Discovery (3/3)
    Way Forward:
    VPLMN NF can use the MNC+MNC to find the right PLMN
    VPLMN NF can also use the Routing ID that is part of SUCI, to find the right UDM/AUSF
    HPLMN NF can also use the Routing ID that is part of SUCI, to find the right UDM/AUSF
    When SUPI is available, Routing ID is not needed for UDM Discovery nor AUSF Discovery

## Slide 7: Company Contributions in SA2#127bis
Source | Proposal | 
Ericsson | S2-184772 – Discussion on AUSF/UDM selection using SUCI Use of the recently defined AUSF/UDM Group IDs Proposal 1: Include as output of the AUSF/UDM discovery procedure the AUSF/UDM Group ID so that AMF and AUSF can make use of this information if needed in subsequent AUSF/UDM selection procedures using SUCI. Proposal 2: Include as input for AUSF/UDM selection procedure the AUSF/UDM Group ID in TS 23.501. Proposal 3: Combine the Group IDs defined for AUSF/UDM in a single Group ID representing the AUSF/UDM instance(s) managing a specific set of SUPIs. It sounds reasonable that the AUSF/UDM Group IDs assigned to a given SUPI are defined consistently (i.e. using the same value) and thus the AUSF and UDM instances managing a set of SUPIs could be represented by a single Group ID parameter. Conclusion 4: It is required that the home network pays special attention to how the values for the AUSF/UDM Group IDs are assigned to properly protect the subscriber privacy. Proposal 4: Include these privacy considerations in the definition of the AUSF/UDM Group ID if they are used as the additional parameter within SUCI to be used for AUSF/UDM selection using SUCI. If SA2 cannot agree on the use of the AUSF/UDM Group ID for this purpose, SA2 should define a new parameter instead. S2-184773 - NF Registration via the NRF [TS 23.501] AUSF/UDM Group ID: This refers to one or more AUSF and UDM instances managing a specific set of SUPIs. UDR Group ID: This refers to one or more UDR instances managing a specific set of SUPIs. NOTE 3: It is also expected that the NRF stores a mapping between AUSF/UDM Group ID and SUPI(s) and, UDR Group ID and SUPI(s), AUSF Group ID and SUPI(s) to enable discovery of UDM, UDR, AUSF using SUPI, SUPI ranges as specified in clause 6.3. NOTE 4: The UE includes the AUSF/UDM Group ID within the SUCI so it can be used as input for AUSF/UDM selection when different AUSF/UDM instances manage specific sets of SUPIs within the HPLMN. S2-184774 - NF Discovery via the NRF [23.502] Includes the UDM/AUSF Group Id as possible output of the UDM/AUSF discovery procedure. Later it is used as input for the AUSF/UDM selection when SUCI is used and different UDM/AUSF instances manage specific sets of SUPIs. | 

## Slide 8: Company Contributions in SA2#127bis
Source | Proposal
Nokia | S2-184933 - NRF Service Operations [TS 23.502] Nnrf_NFManagement_NFRegister service operation: If the consumer is UDM, UDR or AUSF, they can include UDM Group ID, UDR Group ID, AUSF Group ID, Routing ID . Nnrf_NFDiscovery service operation: If the target NF is UDM or AUSF, the request may include Routing ID that was part of SUCI. S2-184938 - 23.502: UDM-AUSF Discovery [TS 23.502] Include Routing ID part of SUCI for UDM discovery and AUSF discovery 23.501: UDM-AUSF Discovery [TS 23.501]
NEC | S2-185347 - Updates to clause 6.3.8 UDM discovery function [TS 23.501] Use of SUPI range indicator (when more than one UDM instance(s) or UDM are deployed in a network and SUPI is not available). S2-185360 - Changes to usage of SUPI as NF instance(s) service discovery information [TS 23.501] 4.17.4 NF/NF service discovery in the same PLMN: The NF service consumer invokes Nnrf_NFDiscovery_Request, where parameter may include optionally SUPI or SUPI range indicator. In case the target NF is UDR, if SUPI or SUPI range indicator was used as optional input parameter in the request, the NRF shall provide the UDR instance(s) that matches the optional input SUPI or SUPI range indicator. S2-185363 - Reply LS to “LS on AUSF/UDM instance selection and SUCI parameters”
CATT | S2-185251 Update to UDM discovery [TS 23.501] 1. Clarifying that the unencrypted routing assistance information within the SUCI should be used to discover a UDM in HPLMN. 2. Clarifying that the SUCI can be used for UDM discovery.