## Slide 1: Discussion on eSBA Key Issue 3: Improvements to service framework related aspects
Oracle/Verizon
3GPP SA WG 2 Meeting#128
Vilnius Lithuania, 2 – 6 July 2018
S2-186658

## Slide 2: Introduction
This paper tackles Key Issue 3: Improvements to service framework related aspects.
The paper proposes a third solution. This solution follows the key principles of solutions 3.1 and 3.2. However, in addition, it combines the pros of solutions 3.1 and 3.2 and resolves their cons.
The paper compares the new solution to the two existing ones.

## Slide 3: Solution #3 (a new proposed Solution)
NF1(BL)
Service Framework
NF2 (Business Logic)
BL = Business Logic
NF3(BL)
NF4(BL)
NRF (Business Logic)
SBI
SBI
SBI
SBI
Svc Reg. management
Discovery management
Authorization management
Load Balancing
Overload Control
More Services…

## Slide 4: Description and Key principles of Solution #3
Keeping the Rel-15 NFs intact by letting them take care of the Business Logic only and keeping Rel-15 services/HTTP API as is, i.e. the service framework consumes native messages generated by 3GPP service consumers/producers.
Having the Rel-15 NFs talk to the Service Framework (via the existing Rel-15 services/HTTP API or native SBI used for 3GPP services) as a mediator between the NFs.
  Removes the burden of handling all of the Services communication aspects from the NFs/service consumers/producers.
  Discovery/selection of peer service instance, message authorization/authentication, peer communication maintenance, load balancing, communication error handling etc. are handled by the Service Framework, transparently to the business logic.
Having the Service Framework interact with the NRF to learn about registered services, and as such being able to perform service discovery on behalf of consumer NFs.
Solution #3 does not have an explicit SAPo or Framework agent; requires a component to interface with the 3GPP service consumers/producers, but this is left to the service framework implementation. The NFs can have the Service Framework configured as an HTTP outbound proxy or the like.
A Rel-15 NF talks to the Service Framework using the Rel-15 API as is. In addition, it may (or may not) be configured to suppress service discovery. In this mode, it can send its first actual service message, skipping NRF discovery-related interaction, allowing the Service Framework transparently take care of the NRF interaction on its behalf.

## Slide 5: Key principles of Solution #1 (3.1) – part I:
Complete separation between Business Logic and Service Framework (Discovery/selection of peer service instance, message authorization, peer communication maintenance, Load balance, communication error handling are handled by the service framework, transparently to the business logic).
SAPo is an adapter between the Business Logic and the Service Framework.
3GPP defined SAPA as the Northbound (relative to SAPo) API interface between the Business Logic and the SAPo
Service framework, SAPo and the interface between them - not standardized by 3GPP.
The “southbound” interface of the SAPo MAY (or may not) use (a Non-3GPP) standard protocol, e.g. AMQP (standardized by OASIS)

## Slide 6: Key principles of Solution #1 (3.1) – part II:
Normally SAPo is standalone component (ie it resides outside of the Business Logic). However SAPo MAY be
integrated into a service implementation (Business Logic)(as per section 6.3.1.2.4).
Per section 6.3.1.3.1, the procedures for the registration/de-registration/discovery of NF/NF service (instances) (w/ the NRF) are unchanged compared to R15.
Per section 6.3.1.4, the procedures for registration, de-registration and update of NF instances or NF service instances do not change on Stage 2 level.
Per section 6.3.1.3.2, the component, which performs service discovery (eg invoke Nnrf_NFDiscovery
service) is the Service Framework. The Business Logic just sends a message to the Service Framework.
The Service Framework then works in a proxy mode, i.e. it performs service discovery (via the NRF) followed by a message delivery to the discovered service peer (this is done transparent to the Business Logic).

## Slide 7
Complete separation between Business Logic and Service Framework.
Framework agent is an adapter between the Business Logic and the Service Framework. It is the
equivalent of the SAPo of solution 3.1. The Framework agent is collocated with the Business Logic.
3GPP defines the Northbound API interface between the Framework agent and the Business Logic.
Service Framework basic services such as Discovery, Svc Registration, Routing ctrl and authorization are 3GPP defined, while additional services may be vendor specific.
Key principles of Solution #2 (3.2):

## Slide 8: The common between Solutions #1 and #2
The differences between Solutions #1 and #2
Complete separation between Business Logic and Service Framework.
Having an adapter between the Business Logic and the Service Framework (SAPo(#1) or Framework agent(#2)).
3GPP defined Northbound API interface between the Business Logic and the adapter
(SAPo/Framework agent).
Both solutions keep the Rel-15 stage 2 services and corresponding stage 3 HTTP API intact. This includes the services provided by the NRF.
Business Logic and Adapter(SAPo/Framework agent) – in solution #1 are normally expected to be separate (integration is not precluded). In solution #2 they are always integrated together.
Service Framework - not standardized in 3GPP in solution #1 . While in solution #2 some key/basic services are standardized in 3GPP.
“Southbound” interface – In solution #1 the interface between the Adapter (SAPo) and the Service Framework is not standardized in 3GPP, while in solution #2 it is implicitly standardized in 3GPP, as in solution #2 the key/basic services are standardized in 3GPP.

## Slide 9: The Pros and Cons of Solutions #1 and #2
Solution #1
Solution #2
Pros
Service Framework not defined by 3GPP - enables rich and easily extendable implementations. Enables vendors to leverage industry service frameworks.
APIs between Service Framework and the adapter (SAPo) may be used in the future for protocols beyond HTTP.
Cons
Having a standardized SAPA (Northbound API interface) requires the Business Logic to implement an API within an API, i.e. first the Business Logic needs to create and populate an HTTP message based on the Rel15 stage 2 and 3 definitions of NF services (23.502 5.2). Then instead of simply forwarding this message, it needs to “tunnel” it over an API message. Consequently, communication is not transparent any more to the Business Logic. In addition, metadata required in SAPA to reflect the critical 5G message elements results in duplication of information.
Pros
APIs between Service Framework and the adapter (Framework agent) may be used in the future for protocols beyond HTTP.
Cons
Service Framework services (and its interface to the adapter(Framework agent)) are unnecessarily defined by 3GPP. It would be better to leverage industry existing services/solutions.
The API within an API con indicated for solution #1
Mandating colocation of the Business Logic and the adapter (Framework agent) may cause unnecessary tight coupling, which makes testing and deployments more complicated and less agile.

## Slide 10: The common between Solutions #1 and #2 and #3
The unique aspects of Solutions #3
Complete separation between Business Logic and Service Framework.
All solutions keep the Rel-15 stage 2 services and corresponding stage 3 HTTP API intact. This includes the services provided by the NRF. (NOTE: Solutions #1 and #2 use though an API within an API on the “Northbound” interface)
No need for an adapter(SAPo/Framework Agent/Proxy Agent) between the Business Logic and the Service Framework.
Service Framework - not standardized in 3GPP, same as in solution #1.
“Northbound” interface (between the NF(Business Logic) and the Service Framework) is the 3GPP rel-15 interface between NFs as is. I.e No need for a new API interface (whether a 3GPP API or a non-3GPP API)
“Southbound” interface – by definition not needed.
Backward compatible with Rel-15

## Slide 11: The Pros and Cons of Solutions #3
Solution #3
Pros
Service Framework not defined by 3GPP - enables rich and easily extendable implementations. Enables vendors to leverage industry service frameworks.
Keeping the “Northbound” interface (between Service Framework and NF(Business Logic)) intact achieves the following:
  Simpler solution by having the service framework be transparent to the service consumers/producers.
  It also enables backward compatibility and so saves cost for vendors (development and testing effort) and operators, and is backward compatible with Rel-15.
No need for an explicit “Southbound” interface (introduced in solutions #1 and #2) i.e. less development and testing effort.
Cons
New types of transport used for 3GPP SBIs require updates to the service framework (e.g. QUIC)

## Slide 12: Conclusion
Solution #3 follows the key common principles of solutions #1 and #2 and in addition combines the pros of the above solutions and resolves their cons. This is also backward compatible with Rel-15.
  Therefore it is recommended to go with solution #3 as a way forward.