## Slide 1: Discussion about NWDAF interactions with OAM
Huawei, HiSilicon, CATR, Convida Wireless LLC, China Unicom, China Mobile, Orange, Alibaba, KDDI, NEC

## Slide 2
Current status for interactions between SA5/OAM and SA2/NWDAF
During the SA2#127bis meeting, it is approved in the Architecture Requirements in TR 23.791,
      As part of this study, exchange of information between NWDAF and OAM may be defined. Interactions between OAM and NWDAF shall be based on use case requirements. The OAM could be a potential consumer or provider of the information for the NWDAF. The definition of such interaction shall be coordinated with SA WG5.
      For the collection of OAM data, the NWDAF shall reuse existing mechanisms and interfaces defined by SA WG5. For OAM information exchange beyond existing mechanisms and interfaces defined by SA WG5, close co-operation with SA WG5 is needed.
      Based on the aforementioned data collection, the NWDAF performs data analysis and provides the analytical result to the AF, the 5GC NFs and the OAM.
  However, it is unclear how to define the interactions between the NWDAF and OAM in detail.

## Slide 3
Tenant Requirements
Tenants/Applications provide their requirements considering the following two aspects:
      SA5 scope:
    Tenant Requirement 1: Network slice level attributes (as defined in Table1, TS 28.532) , which are used by the OAM to create network slice. Also OAM could adjust the network slice resource per network KPIs (as defined in Table 2, TS28.55x series), but so far without considering how many percent UEs’ experience is satisfied per application
      SA2 scope:
    Tenant Requirement 2: How many percent UEs’ experience satisfy per application (as defined in Table 3), which is based on individual UE service experience measurement in clause 6.3, TR 23.791 Solution 3: QoS Profile Provisioning.
E2E network / Network slice | 5GC
1.Registered Subscribers of network and network Slice Instance | 1. Mean/Maximum number of registered subscribers (AMF)
2. End-to-end Latency of 5G Network | 2. Mean/Maximum Number of active PDU sessions(SMF)
3. Upstream/Downstream Throughput for Network and Network Slice Instance | 3. Number of incoming GTP data packets on the N3 interface, from (R)AN to UPF (UPF, N3)
4.Number of PDU sessions of network and network slice instance | 4. Number of outgoing GTP data packets of on the N3 interface, from UPF to (R)AN(UPF, N3)
5.Virtualised resource utilization of network slice instance | 5. Number of octets of incoming GTP data packets on the N3 interface, from (R)AN to UPF(UPF, N3)
6.DL latency in NG-RAN | 6. Number of octets of outgoing GTP data packets on the N3 interface, from UPF to (R)AN(UPF, N3)
7.Upstream/Downstream Throughput at N3 interface | 7. N6 outgoing link usage (UPF, N6)
Table 1
Table 2
Information | Presence | Source | Description
S-NSSAI | M | AMF | To identify the slice instance and support analytics per slice instance
Application ID | M | AF/PCF | To identify the service and support analytics per type of service e.g. voice or video
how many percent UEs’ service experience is satisfied | M | NWDAF | To indicate how many percent UEs’ service experience is satisfied (observed/measured by NWDAF) , e.g. 60% UE’s service experience is satisfied for voice service while Tenant requested 95%
Timestamp | M | NWDAF | The timing for the service in the slice instance.
Table 3

## Slide 4
Background: how to measure individual user service experience
Per clause 6.3, TR 23.791 Solution 3: QoS Profile Provisioning, with service Mean Opinion Score(MOS) data from AF and network data from 5GS, the NWDAF is to train e.g. a linear regression model for a given service:
    (1)
    In formula (1)
    is the service experience for a given service e.g. service MOS ;
    is a input variable vector, where e.g. is Packet Delay, is Packet Error Ratio, …, is Flow Bit Rate (i.e. all the factors could have impacts on the service experience). Please note is a constant and will be normalized to a fixed range e.g. 0-1 range(a.k.a data normalization/feature scale).
    is a parameter vector, as known as weight vector.
As the service model will be well trained in NWDAF, the formula (1) equals to service MOS formula and therefore NWDAF is able to accurately measure individual user service experience, allowing NWDAF to determine how many percent UEs’ experience satisfy.
Notes: Data normalization or feature scaling
https://en.wikipedia.org/wiki/Feature_scaling
Since the range of values of raw data varies widely, in some machine learning algorithms, objective functions will not work properly without normalization. For example, linear regression model as shown in formula (1), who acts as weight vector may not work properly as the range of values of raw data varies widely.
Another example is that the majority of classifiers calculate the distance between two points by the Euclidean distance. If one of the features has a broad range of values, the distance will be governed by this particular feature. Therefore, the range of all features should be normalized so that each feature contributes approximately proportionately to the final distance.
Another reason why feature scaling is applied is that gradient descent converges much faster with feature scaling than without it.
Data normalization or feature scaling
https://en.wikipedia.org/wiki/Feature_scaling
Since the range of values of raw data varies widely, in some machine learning algorithms, objective functions will not work properly without normalization. For example, linear regression model as shown in formula (1), 𝑊=( 𝑤_0,𝑤_1 𝑤_2,𝑤_3, …, 𝑤_𝐷) who acts as weight vector may not work properly as the range of values of raw data varies widely.
Another example is that the majority of classifiers calculate the distance between two points by the Euclidean distance. If one of the features has a broad range of values, the distance will be governed by this particular feature. Therefore, the range of all features should be normalized so that each feature contributes approximately proportionately to the final distance.
Another reason why feature scaling is applied is that gradient descent converges much faster with feature scaling than without it.

## Slide 5: Background: how to measure individual user service experience(cont.)
Information | Presence | Source | Description
Correlation ID | M | AF | Could be e.g. IP address 5-tuple or newly allocated temporary ID by 5GC , which is used by NWDAF to correlate the service data from AF and the network data from 5GC NF for the service
Application ID | M | AF | To identify the service and support analytics per type of service (the desired level of service)
Service Experience | M | AF | E.g. Service MOS, MOS or vMOS, to characterize the experience for the service. (The observed level of service by AF)
Timestamp | M | AF | The timing for the service.
TR 23.791 Table 6.3.1.1-1: Service Data from AF related to the observed service experience
Information | Presence | Source | Description
Correlation ID | M | PCF | Could be e.g. IP address 5-tuple or newly allocated temporary ID by 5GC , which is used by NWDAF to correlate the service data and the network data for the service
Timestamp | M |  | The timing for the service.
S-NSSAI | M | SMF/AMF | To identify the S-NSSAI for the PDU Session which contains the QoS flow
Application ID | M | PCF | Provided by the AF, which is used by NWDAF to identify the application service provider and application for the QoS flow
QFI | M | PCF or SMF | To identify the QoS flow
QoS flow Bit Rate | M | SMF | To determine the QoS parameter: GFBR/MFBR
QoS flow Packet Delay | M | SMF | To determine the QoS parameter: PDB
QoS flow Packet Error Rate | M | SMF | To determine the QoS parameter: PER
TR 23.791 Table 6.3.1.1-2: QFI level measurements/KPIs
Solution 3: QoS Profile Provisioning has been captured in clause 6.3, TR 23791
    (1)
Move from backup slide

## Slide 6
Background: how to measure individual service experience (cont.)
Data normalization or feature scaling
  Since the range of values of raw data varies widely, in some machine learning algorithms, objective functions will not work properly without normalization.
  For example, linear regression model in formula (1), who acts as weight vector may not work properly as the range of values of raw data varies widely.
  Another example is that the majority of classifiers calculate the distance between two points by the Euclidean distance. If one of the features has a broad range of values, the distance will be governed by this particular feature. Therefore, the range of all features should be normalized so that each feature contributes approximately proportionately to the final distance.
  Another reason why feature scaling is applied is that gradient descent converges much faster with feature scaling than without it.
Notes: Data normalization or feature scaling
https://en.wikipedia.org/wiki/Feature_scaling
Since the range of values of raw data varies widely, in some machine learning algorithms, objective functions will not work properly without normalization. For example, linear regression model as shown in formula (1), who acts as weight vector may not work properly as the range of values of raw data varies widely.
Another example is that the majority of classifiers calculate the distance between two points by the Euclidean distance. If one of the features has a broad range of values, the distance will be governed by this particular feature. Therefore, the range of all features should be normalized so that each feature contributes approximately proportionately to the final distance.
Another reason why feature scaling is applied is that gradient descent converges much faster with feature scaling than without it.
Data normalization or feature scaling
https://en.wikipedia.org/wiki/Feature_scaling
Since the range of values of raw data varies widely, in some machine learning algorithms, objective functions will not work properly without normalization. For example, linear regression model as shown in formula (1), 𝑊=( 𝑤_0,𝑤_1 𝑤_2,𝑤_3, …, 𝑤_𝐷) who acts as weight vector may not work properly as the range of values of raw data varies widely.
Another example is that the majority of classifiers calculate the distance between two points by the Euclidean distance. If one of the features has a broad range of values, the distance will be governed by this particular feature. Therefore, the range of all features should be normalized so that each feature contributes approximately proportionately to the final distance.
Another reason why feature scaling is applied is that gradient descent converges much faster with feature scaling than without it.

## Slide 7
How SA2/SA5 work jointly to meet tenant requirements
NWDAF should combine the percentage of UEs’ experience per application that has been satisfied (in SA2) and the associated network level KPIs (in SA5)
Then NWDAF find the correlation b/w application experience and network slice resource , which could be used by OAM to adjust network slice resource.
E2E network / Network slice | NR and NG-RAN | 5GC
1.Registered Subscribers of network and network Slice Instance | 1. UL Packet Loss Rate(gNB-CU) | 1. Mean/Maximum number of registered subscribers (AMF)
2. End-to-end Latency of 5G Network | 2. UL F1-U Packet Loss Rate(gNB-CU) | 2. Mean/Maximum Number of active PDU sessions(SMF)
3. Upstream/Downstream Throughput for Network and Network Slice Instance | 3. DL Packet Drop Rate (gNB-CU) | 3. Number of incoming GTP data packets on the N3 interface, from (R)AN to UPF (UPF, N3)
4.Number of PDU sessions of network and network slice instance | 4. DL F1-U Packet Loss Rate (gNB-DU) | 4. Number of outgoing GTP data packets of on the N3 interface, from UPF to (R)AN(UPF, N3)
5.Virtualised resource utilization of network slice instance | 5. DL Packet Drop Rate (gNB-DU) | 5. Number of octets of incoming GTP data packets on the N3 interface, from (R)AN to UPF(UPF, N3)
6.DL latency in NG-RAN | 6. UE Context Release Request(gNB-DU initiated) | 6. Number of octets of outgoing GTP data packets on the N3 interface, from UPF to (R)AN(UPF, N3)
7.Upstream/Downstream Throughput at N3 interface | 7.DL/UL Total PRB Usage (gNB-DU) | 7. N6 outgoing link usage (UPF, N6)
Information available at OAM/SA5
Information to be defined at NWDAF/SA2
Information | Presence | Source | Description
S-NSSAI | M | AMF | To identify the slice instance and support analytics per slice instance
Application ID | M | AF/PCF | To identify the service and support analytics per type of service e.g. voice or video
how many percent UEs’ service experience is satisfied | M | NWDAF | To indicate how many percent UEs’ service experience is satisfied (observed/measured by NWDAF) , e.g. 60% UE’s service experience is satisfied for voice service while Tenant requested 95%
Timestamp | M | NWDAF | The timing for the service in the slice instance.
Table 3: How many percent UEs’ service experience is satisfied observed/measured by the NWDAF
Table 2:KPIs per Network Slice as defined in PM (Performance Management) services (TS28.55x series)

## Slide 8
Single Application Analysis per Network Slice
    when a network slice is composed of one application, in order to meet the tenant requirements, first, some calculations and analytics need to be done, e.g. trained a linear regression model for the given application as follows:
    (1)
    In formula (1)
    is the percentage of the UEs whose experience satisfied for the given application, e.g. 80% of UEs‘ application experience is satisfied (as defined in Table 3)
    is a input variable vector i.e. network level KPIs as defined in Table 2 , e.g. is Registered Subscribers of network and is End-to-end Latency of 5G Network. Please note is a constant and will be normalized to a fixed range e.g. 0-1 range.
    is a parameter vector, as known as weight vector
    Based on the model in formula (1) and the tenant requirement (2) about how many percent UEs’ application experience should be satisfied, e.g.
    (2)
    Then a set of network level KPIs combination(s) is to be found (which meets UEs’ application experience is satisfied) and is fed to OAM, assisting OAM to perform resource adjustment if the network slice cannot meet the tenant requirement.

## Slide 9
Multiple Applications Analysis per Network Slice
    When a network slice are composed of multiple applications, in order to meet the tenant requirements, first, some calculations and analytics need to be done, e.g. training and evaluating a linear regression model per application as follows:
(1)
(2)
….
(M)
    Based on the model in formula (1) ~ () and the tenant requirement (1)~(M) about how may percent UEs’ experience per application should be satisfied, e.g.
(1)
(2)
….
(M)
    Then a set of network level KPIs combination(s) is to be found(which can meet the tenant requirement (1)~(M) at the same time) and is fed to OAM, assisting OAM to perform resource adjustment if the network slice cannot meet the tenant requirement.

## Slide 10: Open Discussion: how to collect QFI level measurement/KPIs
      Option 2
    OAM collects QFI and network level network data from 5GC NFs;
    OAM provides QFI and network level network data to NWDAF.
OAM
NWDAF
5GC NF (e.g. PCF)
      Option 1
    5GC NFs provide QFI level network data to the NWDAF;
    OAM provides network level data to the NWDAF.
OAM
NWDAF
5GC NF (e.g. PCF)
QFI Level measurements/KPIs as defined in Table 6.3.1.1-2, TR 23.791 for solution 3: QoS profile provisioning | 
S-NSSAI | To identify the S-NSSAI (SMF/AMF)
Application ID | To identify application (PCF)
QFI | To identify the QoS flow (PCF/SMF)
QoS flow Bit Rate | To determine the QoS parameter: GFBR/MFBR (SMF)
QoS flow Packet Delay | To determine the QoS parameter: PDB (SMF)
QoS flow Packet Error Rate | To determine the QoS parameter: PER (SMF)
…… | ……
Network level measurements/KPIs defined in SA5, TS 28.532 | 
1.Registered Subscribers of network and network Slice Instance | 1. Mean/Maximum number of registered subscribers (AMF)
2. End-to-end Latency of 5G Network | 2. Mean/Maximum Number of active PDU sessions(SMF)
3. Upstream/Downstream Throughput for Network and Network Slice Instance | 3. Number of incoming GTP data packets on the N3 interface, from (R)AN to UPF (UPF, N3)
4.Number of PDU sessions of network and network slice instance | 4. Number of outgoing GTP data packets of on the N3 interface, from UPF to (R)AN(UPF, N3)
5.Virtualised resource utilization of network slice instance | 5. Number of octets of incoming GTP data packets on the N3 interface, from (R)AN to UPF(UPF, N3)
…… | ……
Newly added
Question:
    It is clear that network level measurements/KPIs are collected by OAM, however what is not clear is that how to collect QFI level measurements/KPIs:
  Option 1: QFI level measurements/KPIs collected from 5GC NF?
  Option 2: QFI level measurements/KPIs collected from OAM?
  Option 1+2

## Slide 11
Data Analytics Interactions between OAM and NWDAF
      Option A
      Option B
OAM
NWDAF
    NWDAF provides how many percent UEs’ experience is satisfied per application to OAM
    OAM derives a set of recommended network KPIs combination(s)
    OAM adjust slice resource if the network slice cannot meet the tenant requirement.
    Question to SA5: whether OAM should get aware of the application related info?
OAM
NWDAF
    NWDAF retrieves network KPIs from OAM;
    NWDAF provides a set of recommended network KPIs combination(s) to the OAM
    OAM adjust slice resource if the network slice cannot meet the tenant requirement
      Option C
OAM
NWDAF
5GC NF (e.g. PCF,NSSF)
    NWDAF retrieves network KPIs from OAM;
    NWDAF provides a data analytics to 5GC NF, e.g. slice congestion level by NWDAF to PCF/NSSF and OAM
    5GC NF adjust slice resource if the network slice cannot meet the tenant requirement
Assume that QCI level measurements/KPIs are resolved by previous slide

## Slide 12
Data Analytics Interactions between OAM and NWDAF(Cont.)
    What is clear now:
      Network slice resource adjustment is in the scope of SA5
      Data analytics provided by NWDAF will benefit OAM to e.g. perform network slice resource adjustment
    What is not clear so far :
      Granularity of Data analytics provided by NWDAF to OAM
      How/whether NWDAF is to retrieve the network level KPIs from OAM
    To make progress, it is proposed to adopt Opt A+B+C temporarily, encouraging SA2 and SA5 to have a joint investigation:
      SA2 update Key Issue 4: Interactions with OAM for Data Collection/Analytics Exposure to discuss (S2-186668) :
    Data analytics feedback mechanism b/w OAM and NWDAF for Opt A+B+C
    NWDAF retrieving data from OAM for Opt B+C
    SA2/SA5 joint evaluation during conclusion phase e.g. joint meeting
      LS out to SA5 (S2-186667) on current NWDAF SA2 status, asking for cooperation

## Slide 13: BACKUP