## Slide 1: EPS SPID/RFSP concept extension TEI-16 Proposal
Source: Vodafone, Verizon, Telstra, Telecom Italia, Ericsson
SA WG2 Meeting #129bis November 26 - 30, 2018, West Palm Beach, USA
Agenda item: 7.1
Tdoc S2-1812492
Rev of S2-1812020
Slides 3 and 4 added. Other changes in Green/strikethrough

## Slide 2: Use case 1: Prioritise capacity for a specific enterprise on a specific macro cell
Cell A
Cell B
Enterprise 1
Enterprise 2
Cell A RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell A resources.
  Handle Enterprise 2 employees and other users with default behaviour
  Cell B RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell B resources.
  Handle Enterprise 1 employees and other users with default behaviour

## Slide 3: Use case 2: Prioritise capacity for specific enterprises on a specific cell of a sectored macro eNB
eNB K
Cell K1 (West Sector)
Enterprise 1
Enterprise 2
Cell K1 (eNB K, West Sector) RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell K1 resources.
  Handle Enterprise 2 employees and other users with default behaviour
  Cell K2 (eNB K, East Sector) RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell K2 resources.
  Handle Enterprise 1 employees and other users with default behaviour
Cell K2
(East Sector)

## Slide 4: Use case 3: Prioritise different capacities for multiple enterprises on specific cells of a sectored macro eNB
eNB K
Cell K1 (West Sector)
Enterprise 1
Enterprise 2
Cell K1 (eNB K, West Sector) RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell K1 resources.
  Enterprise 3’s employees get priority access to W% (but not all) of Cell K1 resources
  Handle Enterprise 2 employees and other users with default behaviour
  Cell K2 (eNB K, East Sector) RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell K2 resources.
  Enterprise 3’s employees get priority access to Z% (but not all) of Cell K2 resources.
  Handle Enterprise 1 employees and other users with default behaviour
Cell K2
(East Sector)
Enterprise 3
Enterprise 3

## Slide 5: Additional Description
This is not a ‘closed access’ cell that is reserved exclusively for the use of an enterprise
Some similarity to a WiFi Access Point that has two SSIDs, one for private use and one for public use.
Cell A is configured with knowledge that it needs to give special treatment to Enterprise 1’s users.
  Requires cell A to know whether the UE belongs to ‘enterprise 1’
  For non-enterprise users, or, users from other enterprise groups <> 1, default behavior is applied. Some resources are reserved for them in order to ensure coverage.
The RRM strategy of the cells is operator/implementation specific.
  However, as indicated in the WID, RP-151827 “RAN Aspects of RAN Sharing Enhancements for LTE”, existing eNBs are able to share load between the sharing PLMNs’ customers (“Sharing is normally based on agreed quota or share ratio.“)
  In a non-shared PLMN, or a PLMN with few sharing partners, this eNB functionality could be re-purposed to serve a “Matching Enterprise user group” and a “Default user group”
Cell A generates separate counters/statistics for ‘enterprise 1’ and ‘other’ users -> enables any Service Level Agreement to be monitored.

## Slide 6: No current tools available to solve this (1)
Current QoS information is ‘abstract’ and relates primarily to that UE, rather than the “set of UEs used by the enterprise’s employees”
RAN does not know the ‘group’ of the UE
RAN does not have visibility of the IMSI
There are too many enterprises to allocate different IMSI ranges to different enterprises.
APN is not visible to the RAN
Hybrid CSG -> see next slide
Access Class Barring only applies to idle mode. Also, Access Classes need to be randomly allocated to devices – so all ‘groups’ are likely to have an equal proportion of devices in each Access Class.
“Low Access Priority” does not help as LAPI devices should not be rejected if their group’s load is within the eNB’s quota for that group.
SPID/RFSP has only 256 values. This can identify that the UE is an Enterprise subscriber but NOT WHICH ENTERPRISE
  there are insufficient values to identify different the enterprises within a PLMN (or MME area, or even a Tracking Area)
Use of 5GCore -> enterprise provided (or ‘bring your own’) devices are frequently not leading edge devices – e.g. they may well not be 5GCore capable devices

## Slide 7: No current tools available to solve this (2): Hybrid Closed Subscriber Group
Hybrid CSG specified in Rel 9. Developed for Home eNB concept with one cell per eNB.
CSG concept involves - when eNB is connected, the eNB’s CSG ID(s) are supplied to the MME - the UE’s CSG ID(s) are sent from the HSS to the MME - the MME compares the eNB’s and UE’s CSG IDs and sends the binary result to the eNB.
Current CSG concept does not support Use Cases 2 and 3 as: - the S1 Setup associates the CSG ID(s) with all cells of the eNB; - the UE Associated S1-AP signalling does not indicate which CSG the UE is a member of; - while the MME could activate Location Reporting on the eNB to track intra-eNB cell changes, the Location Report sent by the eNB does not contain any CSG-ID.

## Slide 8: Proposed solution: Extend concept of SPID/RFSP
Add a 32 bit, optional, parameter to S6a and S1 interfaces and handle using the same mechanisms as specified in TS 23.401 (e.g. clause 4.3.6). 'Index to RAT/Frequency Selection Priority' (RFSP Index) so that e.g. individual enterprises can be differentiated from each other.
Rationale:
The SPID/RFSP mechanism was specified in 3GPP Release 8
The standardised values in Annex I of TS 36.300, and e.g. the LS from GSMA in S2-178308 ,imply that it is at least somewhat implemented, rather than being an unimplemented or “yet to be implemented” feature.
RFSP functionality specified in clause 4.3.6 of TS 23.401 allows visited network policy to be applied to the RFSP Index of Roaming subscriber.
Outside of clause 4.3.6, the definitions, and the sections on HSS and MME storage, there is only one other usage of “RFSP” in TS 23.401 (and that section refers straight to clause 4.3.6). - In contrast there are 730 occurrences of CSG in TS 23.401 spread throughout TS 23.401, and all of these would need checking and possibly modifying if the CSG concept is modified to support use cases 2 and 3.
Existing MME, S1 interface, and E-UTRAN behavior provides the ability to handle a mix of supporting and non-supporting entities smoothly.
Why 32 bit extension?
  gives sufficient codespace for identification of an enterprise (16 bits is insufficient; 24 bits is borderline for large PLMN)
  CT4’s Diameter and GTP-C specifications seem to use 32 bit parameters
  if desired, could allow 1:1 mapping with a 5GCore NSSAI parameter.

## Slide 9: Alternative potential solutions:
UE Usage Type (c.f. R13 DECOR)
  This is only 8 bits long
  Not sent to RAN, nor transferred on X2
  As not sent to RAN, no concept of VPLMN policing the value from HPLMN specified As NB-IoT MME selection can be “RAT based”, probably less widely implemented than RFSP Index
DCN ID (c.f. R14 eDECOR)
  16 bits long (as indicated by NG-RAN’s use of 24 bit TACodes, 16 bits are really not sufficient for simple allocation to large numbers of different enterprises)
  Intended for very different purpose (i.e. MME selection at PLMN change)
New parameter
  Slower rollout than with existing concept
“Full 5GCore Slicing”
  Unnecessary complexity for EPC
 Extension of SPID/RFSP concept is sufficient

## Slide 10: Specification Impacts of SPID/RFSP
Stage 2: TS 23.401
  Potentially no change needed in 4.3.6
  However, probably useful to describe in clause 4.3.6 of TS 24.301 the added field, and update the HSS and MME storage tables
  Existing ‘fallback’ mechanisms support partial rollout in core or RAN:
  “…The MME stores the subscribed RFSP Index value received from the HSS and the RFSP Index value in use. During the Tracking Area Update procedure, the MME may update the RFSP Index value in use (e.g. the MME may need to update the RFSP Index value in use if the UE related context information in the MME has changed)…”
  - Add RFSP and the new parameter to S1-Path Switch Ack to handle mix of supporting and non-supporting eNBs
Interworking with 5GCore Depends whether RFSP extension is desired in 5GCore
  Can reuse S10 (= N26) functionality
  TS 23.501 clause 5.3.4.3 is close copy of clause 4.3.6 of TS 23.401.
CT 4 specifications:
  29.272 Diameter, add new parameter to the Subscription-Data AVP (which carries the existing RAT-Frequency-Selection-Priority-ID)
  29.274 GTP-C, add the ‘subscribed’ and ‘in use’ values for the new parameter to Forward Relocation Request and Context Response messages (which carry the existing RFSP Index parameters)
RAN 3 specifications
  36.413 S1 AP, add the new parameter to messages carrying Subscriber Profile ID for RAT/Frequency priority
  36.423 X2 AP: as S1-AP
  36.300 potentially add new “well known” value for Enterprise

## Slide 11: Proposals
Agree to draft TEI-16 EPC CRs for this functionality.
Decide now whether or Agree not to replicate in 5GCore.
Allocate 0.5 TU in SA2 for this work.
Report to SA/RAN/CT on the need for limited stage 3 work.