## Slide 1: EPS SPID/RFSP concept extension/alternative TEI-16 Proposal
Source: Vodafone, Verizon, Telstra, Telecom Italia, Ericsson
SA WG2 Meeting #129bis November 26 - 30, 2018, West Palm Beach, USA
Agenda item: 7.1
Tdoc S2-1813343
Rev of S2-1812492

## Slide 2: Use case 1: Prioritise capacity for a specific enterprise on a specific macro cell
Cell A
Cell B
Enterprise 1
Enterprise 2
Cell A RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell A resources.
  Handle Enterprise 2 employees and other users with default behaviour
  Cell B RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell B resources.
  Handle Enterprise 1 employees and other users with default behaviour

## Slide 3: Use case 2: Prioritise capacity for specific enterprises on a specific cell of a sectored macro eNB
eNB K
Cell K1 (West Sector)
Enterprise 1
Enterprise 2
Cell K1 (eNB K, West Sector) RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell K1 resources.
  Handle Enterprise 2 employees and other users with default behaviour
  Cell K2 (eNB K, East Sector) RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell K2 resources.
  Handle Enterprise 1 employees and other users with default behaviour
Cell K2
(East Sector)

## Slide 4: Use case 3: Prioritise different capacities for multiple enterprises on specific cells of a sectored macro eNB
eNB K
Cell K1 (West Sector)
Enterprise 1
Enterprise 2
Cell K1 (eNB K, West Sector) RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell K1 resources.
  Enterprise 3’s employees get priority access to W% (but not all) of Cell K1 resources
  Handle Enterprise 2 employees and other users with default behaviour
  Cell K2 (eNB K, East Sector) RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell K2 resources.
  Enterprise 3’s employees get priority access to Z% (but not all) of Cell K2 resources.
  Handle Enterprise 1 employees and other users with default behaviour
Cell K2
(East Sector)
Enterprise 3
Enterprise 3

## Slide 5: Additional Description
This is not a ‘closed access’ cell that is reserved exclusively for the use of an enterprise
Cell A is configured with knowledge that it needs to give special treatment to Enterprise 1’s users.
  Requires cell A to know whether the UE belongs to ‘enterprise 1’
  For non-enterprise users, or, users from other enterprise groups <> 1, default behavior is applied. Some resources are reserved for them in order to ensure coverage.
The RRM strategy of the cells is operator/implementation specific.
  However, as indicated in the WID, RP-151827 “RAN Aspects of RAN Sharing Enhancements for LTE”, existing eNBs are able to share load between the sharing PLMNs’ customers (“Sharing is normally based on agreed quota or share ratio.“)
  In a non-shared PLMN, or a PLMN with few sharing partners, this eNB functionality could be re-purposed to serve a “Matching Enterprise user group” and a “Default user group”
Cell A generates separate counters/statistics for ‘enterprise 1’ and ‘other’ users -> enables any Service Level Agreement to be monitored.

## Slide 6: Proposals
Agree to draft TEI-16 EPC CRs for this functionality.
Choose between SPID/RFSP based concept and alternative approaches
Agree not to replicate in 5GCore.
Allocate 1 TU spread over two SA2 meetings for this work.
Report to SA/RAN/CT on the need for limited stage 3 work.