## Slide 1: Way forward for Enable Location Service in Rel-16
CATT

## Slide 2: Latest Status of FS_eLCS
Some text from the SID Objective:
  This study will consider un-trusted non-3GPP access and 3GPP access first from the perspective of UE access (though can allow non-3GPP access to be used for UE location determination. After the architecture for connecting trusted non-3GPP access to 5GC has been specified, the study will also consider how to support location services for trusted non-3GPP access.
First part:
  Focus on “un-trusted non-3GPP access and 3GPP access ”
  16 key issues, 27 solutions captured in TR23.731;
  Interim conclusion already reached on 10 key issues(#: 1,3,4,6,7,8,9,10,12 and 14); Most of them would be converted to conclusions for normative work;
    For This meeting, some key issues are expected to concluded (#: 2,5,16), the others may not (#11, 13, 15);
Second part:
  Focus on “trusted non-3GPP access ”, has dependency on the Study FS_5WWC;
  The FS_5WWC progress well:
    the architecture for connecting trusted non-3GPP access to 5GC is expected to be specified during the normative phase of 5WWC;
  LCS Solutions for this part is expected in this meeting;

## Slide 3: RAN dependency (1/2)
RAN#80 Approved “NR Positioning” in RP-181399, and RAN#81 Updated it in RP-182155 , which related to First part:
  Objective:
    Select the requirements, and study corresponding evaluation scenarios/methodologies to enable positioning in regulatory and commercial use cases; [RAN1]
    Study and evaluate potential solutions of positioning technologies based on the above identified requirements, evaluation scenarios/methodologies [RAN1]
    Study of positioning architecture for location services, functional interfaces, protocol, and procedures for supporting NR dependent positioning technologies (if needed; otherwise, need to be confirmed) [RAN2 primary,, RAN3 checks, according to current practices for positioning architecture]
  TimeLine:
    Target completion date: RAN#83 (March’2019):
    2 TU each allocated for RAN1 in Q4’2018 and Q1’2019;
    0.5 TU each allocated for RAN2 in Q4’2018 and Q1’2019;
    1 TU allocated for RAN3 in Q1’2019;

## Slide 4: RAN dependency (2/2)
Status of Study “NR Positioning” after RAN WGs Nov meeting:
  RAN WG1:
    Target NR Positioning Requirements (regulatory and commercial ) were agreed;
    Scenarios and System Parameters for Positioning Evaluations were defined;
    RAT-dependent NR Positioning Technologies to be investigated and evaluated were identified
  RAN WG2: [SA2 work has dependency here]
    Working assumption, working agreement on Architecture and Protocol reached, and LS out on “Location Service exposure to NG-RAN ”approved in RP-1819099.
  RAN WG3:
    Not on Q4 meeting agenda:

## Slide 5: Way Forward: General
To agree the WID this meeting:
  Objective:
    Specify what have be agreed to be move to normative work;
  Timeline:
    Target Completed Date: SA#84, i.e. June 2019;
To conclude as much as possible during this meeting;
  For those key issues unable to concludes, to decide
    which to be studied continuously next Q1;
    which to be deferred to next release;

## Slide 6: Way Forward : Detail Plan for Q1
Work plan for next Q1:
  2 TUs request for each meeting:
    Those TUs are requested for combined WID and SID work;
    ½ TU per meeting should be used for the study.
  List of key issues for continuation/conclusion in Q1:
    Conclusion on KI#2,5,16; also considering related RAN and SA1 input;
    Conclusion on LCS for trusted-NON-3GPP access aspects;
    This list/items are be verified, updated, completed and decided during SA2#129bis
  Conclude the Study in Q1:
    Conclude the Study by follow normal procedure; sending the TR for approval in Q1;
    If some agreements reached for normative work for Rel-16, WID will be updated accordingly;

## Slide 7: THANKS!

## Slide 8: Annex A: Key Issues, and their status
# | Title | Interim conclusion | Remarks
1 | Enhancement to LCS Architecture | Yes | 
2 | Positioning via user plane transmission |  | This meeting may concluded.
3 | Support of low latency and high performance LCS | Yes | 
4 | Reduce overhead for repetitive non-successful privacy verification | Yes | 
5 | Slicing dependent location service |  | This meeting may concluded.
6 | Scalability | Yes | 
7 | Location service exposure | Yes* | Whether exposure to NG-RAN is under going cross TSG coronation
8 | Support of IoT UEs | Yes | 
9 | Support EUTRAN positioning methods | Yes | Has RAN dependency.
10 | Support NR positioning methods | Yes | Has RAN dependency.
11 | Coordination of Positioning Signalling Transmitted via Control Plane Path and User Plane Path |  | Maybe deferred.
12 | LCS support for Non-3GPP access | Yes* | Trust NON-3GPP Access need further input;
13 | Support of Flexible and Efficient Periodic and Triggered Location |  | Maybe deferred.
14 | Positioning Access selection for LCS service | Yes | 
15 | Location continuity support |  | Maybe deferred.
16 | Distribution Positioning Assistance Data |  | This meeting may concluded. Has RAN dependency.

## Slide 9: Annex B-1: SA1 status on 5G_HYPOS after SA1#84
Tdoc | Title | Source | Doc-type | Spec | CRnbr | Decision
S1-183471 | Functional requirements for 5G positioning services (clause 6) | ESA | CR | 22.261 | 0331 | agreed
S1-183631 | Termnology correction for positioning-related tables in 7.3.2 | LG Electronics Mobile Research | CR | 22.261 | 0309 | agreed
S1-183687 | Clarification on positioning-related descriptions in 7.3.1 | LG Electronics Mobile Research | CR | 22.261 | 0308 | agreed
S1-183696 | Clarification of requirement on energy per fix in clause 7.3.2.3 | ESA | CR | 22.261 | 0330 | agreed
Initial thoughts:
  SA2 may check those CRs during next Q1;

## Slide 10: Annex B-2: SA3 status on FS_eLCS_Sec after SA3#93
First SA3 meeting on FS_eLCS_Sec;
Tdoc | Title | Source | Doc-type | Spec | Decision
S3-183527 | Bluetooth positioning - new KI for the upcoming TR on FS_eLCS_Sec | Ericsson | pCR | 33.814 | approved
S3-183744 | pCR to TR33.814 - Scope | CATT | pCR | 33.814 | approved
S3-183811 | Draft skeleton for TR 33.814 | CATT | pCR | 33.814 | approved
S3-183814 | TBS positioning - new KI for the upcoming TR on FS_eLCS_Sec | Ericsson | pCR | 33.814 | approved

## Slide 11: Annex C: RAN2 status on “Study on NR Positioning Support”
Working assumption
1: Rel-15 positioning architecture is the baseline for Rel-16 (for evaluation for proposed changes)
Agreements
1. RAN2 will study the RAN2 protocol impacts associated with supporting location management functionality in RAN
2. RAN2 expect SA2 to consider the E2E delay aspects of supporting location management functionality in RAN
Agreements
1. LPP is reused and extended to support the new NR RAT dependent positioning methods (that are discussed in the scope of this SI)
2. RAN2 assume that NRPPa is reused to support new NR RAT dependent positioning methods (this is a RAN3 decision)
R2-1819099 Reply LS on Location Service exposure to NG-RAN Ericsson LS out Approved

## Slide 12: Annex D: RAN1 status on “Study on NR Positioning Support”
Rel. 16 NR Positioning Requirements
  Regulatory requirements are considered as a minimum performance targets for NR Positioning studies. Additional requirements based on commercial use cases can be used as input performance targets.
For regulatory use cases:
  Horizontal positioning error <= 50m for 80% of UEs
  Vertical positioning error [<5 m] for [80%] of UEs
  End to end latency and TTFF < 30 seconds
For commercial use cases:
  Horizontal positioning error < 3m for 80% of UEs in indoor deployment scenarios
  Vertical positioning error < [3]m for [80]% of UEs in indoor deployment scenarios
  Horizontal positioning error < 10m for 80% of UEs in outdoor deployments scenarios
  Vertical positioning error < [3]m for [80]% of UEs in outdoor deployment scenarios
  End to end latency < [1]s
  Notes:
    This does not eliminate more or less demanding commercial use cases.
    For commercial use cases, indoor deployment means indoor deployed UEs and gNBs.
    For commercial use cases, outdoor deployment means outdoor deployed UEs and gNBs.
Note: It is understood that no single positioning technology has to meet all the requirements for every scenario.

## Slide 13: Annex D: RAN1 status on “Study on NR Positioning Support” (cont.)
For evaluating baseline performance, scenarios (with various options/configurations) are defined below for RAT-dependent positioning techniques for NR positioning study:
  Scenario 1. Indoor Office for FR1 and FR2 (Open office and Mixed Office)
  Scenario 2. UMi street canyon for FR1 and FR2 (ISD 200m)
  Scenario 3. UMa (ISD 500m, TBD: ISD > 500m) for FR1 only (Macro cell only deployment scenario)

## Slide 14: Annex D: RAN1 status on “Study on NR Positioning Support” (cont.)
RAT-dependent NR Positioning Technologies
  Downlink based solutions
  Downlink and uplink based solutions
  Uplink based solutions
  Combination of downlink, uplink as well as downlink and uplink techniques can be used for NR positioning.

## Slide 15: Annex D: RAN1 status on “Study on NR Positioning Support” (cont.)
Downlink Based Solutions
  Timing based techniques
    Timing of arrival path(s)
    Phase difference based techniques
      Note: feasibility needs to be further assessed
  Angle-based techniques
    Downlink angle(s) of departure
    Downlink angle(s) of arrival
  Carrier-phase based techniques
    Note: feasibility needs to be further assessed
  Received reference signal power based techniques
  Cell ID and TRP related information (e.g. RS resource and/or resource set ID)

## Slide 16: Annex D: RAN1 status on “Study on NR Positioning Support” (cont.)
Uplink Based Solutions
  Timing based techniques
    Timing of arrival path(s)
  Angle-based techniques
    Uplink angle(s) of departure
    Uplink angle(s) of arrival
  Carrier-phase based techniques
    Note: feasibility needs to be further assessed
  Received reference signal power based techniques

## Slide 17: Annex D: RAN1 status on “Study on NR Positioning Support” (cont.)
Downlink and Uplink Based Solutions
  Timing based techniques
    Round trip time measurement including support for multiple TRPs
  Combination of DL and UL techniques for NR positioning
    e.g. E-CID like techniques (including one or multiple cells)