## Slide 1: Slice SLA Guarantee from Control plane China Mobile, Huawei

## Slide 2: NWDAF-Assisted Service Characteristics Learning for Slice
AMF
CN
UE
Operator
Tenant
RAN
NSSF
OAM
MDAF
NSMF/
NSSMF
NWDAF
SMF/
PCF
SMF/
PCF
Newly added Slice B without agreed SLA
( field trial phase )
Deployed Slice A with agreed SLA
Field Test Indication
(5GS de-prioritizes Slice B related activity)
Slice B QoE
Characteristic Analytics
A slice are composed of multiple services and Slice SLA is related to Service MOS. This paper propose a solution about Slice SLA guarantee from control plane

## Slide 3: NWDAF-Assisted Service Characteristics Learning for Slice
1. Slice B is created by OAM but SLA b/w operator and Tennant B is not signed. Slice B Field Test starts to learn Service Characteristics for Slice B and avoid impacting on Slice A (as SLA b/w operator and Tennant A is already agreed).
2. NSSF temporarily indicates slice B Field Trial Indication to PCF, in order to avoid impacting the agreed SLA for Slice A i.e. RAN will prioritize Slice A related activity compared to slice B.
3. NSSF sends the QoE Requirement for Slice B to NWDAF and NWDAF derives the Service Characteristics for Slice B.
4. NWDAF-Assisted QoS profile provisioning for slice B is performed, which depends on discussion outcome key issue 5 and QoS Profile Provisioning.
5a. Only when NWDAF-Assisted QoS profile provisioning is successfully finished and the stable QoS profile per App ID is found e.g. QoS parameters combinations per Service MOS Window for APP 3 and APP4 , the procedure for NWDAF-Assisted Network Load Level Info will be performed and .
NWDAF classify the observed QoE data i.e. how many percent of user’s service experience satisfy per APP ID per slice per time (Slice A: x1% for APP 1, x2% for APP 2; Slice B: x3% for APP 3, x4% for APP 4)to 5 categories, which equals to Network Load Level 1~5 ->see next slides for details.
5b. The NWDAF figures out the Network Load Level info per time per Region, by measuring the similarity between the observed QoE data i.e. how many percent of user’s service experience satisfy per APP ID per slice per time and and the Network Load Level 1~5. ->see next slides for details.
5c~5d. NSSF/PCF may use the Network Load Level info for slice selection or slice congestion control or the policy decisions.
6. Slice B Field Test completes and the field test indication is removed and SLA between Operator and Tenant B is signed.

## Slide 4: How NWDAF figure out Network Load Level ID (step 5a)
Slice A: 98% for APP 1, 98% for APP 2; Slice B: 98% for APP 3, 97% for APP 4
Slice A: 90% for APP 1, 90% for APP 2; Slice B: 90% for APP 3, 90% for APP 4
Slice A: 85% for APP 1, 87% for APP 2; Slice B: 86% for APP 3, 88% for APP 4
Information
Region per Network
Time window
Slice A
>App 1
>>how many percent UEs’ experience satisfy
>App 2
>>how many percent UEs’ experience satisfy
Slice B
>App 3
>>how many percent UEs’ experience satisfy
>App 4
>>how many percent UEs’ experience satisfy
Table 1: Region level input information for K-Means
Figure 1. Training process for K-Means, e.g. K=2
K=5, given by PCF or configured in NWDAF, which means that number of load levels is 5
K-Means algorithm
Note: Slice requirement for load level 3 is Slice QoE baseline Requirement from Tenant
Slice A: 80% for APP 1, 80% for APP 2; Slice B: 80% for APP 3, 80% for APP 4
Slice A: 70% for APP 1, 70% for APP 2; Slice B: 70% for APP 3, 70% for APP 4

## Slide 5: How NWDAF figure out the associated Slice Load Level ID(step 5a)
Slice A: 98% for APP 1, 98% for APP 2; Slice B: 98% for APP 3, 97% for APP 4
Slice A: 90% for APP 1, 90% for APP 2; Slice B: 90% for APP 3, 90% for APP 4
Slice A: 85% for APP 1, 87% for APP 2; Slice B: 86% for APP 3, 88% for APP 4
Information
Region per Network
Time window
Slice A
>App 1
>>how many percent UEs’ experience satisfy
>App 2
>>how many percent UEs’ experience satisfy
Slice B
>App 3
>>how many percent UEs’ experience satisfy
>App 4
>>how many percent UEs’ experience satisfy
Table 1: Region level input information for K-Means
Figure 1. Training process for K-Means, e.g. K=2
K=5, given by PCF or configured in NWDAF, which means that number of load levels is 5
K-Means algorithm
Slice A: 80% for APP 1, 80% for APP 2; Slice B: 80% for APP 3, 80% for APP 4
Slice A: 70% for APP 1, 70% for APP 2; Slice B: 70% for APP 3, 70% for APP 4
Slice Load Level 1 for Slice A
Slice Load Level 1 for Slice B
Slice Load Level 2 for Slice A
Slice Load Level 2 for Slice B
Slice Load Level 3 for Slice A
Slice Load Level 3 for Slice B
Slice Load Level 4 for Slice A
Slice Load Level 4 for Slice B
Slice Load Level 5 for Slice A
Slice Load Level 5 for Slice B
Note: Slice requirement for load level 3 is Slice QoE baseline Requirement from Tenant

## Slide 6: Service Distribution Model Training per Region
Note. It could be a supervised learning based neural network (NN), e.g. Recurrent Neural Network (RNN) which allows to exhibit temporal dynamic behavior for a time sequence.
Slice A
Slice B
……
Cell 1
App 1
NSI 1
NSI X
App P
……
Number of active PDU Sessions in NSI 1
Number of users for application 1
Number of users whose service MOS[0, 3.0]
Number of users whose service MOS[3.0, 4.0]
Number of users whose service MOS[4.0, 5.0]
percentage of service MOS3.0
……
……
……
Region
(e.g. Cell or cell list)
how many percent UEs’ experience satisfy for App 1
how many percent UEs’ experience satisfy for App 2
how many percent UEs’ experience satisfy for App Q
Cell 2
……
Region
(e.g. Cell or cell list)
Slice C

## Slide 7: How NWDAF figure out Network Load Level Info(step 5b)
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
5G NF
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
RAN
CN
NEF
Service Distribution Model training
Service MOS Data
Service MOS model training
NSSF/PCF
Mobile Pay
QoE Requirement +
Load level space +
Region Info(e.g. cell list )
Trained Service Distribution model
Load level Space, e.g. 1=very light, 2=light, 3=normal, 4=congestion, 5=heavy
Region Info, e.g. Cell ID list
QoE Requirement+ Load level space
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
Load
level 3
Load
level 4
.
.
.
Network Load level ID
Corresponding service distribution Infor
Network
Load Level 1:
Slice A
Load Level 1:
Slice B
Load Level 2:
Network
Load Level 2:
Slice A
Load Level 2:
Slice B
Load Level 1:
Network
Load Level 3:
Slice A
Load Level 2:
Slice B
Load Level 3:
Network
Load Level 4:
Slice A
Load Level 4:
Slice B
Load Level 4:
Network
Load Level 5:
Slice A
Load Level 4:
Slice B
Load Level 5:
Load level Infor per Region

## Slide 8
Thanks!

## Slide 9: Network Load Level ID derivation per Load level space
Information
Region per Network
Time window
Application 1
>how many percent UEs’ experience satisfy for application 1
>number of users for application 1
>number of users whose MOS[0, 3.0] for application 1
>number of users whose MOS[3.0, 4.0] for application 1
>number of users whose MOS[4.0, 5.0] for application 1
Application 2
>how many percent UEs’ experience satisfy for application 2
>number of users for application 2
>number of users whose MOS[0, 3.0] for application 2
>number of users whose MOS[3.0, 4.0] for application 2
>number of users whose MOS[4.0, 5.0] for application 2
…
Information
Region per Network
Time window
Application 1
>how many percent UEs’ experience satisfy for application 1
>number of users for application 1
Application 2
>how many percent UEs’ experience satisfy for application 2
>number of users for application 2
…
Table 3: Region level input information for K-Means
Figure 1. Training process for K-Means, e.g. K=2
K=5, given by PCF or configured in NWDAF, which means that number of load levels is 5
K-Means algorithm
Information
Region
Time window
Centroid 1
>Application 1
>>how many percent UEs’ experience satisfy for application 1
>>number of users for application 1
>>number of users whose MOS[0, 3.0] for application 1
>>number of users whose MOS[3.0, 4.0] for application 1
>>number of users whose MOS[4.0, 5.0] for application 1
>Application 2
>>how many percent UEs’ experience satisfy for application 2
>>number of users for application 2
>>number of users whose MOS[0, 3.0] for application 2
>>number of users whose MOS[3.0, 4.0] for application 2
>>number of users whose MOS[4.0, 5.0] for application 2
>Application 3
…
Centroid 2
…
Centroid 5
…
Information
Region
Time window
Centroid 1
>Application 1
>>how many percent UEs’ experience satisfy for application 1
>>number of users for application 1
>Application 2
>>how many percent UEs’ experience satisfy for application 2
>>number of users for application 2
>Application 3
…
Centroid 2
…
Centroid 5
…
Table 4: Centroid for each cluster derived by NWDAF
Figure 2. Cosine Similarity values for different vectors.
Slice QoE Requirement vector from AF: (85%, 92%, 87%, 80%, 80%, …)
Information
Region
Time window
Load Level 1
>Application 1
>>lower bound for how many percent UEs’ experience satisfy for application 1
>>upper bound for how many percent UEs’ experience satisfy for application 1
>Application 2
>>lower bound for how many percent UEs’ experience satisfy for application 2
>>upper bound for how many percent UEs’ experience satisfy for application 2
>Application 3
…
Load Level 2
…
Load Level 5
…
Table 5: Slice Requirement for different load levels
Note: NWDAF will derive the Slice Load Level info based on the same procedure

## Slide 10: Data Collection for Neural Network
Information | Description | Input in Neural Network
Time window | To indicate interval of time associated with a network area | 
Cell ID | To identify a cell | 
Slice A |  | 
>S-NSSAI |  | 
>Network slice instance list |  | 
>>NSI 1 |  | 
>>Number of active PDU Sessions per network slice instance |  | 
>>>Application 1 |  | 
>>>>Application ID 1 | To identify an application | 
>>>>Number of users for application 1 | To indicate number of users for application 1 | 
>>>>Number of users whose service MOS[0, 3.0] | To indicate number of users whose service MOS[0, 3.0] | 
>>>>Number of users whose service MOS[3.0, 4.0] | To indicate number of users whose service MOS[3.0, 4.0] | 
>>>>Number of users whose service MOS[4.0, 5.0] | To indicate number of users whose service MOS[4.0, 5.0 | 
>>>>percentage of service MOS3.0 | To indicate how many percent users within service MOS3.0 | 
>>>Application 2 |  | 
>>>>… |  | …
>>>Application P |  | 
>>NSI 2 |  | 
… |  | …
>>NSI Z |  | 
Slice B |  | 
>… |  | …
Slice C |  | 
>… |  | …
Information | Description | Input in Neural Network
Time window | To indicate interval of time associated with a network area | 
Cell ID | To identify a cell | 
Slice A |  | 
>S-NSSAI |  | 
>Network slice instance list |  | 
>>NSI 1 |  | 
>>Number of active PDU Sessions per network slice instance |  | 
>>>Application 1 |  | 
>>>>Application ID 1 | To identify an application | 
>>>>Number of users for application 1 | To indicate number of users for application 1 | 
>>>Application 2 |  | 
>>>>… |  | …
>>>Application P |  | 
>>NSI 2 |  | 
… |  | …
>>NSI Z |  | 
Slice B |  | 
>… |  | …
Slice C |  | 
>… |  | …
Table 1: Network Information for input layer (only list network information per Cell and network data per region are composed of multiple cells network information)
Information | Description | Output in Neural Network
Region | e.g. Cell or Cell list | 
Time window | To indicate interval of time | 
Application 1 |  | 
>how many percent UEs’ experience satisfy | Region level statistics in the network area | 
Application 2 |  | 
>how many percent UEs’ experience satisfy | Region level statistics in the network area | 
… |  | 
Information | Description | Output in Neural Network
Region | e.g. Cell or Cell list | 
Time window | To indicate interval of time | 
Application 1 |  | 
>how many percent UEs’ experience satisfy | Region level statistics in the network area | 
Application 2 |  | 
>how many percent UEs’ experience satisfy | Region level statistics in the network area | 
… |  | 
Table 2: Network Information for output layer

## Slide 11: First Slice A is deployed and Slice A SLA is met totally
eMBB_MNO slice
AMF
CN
APP | Network slice
 | eMBB_MNO
 | URLLC_OTT2
UE
Operator
Tenant
RAN
NSSF
OAM
MDAS
NSMF
NWDAF
1. QoS profile recommendation per service for slice A
2. Load Level Info for Slice A
  Load Level ID
  Service distribution Info
2. Service distribution Info
per cell per region for slice A
PDU Session Establishment Control
Service Setup Control
PCF

## Slide 12: Slice B Characteristics is learned and Slice B SLA is met partially or totally
eMBB_MNO slice
AMF
URLLC_OTT2 slice
CN
UE
Operator
Tenant
RAN
NSSF
OAM
MDAS
NSMF
NWDAF
PDU Session Establishment Control
Service Setup Control
PCF
PCF
2. Slice B Service distribution
Info per cell per region
APP | Network slice
 | eMBB_MNO
 | URLLC_OTT2
1. QoS profile recommendation per service for slice B
2. Load Level Info for Slice B
  Load Level ID
  Service distribution Info

## Slide 13: Request Management Plane Adjustment when Slice B SLA is partially met
eMBB_MNO slice
AMF
URLLC_OTT2 slice
CN
UE
Operator
Tenant
RAN
NSSF
OAM
MDAS
NSMF
NWDAF
PDU Session Establishment Control
Service Setup Control
1. Slice Congestion Notification +
Slice A/B QoE Requirement
2. Slice QoE
3. Network KPIs Combination
PCF
PCF
4. Slice Resource update
APP | Network slice
 | eMBB_MNO
 | URLLC_OTT2

## Slide 14: Slice Resource Adjustment
5G NF
Mobile Pay
Auto Drive
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
OAM
RAN
CN
Data from OAM
NEF
Slice Resource Configuration Model training
PCF
Slices Requirement
Tenant Requirement for Slice N
Slice B
Slice A
(1)
(2)
(3)
(4)
...
Slice N
(M)
Tenant Requirement for Slice B
Tenant Requirement for Slice A
(1)
(2)
(3)
(4)
…
(M)

## Slide 15: Content
General introduction and discussion
NWDAF Provide Load Level Info to 5GC NF
Network Slice Priority

## Slide 16: Physical Network Deployment per potential Tenant SLA Set
Tenant
Physical Network
Deployment
RAN
Deployment
NSMF
CN
Deployment
TN
Deployment
RAN&CN&TN physical network
Potential Tenant SLA Set
SLA decomposition per domain
Static: physical network deployment per domain

## Slide 17: First Slice A is deployed and Management Plane is to create slice A per the tenant SLA
Creating/configuring
Slice A
RAN-
NSSMF
NSMF
CN-
NSSMF
TN-
NSSMF
CN slice
TN slice
On demand RAN/CN/TN
slice isolation
MDAS
SLA per domain
Tenant A SLA
Physical Network
Deployment
RAN
Deployment
NSMF
CN
Deployment
TN
Deployment
RAN&CN&TN physical network
Potential Tenant SLA Set
SLA decomposition per domain
MDAS-Assisted Management Plane
Slice SLA Management
Static: physical network deployment per domain
Tenant

## Slide 18: NWDAF-Assisted Control Plane Slice A SLA Guarantee
RAN
Service Guarantee for Slice A
PCF
⑤ Slice A QoE Response
- Geo Area
- Service MOS Requirement
e.g. MOS 3.0
- Service MOS Percentage
Requirement e.g. 90%
- Max Users per APP ID, e.g. 1000
- Flow bit rate ,e.g. 2MB
NSSF
NWDAF
Slice A SLA between Operator and Tenant is agreed only after field trial is successfully finished
③ Slice A QoS Parameter Combination
Recommendation per APP ID
④ Slice A load level info
per Region per time
① Slice A QoE Request
- Geo Area
- Service MOS Requirement
e.g. MOS 3.0
- Service MOS Percentage
Requirement e.g. 90%
- Max Users Requirement per APP ID e.g. 1000
- Flow bit rate Requirement ,e.g. 2MB
② Network Load Level Info per Region per time:
- Slice A load level info per Region per time
- S-NSSAI
- Max Registration Users per cell
- Max Users per App ID per cell
- Max Users per MOS Window per APP ID per cell
SMF
AMF
Creating/configuring
Slice A
RAN-
NSSMF
NSMF
CN-
NSSMF
TN-
NSSMF
CN slice
TN slice
On demand RAN/CN/TN
slice isolation
MDAS
SLA per domain
Tenant A SLA
Physical Network
Deployment
RAN
Deployment
NSMF
CN
Deployment
TN
Deployment
RAN&CN&TN physical network
Initial Tenant SLA Set
SLA decomposition per domain
NWDAF-Assisted Control Plane
Slice SLA Guarantee
MDAS-Assisted Management Plane
Slice SLA Management
Static: physical network deployment per domain
Tenant
Notes: 1、Tenant usually have a general SLA per Region and does not care about SLA per cell level
2、Region are usually composed of multiple cells and each cell could have very different characteristic e.g. one cell camping 200 users while another cell only camping 30 users
3、So Slice Load Level information should be composed of information per cell e.g. Max Registration user per cell and Max Users per MOS Window per APP ID per cell as different MOS window have different QoS profile and consequently different resource requirement

## Slide 19: OAM determines network has resource and then new Slice B is created
Creating/configuring
Slice A
RAN-
NSSMF
NSMF
CN-
NSSMF
TN-
NSSMF
MDAS
SLA per domain
Tenant B SLA
Physical Network
Deployment
RAN
Deployment
NSMF
CN
Deployment
TN
Deployment
RAN&CN&TN physical network
Potential Tenant SLA Set
SLA decomposition per domain
Creating/configuring
Slice B
On demand RAN/CN/TN
slice isolation
CN slice
TN slice
RAN
Service Guarantee for Slice A
PCF
⑤ Slice A QoE Response
- Geo Area
- Service MOS Requirement
e.g. MOS 3.0
- Service MOS Percentage
Requirement e.g. 90%
- Max Users per APP ID, e.g. 1000
- Flow bit rate ,e.g. 2MB
NSSF
NWDAF
③ Slice A QoS Parameter Combination
Recommendation per APP ID
④ Slice A Load Level Info
per Region per time
① Slice A QoE Request
- Geo Area
- Service MOS Requirement
e.g. MOS 3.0
- Service MOS Percentage
Requirement e.g. 90%
- Max Users Requirement per APP ID e.g. 1000
- Flow bit rate Requirement ,e.g. 2MB
SMF
AMF
NWDAF-Assisted Control Plane
Slice SLA Guarantee
MDAS-Assisted Management Plane
Slice SLA Management
Static: physical network deployment per domain
② Network Load Level Info per Region per time:
- Slice A load level info per Region per time
- S-NSSAI
- Max Registration Users per cell
- Max Users per App ID per cell
- Max Users per MOS Window per APP ID per cell
① Network Load
Level Info
OAM could take into account Network Load Level Info when determining network has resource
Tenant

## Slide 20: New Slice B with filed trial indication to avoid impacting the agreed Slice A SLA
Deployed Slice A with agreed SLA
AMF
Newly added Slice B without agreed SLA
( field trial phase )
CN
UE
Operator
Tenant
RAN
NSSF
OAM
MDAS
NSMF
NWDAF
PDU Session Establishment Control
Service Setup Control
PCF
PCF
1. Field Test Indication
B is newly added and Slice B Field Test starts without agreed SLA

## Slide 21: NWDAF-Assisted Control Plane Slice B SLA Guarantee and partial or total Slice B Requirement could be met
Creating/configuring
Slice A
RAN-
NSSMF
NSMF
CN-
NSSMF
TN-
NSSMF
MDAS
SLA per domain
Tenant B SLA
Physical Network
Deployment
RAN
Deployment
NSMF
CN
Deployment
TN
Deployment
RAN&CN&TN physical network
Potential Tenant SLA Set
SLA decomposition per domain
Creating/configuring
Slice B
On demand RAN/CN/TN
slice isolation
CN slice
TN slice
RAN
Service Guarantee for Slice A
PCF
⑤ Slice B QoE Response
- Geo Area
- Service MOS Requirement
e.g. MOS 3.5
- Service MOS Percentage
Requirement e.g. 85%
- Max Users per APP ID, e.g. 400
- Flow bit rate ,e.g. 2.5MB
NSSF
NWDAF
③ Slice B QoS Parameter Combination
Recommendation per APP ID
① Slice B QoE Request
- Geo Area
- Service MOS Requirement
e.g. MOS 3.5
- Service MOS Percentage
Requirement e.g. 85%
- Max Users Requirement per APP ID e.g. 500
- Flow bit rate Requirement ,e.g. 3.5MB
SMF
AMF
NWDAF-Assisted Control Plane
Slice SLA Guarantee
MDAS-Assisted Management Plane
Slice SLA Management
Static: physical network deployment per domain
④ Slice B load level info
per Region per time
② Network Load Level Info per Region per time:
- Slice A Load level info per Region per time
- Slice B Load level info per Region per time
- S-NSSAI
- Max Registration Users per cell
- Max Users per App ID per cell
- Max Users per MOS Window per APP ID per cell
Service Guarantee for Slice B
Tenant

## Slide 22: Control plane notify management plane if slice B is partially met
Service Guarantee for Slice B
Creating/configuring
Slice A
RAN-
NSSMF
NSMF
CN-
NSSMF
TN-
NSSMF
MDAS
Network KPIs per domain
Tenant B SLA
Physical Network
Deployment
RAN
Deployment
NSMF
CN
Deployment
TN
Deployment
RAN&CN&TN physical network
Potential Tenant SLA Set
SLA decomposition per domain
Creating/configuring
Slice B
On demand RAN/CN/TN
slice isolation
CN slice
TN slice
RAN
Service Guarantee for Slice A
PCF
⑤ Slice B QoE Response
- Geo Area
- Service MOS Requirement
e.g. MOS 3.5
- Service MOS Percentage
Requirement e.g. 85%
- Max Users per APP ID, e.g. 400
- Flow bit rate ,e.g. 2.5MB
NSSF
NWDAF
③ Slice B QoS Parameter Combination
Recommendation per APP ID
④ Slice B Load Level Info
per Cell per Region per cell
① Slice B QoE Request
- Geo Area
- Service MOS Requirement
e.g. MOS 3.5
- Service MOS Percentage
Requirement e.g. 85%
- Max Users Requirement per APP ID e.g. 500
- Flow bit rate Requirement ,e.g. 3.5MB
② Slice B Load Level Info per cell per Region:
- Max Users
- Time Window
- Max Users per App ID
- Max Users per MOS Window per APP ID
SMF
AMF
NWDAF-Assisted Control Plane
Slice SLA Guarantee
MDAS-Assisted Management Plane
Slice SLA Management
Static: physical network deployment per domain
② Network KPIs Combination
① Slice B Congestion Notification e.g. indicating how much slice B SLA is not met
Tenant

## Slide 23: Alternative Interaction between Control Plane and Management plane
AMF
CN
UE
Operator
Tenant
RAN
NSSF
OAM
MDAS
NSMF
NWDAF
PDU Session Establishment Control
Service Setup Control
1. Slice B Congestion Notification e.g. indicating how much slice B SLA is not met
2. Service QoE data
- UE service MoS data distribution per region per cell
- Slice QoE Requirement
3. Network KPIs Combination
PCF
PCF
4. Slice Resource update
Slice A
Slice B

## Slide 24: Way Forward
Coordination between SA5 and SA2 are required to avoid the conflict adjustment on a case by case basis and SA5 think both management plane and control plane could contribute to better SLA from different aspect, for example:
  SA5 will contribute to SLA in terms of network management optimization aspect
  while SA2 will contribute to SLA by optimizing UE or application service aspect
SA2 acknowledge that the slice SLA (e.g. UE service MoS data distribution per region per cell) discussed in SA2 NWDAF is useful for SLA management and will further study how to provide the information to OAM.
SA2 think slice level congestion in region is more about the summary statistics of UE based application/service experience and would like to clarify with SA5 on what inputs are expected from OAM to support the slice level congestion statistics.
SA2 will study how to provide NWDAF Provide Load Level Info to 5GC NF and network slice priority, which will be discussed in later slides.

## Slide 25: Content
General introduction and discussion
NWDAF Provide Load Level Info to 5GC NF
Network Slice Priority

## Slide 26: How NWDAF Provide Load Level Info to 5GC NF
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
5G NF
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
RAN
CN
NEF
Service Distribution Model training
Service MOS Data
Service MOS model training
NSSF/PCF
Mobile Pay
QoE Requirement +
Load level space +
Region Info(e.g. cell list )
Trained Service Distribution model
Load level Space, e.g. 1=very light, 2=light, 3=normal, 4=congestion, 5=heavy
Region Info, e.g. Cell ID list
Load level Infor per Region
Network Load level ID
Corresponding service distribution Infor
QoE Requirement+ Load level space
Network
Load Level 1:
Slice A
Load Level 1:
Slice B
Load Level 2:
Network
Load Level 2:
Slice A
Load Level 2:
Slice B
Load Level 1:
Network
Load Level 3:
Slice A
Load Level 2:
Slice B
Load Level 3:
Network
Load Level 4:
Slice A
Load Level 4:
Slice B
Load Level 4:
Network
Load Level 5:
Slice A
Load Level 4:
Slice B
Load Level 5:

## Slide 27: Service Distribution Model Training per Region
5G NF
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
RAN
CN
NEF
Service Distribution Model training
Service MOS Data
Service MOS model training
NSSF/PCF
Mobile Pay
Trained Service Distribution model

## Slide 28: NWDAF-assisted Load Level Infor
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
5G NF
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
RAN
CN
NEF
Service Distribution Model training
Service MOS Data
Service MOS model training
NSSF/PCF
Mobile Pay
QoE Requirement +
Load level space +
Region Info(e.g. cell list )
Trained Service Distribution model
Load level Space, e.g. 1=very light, 2=light, 3=normal, 4=congestion, 5=heavy
Region Info, e.g. Cell ID list
QoE Requirement+ Load level space

## Slide 29: NWDAF-assisted Load Level Infor
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
5G NF
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
RAN
CN
NEF
Service Distribution Model training
Service MOS Data
Service MOS model training
NSSF/PCF
Mobile Pay
QoE Requirement +
Load level space +
Region Info(e.g. cell list )
Trained Service Distribution model
Load level Space, e.g. 1=very light, 2=light, 3=normal, 4=congestion, 5=heavy
Region Info, e.g. Cell ID list
QoE Requirement+ Load level space
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
Load
level 3
Load
level 4
.
.
.

## Slide 30: Alternative solution for Question 2 – NWDAF-assisted Load Level Infor
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
5G NF
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
Data Collection
Network Data
RAN
CN
NEF
Service Distribution Model training
Service MOS Data
Service MOS model training
NSSF/PCF
Mobile Pay
QoE Requirement +
Load level space +
Region Info(e.g. cell list )
Trained Service Distribution model
Load level Space, e.g. 1=very light, 2=light, 3=normal, 4=congestion, 5=heavy
Region Info, e.g. Cell ID list
QoE Requirement+ Load level space
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
QoE requirement
for Slice B
QoE requirement
for Slice A
(1)
(2)
(3)
(4)
Load
level 3
Load
level 4
.
.
.
Network Load level ID
Corresponding service distribution Infor
Network
Load Level 1:
Slice A
Load Level 1:
Slice B
Load Level 2:
Network
Load Level 2:
Slice A
Load Level 2:
Slice B
Load Level 1:
Network
Load Level 3:
Slice A
Load Level 2:
Slice B
Load Level 3:
Network
Load Level 4:
Slice A
Load Level 4:
Slice B
Load Level 4:
Network
Load Level 5:
Slice A
Load Level 4:
Slice B
Load Level 5:
Load level Infor per Region

## Slide 31: Alternative solution for Question 3 – NSSF Request OAM Adjustment
    PCF prioritizes slice A + B due to lack of resource
Slice B
Slice A
(1)
(2)
(3)
(4)
Tenant Requirement for Slice B
Tenant Requirement for Slice A
(1)
(2)
(3)
(4)
OAM/MDAS
5G NF
Mobile Pay
Auto Drive
Vertical(URLLC)
NWDAF
Service MOS Measurement and Service SLA Monitoring
Video
RAN
CN
NEF
Slice Resource Configuration Model training
Data
Collection
Network Data
Service QoE
Data
NSSF/PCF
OAM/NSMF
Network slice KPI
Data collection
Service Distribution Model training
Service MOS Data
Slice B Congestion Notification e.g. indicating how much slice B SLA is not met
Network KPIs Value
(for slice A+B)

## Slide 32: Content
General introduction and discussion
NWDAF Provide Load Level Info to 5GC NF
Network Slice Priority

## Slide 33: Procedure for newly added slice B with Field Test Indication
Step 1. Given that a network has deployed Slice A and new slice B is created, field test for slice B begin and Slice B SLA is not signed.
Step 1. NSSF subscribes the network load level information per region per time to the NWDAF;
Step 2. NSSF temporarily indicates slice B Field Trial Indication to PCF to avoid impacting the agreed SLA for Slice A i.e. RAN will prioritize Slice A related activity compared to slice B.
Step 3. Slice B Field Test complete and Slice B SLA is signed
Step 4. NWDAF notifies the slice B load level information to the NSSF.
Step 5. NSSF determines to remove the slice B Field Trial Indication .