## Slide 1: Summary of options for S-NSSAI in Access Stratum signalling
Intel

## Slide 2
Summary of SA2#129 proposals for S-NSSAI in AS signaling
 | A (S2-1810183) | B (S2-1810248) | C (S2-1810389)
S-NSSAI in RRC message | Each S-NSSAI can be configured with a “requiring privacy“ indication. S-NSSAIs without “requiring privacy” indication are provided in RRC as cleartext. S-NSSAIs with “requiring privacy” indication are not provided in RRC. | S-NSSAI is not signalled in RRC at all. | Based on Serving PLMN indication in Registration Accept the UE either signals S-NSSAI in RRC for all Initial NAS messages as cleartext or it does not.
Consequences | Additional configuration per S-NSSAI. For S-NSSAI with ”requiring privacy” indication the initial N2 message is routed to a default AMF, followed by AMF re-allocation (increased signalling in the network). For S-NSSAI without ”requiring privacy” indication the S-NSSAI is sent as cleartext. Efficient N2 routing might occur, but no privacy protection in AS for the S-NSSAIs without ”requiring privacy” indication. | Initial N2 message always routed to a default AMF, followed by AMF re-allocation. Increased signalling in the network. | When S-NSSAI is signalled in RRC, it is sent as cleartext. Efficient N2 routing, but no privacy protection in AS. When S-NSSAI is not signalled in RRC, initial N2 message always routed to a default AMF. Increased signalling in the network.

## Slide 3: Additional comments
Input proposal in S2-1810095 (Intel) has been superceded by S2-1810389 (Nokia et al.)
None of the options A, B and C provides simultaneously both S-NSSAI privacy protection in Access Stratum and efficient routing of the initial N2 message
Some companies (S2-1810095) are of the opinion that addressing both S-NSSAI privacy protection and efficient routing of initial N2 message requires public key encryption at Access Stratum level, which can be considered as a future enhancement
It is noted that with non-3GPP access all “access stratum” information is encrypted as part of IKEv2/IPsec procedures on NWu
….