## Slide 1: Discussion for Solution 32 for How to ensure that slice SLA is guaranteed China Mobile, Huawei

## Slide 2: Background: Resource isolation between slices by RAN/OAM
General Principles and Requirements for Resource isolation between slices
  NG-RAN supports resource isolation between slices.
  NG-RAN resource isolation may be achieved by means of RRM policies and protection mechanisms that should avoid that shortage of shared resources in one slice breaks the service level agreement for another slice.
  It should be possible to fully dedicate NG-RAN resources to a certain slice.
  How NG-RAN supports resource isolation is implementation dependent.
Each slice may be assigned with either shared or dedicated radio resource up to RRM implementation and SLA. To enable differentiated handling of traffic for network slices with different SLA:
  NG-RAN is configured with a set of different configurations for different network slices by OAM;
  To select the appropriate configuration for the traffic for each network slice, NG-RAN receives relevant information indicating which of the configurations applies for this specific network slice.
Attribute name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable
nCGI | M | T | T | F | T
pLMNIdList | M | T | T | F | T
sNSSAIList | CM | T | T | F | T
rRMPolicyType | CM | T | T | F | T
rRMPolicyNSSIId | CM | T | T | F | T
rRMPolicyRatio | CM | T | T | F | T
rRMPolicy | CM | T | T | F | T
Attribute related to role |  |  |  |  | 
rRMPolicyRatio | The RRM policy setting the ratio for the split of the Radio resources between the supported NSIs. It is the list of target percentage values assigned to the corresponding rRMPolicyNSSIId values. Every value specifies the percentage of PRBs to be allocated to the corresponding NSSI, in average over time. The sum of the values shall be less or equal 100. allowedValues: 0 : 100 NOTE: The averaging time interval is implementation dependent | type: Integer multiplicity: 1..* isOrdered: N/A isUnique: N/A defaultValue: None allowedValues: N/A isNullable: False
rRMPolicy | It represents RRM policy which includes guidance for split of radio resources between multiple slices the cell supports in case when the rRMPolicyType is absent or equal to 0.. The RRM policy is implementation dependent. allowedValues: Not applicable | type: String multiplicity: 1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False
Extracted from TS 28.541 Clause 4.3.4.2
Extracted from TS 28.541 Clause 4.4.1
Extracted from TS 38.300 Clause 16.3.1
Extracted from TS 38.300 Clause 16.3.3

## Slide 3: Overview: how to guarantee slice SLA by MP and CP
  Slice QoE calculation: Based on service MOS and network data, NWDAF trains the Service MOS model and measure service MOS per slice.
  Control Plane in 5GC:
  Based on slice QoE from NWDAF, NSSF evaluates the slice SLA fulfilment Info and perform admission control for the new slice;
  NSSF recognizes the problematic area based on the feedback from NWDAF, and sends the slice SLA fulfilment Info per problematic area.
  Slice level RAN resource schedule: Within the RAN resource configured by OAM, RAN schedule slice level resource based on slice SLA fulfilment Info from NSSF.
  Slice level RAN resource adjustment: Based on slice QoE, OAM trains slice resource model and adjust the slice level resource configuration.
Slice level resource configuration and schedule:
- Existing Slice:
> Guaranteed: 10%
> Maximum: 15%
- New Slice (Initial)
> Guaranteed: 20%
> Maximum: 25%
RAN
NSSF
(Admission Control + Slice Evaluation)
CN
OAM (Slice Creation + Slice Resource Configuration/Adjustment)
 Resource Configuration
3rd AF
⑤ Existing/New slice QoE
Slice SLA Requirement (i.e. Slice QoE Requirement)
- Network Area
- Average Service MOS
- Number of Subscribers
- Percentage Ues’ experience satisfied
NWDAF
(Slice QoE calculation)
② Existing/New slice QoE (Network Area by Tenant)
③ Problematic Area Query
- Average Service MOS < 3
- Percentage Ues’ experience satisfied < 80%
① Initial number of subscribers + slice SLA requirement
AMF
New Slice
Existing Slice
PCF
PCF
⑥ Resource Adjustment
Service MOS
④ Slice SLA fulfilment Info per Problematic area
(Underfit , Overfit)

## Slide 4
Underfitting
Fitting
Overfitting
  In Figure 1 (Off-peak time) and Figure 2 (Peak Time):
  OAM initially configure the RAN resource for the new slice i.e. Guaranteed Slice Radio Resource (e.g. 20%) and Maximum Slice Radio Resource by OAM (e.g. 30%), which are similar to the GFBR and MFBR per QoS flow.
  RAN firstly schedules 20% RAN resource for the new slice, and then the adjust RAN resource based on the slice SLA fulfilment Info by NSSF until the slice SLA requirement is fulfilled:
      When slice SLA fulfilment is more than the slice SLA requirement, RAN schedule less slice level RAN resource
      When slice SLA fulfilment is less than the slice SLA requirement, RAN schedule more slice level RAN resource
  In figure 3, base on slice QoE and OAM data, OAM trains slice resource model and indicate RAN adjust the slice level RAN resource configuration, e.g.
  Guaranteed Slice Radio Resource ，e.g. 20%->18%；
  Maximum Slice Radio Resource ，e.g. 30->28%。
Maximum Slice Radio Resource by OAM
Guaranteed Slice Radio Resource by OAM
Chart: Figure 3: Slice Resource adjustment by OAM
| 00:00-06:00 | 06:00-12:00 | 12:00-18:00 | 18:00-24:00
 | 0.15 | 0.25 | 0.23 | 0.2
Example: how to guarantee slice SLA by MP and CP
Chart: Figure 2: Peak Time (11:00 - 14:00)
| Initial | Round 1 | Round 2 | Round 3 | Round X | Round X+1
 | 0.2 | 0.21 | 0.23 | 0.26 | 0.24 | 0.25
…
Chart: Figure 1: Off-peak Time (00:00 - 06:00)
| Initial | Round 1 | Round 2 | Round 3 | Round X | Round X+1
 | 0.2 | 0.19 | 0.17 | 0.14 | 0.16 | 0.15
…
Decrease Slice Resource Schedule
Decrease Slice Resource Schedule

## Slide 5
Based on the discussion, it is proposed to update the solution 32 in S2-1900582.
Proposal

## Slide 6
Thanks!