## Slide 1: Source: Ericsson Title: EPC Dedicated Bearers for Ethernet Document for: Decision Agenda Item: 6.31 Work Item / Release: TEI16 / Release 16

## Slide 2: Background
S2-1813344 endorsed in SA2#129bis (November 26 - 30, 2018, West Palm Beach, USA)
  Rationale (from S2-1813344 ):
    3GPP’s ecosystem continues to expand to more than smartphones
    Many parts of the world (see annex) might not be in 5GCore coverage
    Small/Medium Enterprises in developed countries might not get dedicated in-building cells
    Reasonable number of applications (machines) expected to only use Ethernet (without IP)
    Many machines require QoS with some guarantees, e.g. a GBR bearer
    EPC does not allow GBR bearers to be the default bearer.

## Slide 3: What PDN type to be used to Ethernet traffic in EPS ?
[Observation-1] Information of Ethernet type is needed for the basic functionalities such as traffic routing over SGi and Policy Control.
[Proposal-1] It’s proposed to introduce new PDN type Ethernet in EPS to have a clean solution.
Specifics for Non-IP traffic and Ethernet traffic
 | Non-IP PDN connection in EPS | Ethernet PDU Session in 5GS
Traffic routing over SGi/N6 | Some tunnelling mechanism is needed over SGi | Ethernet routing
ARP Proxy | NA | SMF can request for proxying function in UPF for Ethernet PDU Session
PCC | Non-IP type is not supported by PCC (in EPC) ; | PCF need to know the Ethernet Type in order to e.g. to provide a list of MAC address, or provide packet filters based on layer 2 address (e.g. VLAN, MAC).
IP address allocation | IP address is allocated for Non-IP type PDN connection, but IP address is not sent to the UE; | In Rel-15, IP address is not allocated to PDU Session of Ethernet Type (23.501 clause 5.6.10.2)

## Slide 4: What network architecture for EPS ?
Arch-Option-1 Enhance PCC in EPC to support Ethernet PDN type
MME
eNB
SGW
SGi
Ethernet network
HSS
PCRF
Rx
Gx
Arch-Option-2 Using PCC in 5GC (i.e. PGW-C+SMF and PCF)
MME
eNB
SGW
SGi/N6
Ethernet network
HSS
PCF
N5
N7
[Observation-2] Arch-Option-1 means that Gx and Rx (which are diameter) need to be enhanced to support Ethernet specifics.
[Observation-3] Arch-Option-1 means that Sx interface between PGW-C and PGW-U needs to be enhanced to support Ethernet specific functionalities.
[Observation-4] Arch-Option-2 (currently for 5GS-EPS interworking) could be adopted to support PDN Connection of Ethernet type, which can avoid update to Gx, Rx and Sx.
[Proposal-2] It’s proposed to adopt Arch-Option-2 to minimize the impact to the system
PGW-U
PGW-C
Sx
PGW-C+SMF
UPF
N4

## Slide 5: Assumptions
Dedicated APN is used for Ethernet PDN connection
Mobility to 2G/3G for Ethernet PDN connection is not required
Ethernet PDN type is not required for WLAN
Homogeneous Ethernet support in MME and SGW (AMF check MME capability but not SGW’s). At mobility, AMF or MME knows if the target/new MME support Ethernet through local configuration.

## Slide 6: Affected EPS Procedures and Functions
Initial Attach
  New PDN type in UE, MME, SGW, and PGW
Inter-MME mobility,
  TAU (Intra-LTE)
  Handover (Intra-LTE)
    Additional configuration in MME for Ethernet capability in EPS:
    if the new/target MME does not support Ethernet but support Non-IP, or
    the new/target MME support neither Ethernet nor Non-IP ?
Dedicated bearer
  New packet filters (TFT currently specified in TS 23.060)
Functional that may be affected, e.g.
  PGW selection
  SGW selection
  MME selection
  PCRF/PCF selection
  Data Off
  …

## Slide 7: Affected 5GS procedures
PDU Session Establishment
MME
AMF
  PDU Session Est Req (UE’s EPS capability of Ethernet)
  PDU Session Est Accept (Network support Ethernet in EPS)
At 5GS to EPS mobility with N26
PGW-C+SMF sends back that Ethernet is supported EPS (based on UE and PGW-C capability.
For Ethernet PDN Type is supported in EPS, for PDU Session Ethernet, EBI allocation may also required for additional QoS Flows.
AMF
  Fetching EPS PDN Connections (MME capability of Ethernet PDN Type)
AMF sends the MME’s Ethernet capability (by local configuration) to SMF when fetching EPS PDN Connections.
V-SMF
MME
At 5GS to EPS mobility without N26
AMF
  Attach (PDN Connectivity Request (PDN Type = Ethernet ))
Attach accepted if Ethernet is supported by MME.
Q: Should UE fallback to non-IP ?
PDU Session of Ethernet Type established, UE and PGW-C supports Ethernet
PGW-C+SMF
PGW-C+SMF
PGW-C+SMF

## Slide 8: Proposed Update in specs
23.401 CR 3498 (S2-1901602)
23.501 CR0929 (S2-1901603)
23.502 CR1027 (S2-1901604)
More to come, e.g.
  23.060 to support Ethernet packet filters in TFT

## Slide 9
THANK YOU !