## Slide 1: Discussion on TSN protocols related to Key Issue#3 Huawei

## Slide 2
IEEE 802.1 TSN Standards/Projects
- 802.1Qav: Credit Based Shaper
- 802.1Qbu: Frame preemption
- 802.1Qbv: Enhancements for Scheduled Traffic
- 802.1Qch: Cyclic Queuing and Forwarding
- P802.1Qcr: Asynchronous Traffic Shaping
TSN Standards/Projects related to Key Issue#3
Latency & Scheduling
Resource Management
- 802.1Qat: Stream Reservation Protocol - 802.1Qcc: TSN configuration (SRP Enhancements)
- P802.1CS: Link-local Registration Protocol
- P802.1Qdd: Resource Allocation Protocol
Time Synchronization
- 802.1AS: Timing and Synchronization
Note: Protocol in red color are under development

## Slide 3: Various packet scheduling mechanisms defined in TSN
802.1Qav: credit-based traffic shaping.
802.1Qbv: provide performance assurances latency and delivery variation by scheduling TSN streams in time-aware traffic windows.
802.1Qbu: addresses the low latency requirements by preempting the transmission of a non-time-critical frame and allowing for one or more time-critical frames to be transmitted.
802.1Qch: specifies synchronized cyclic enqueuing and queue draining procedures. Its conjunction with 802.1Qci and 802.1Qbv ensures that all frames are guaranteed to be transmitted within their allotted cycle time.
P802.1Qcr (ongoing project): guarantees an upper bound on latency by providing an additional layer of shaped egress queues to merge flows into the existing queue structure. It does not rely on time synchronization between bridges.
TSN includes different scheduling mechanisms. Some of these protocols/projects (e.g. 802.1Qav, P802.1Qcr) can be applied to the TSN Streams with latency requirement (but no strong jitter limitation), while others can be applied to the TSN Streams with both latency and jitter (e.g. 802.1Qbv, 802.1Qch).

## Slide 4: TSN Standards/Projects for Resource Management/Configuration
Fully distributed model
  802.1Qat (SRP)
  802.1Qcc (SRP Enhancements)
  P802.1CS (ongoing project)
  P802.1Qdd (ongoing project)
The three deployment models are still under development in IEEE TSN. Each deployment model has its own cros and pros. In 3GPP, it’s not possible to exclude any deployment option for now.
  Centralized network and distributed user model/Fully centralized model
  802.1Qcc
  Centralized network and distributed user model
  Fully centralized model

## Slide 5: Proposals for Endorsement
Interworking with TSN with different scheduling mechanisms (802.1Qav/ 802.1Qbv/ 802.1Qbu) shall be considered in SA2.
Interworking with TSN with 3 deployment models (centralized/fully distributed/hybrid) defined in 802.1Qcc shall be considered in SA2.

## Slide 6
Thank you