## Slide 1: 5G LAN group configuration (for endorsement)
Feb 19. 2019
Samsung
3GPP TSG SA WG2 Meeting #131
February 25 – March 1, 2019, Santa Cruz, Tenerife, Spain
S2-1902105

## Slide 2: 5G LAN user and 5G LAN group
5G LAN group: a list of the UE(s) that are allowed to access 5G LAN-Virtual Network with a 5G LAN group configuration
5G LAN user: a member of a 5G LAN group. Identified by GPSI
UE Subscription data (stored in UDR as a part of UE Subscription, managed by UDM, used by SMF) |  | 
Subscription data type | Field | Description
SMF Selection Subscription data (data needed for SMF Selection as described in clause 6.3.2 of TS 23.501 [2]) SMF Selection | SUPI | Key
 | S-NSSAI | Indicates the value of S-NSSAI
 | Subscribed DNN list | List of the subscribed DNNs for the UE (NOTE 1)
 | Default DNN | The default DNN if the UE does not provide a DNN (NOTE 2).
 | LBO Roaming Information | Indicates whether LBO roaming is allowed per DNN, or per (S-NSSAI, subscribed DNN)
 | Interworking with EPS indication list | Indicates for which DNN from the Subscribed DNN list interworking is supported.
Group Subscription data (stored in UDR as a part of group Subscription, managed by UDM) |  | 
Subscription data type | Field | Description
Group Identifier translation | External Group Identifier | Identifies external group of UEs that the UE belongs to as defined in TS 23.682 [23]
 | (Optional) Internal Group Identifier | Identifies internal group of UEs that the UE belongs to as defined in TS 23.501 [2]
 | SUPI list | Corresponding SUPI list for input External Group Identifier
 | Group Type | Type of Group e.g. 5G LAN Group
 | Domain ID | An administrative domain
5G LAN specific data | 5G LAN Configuration ID(s) | List of identifiers for the 5G LAN Group Configuration.

## Slide 3: 5G LAN group configuration
5G LAN group configuration
  a set of 5G LAN-Virtual Network’s configurations that are used for the UE belonging to the 5G LAN group to establish a PDU Session. It is stored in UDR as a part of Application Data and can be managed by AF.
  5G LAN group configuration is agnostic to 5G LAN group
    5G LAN group configuration shall be identified by its own identifier, which is independent from 5G LAN Group Identifier
    A multiple 5G LAN groups may share the same 5G LAN group configuration
  5G LAN group configuration consists of the following configurations:
    PDU Session related information: DNN, S-NSSAI, PDU Session Type, VLAN Tags, etc
    Related URSP
    Service Area Restriction: CAG, LADN or a configured list of TAI or cell
5G LAN group configuration (stored in UDR as a part of Application Data, managed by NEF) | 
Parameters | Description
5G LAN Configuration ID | A unique identifier to refer the 5G LAN group configuration
Group ID(s) | List of the external group IDs. Each group is allowed to use this configuration
PDU Session related Information | DNN, S-NSSAI, PDU Session Type, VLAN Tags
Related URSP | A set of URSP rules
Service Area Restriction | CAG, or a configured list of TAI, or LADN

## Slide 4: Relationship among UE, Group and 5G LAN configuration
5G LAN member (UE), 5G LAN group, 5G LAN group configuration
5G LAN group configuration
5G LAN group configuration
5G LAN group
n:m relationship
5G LAN user
(UE)
n:m relationship
A 5G LAN user can belong to multiple 5G LAN group
A 5G LAN group can include multiple 5G LAN user
A 5G LAN group configuration can be shared by multiple 5G LAN group
A 5G LAN group is allowed to access multiple 5G LAN group configuration
SUPI (identifier)
Internal Group ID list
Internal Group ID
SUPI list
List of 5G LAN group configurations
5G LAN Configuration ID
List of External group IDs that is allowed to use this configuration

## Slide 5: Benefit of N:M relationship
Operators are able to re-use the same 5G LAN configuration for multiple 5G LAN groups
  For the case when the operators provisioned a 5G LAN Virtual Network for a specific purpose, the operator can keep the same configuration, however the 5G LAN group can be more dynamic based on re-organization or inviting partner’s customers, etc.
A 5G LAN group is allowed to access multiple 5G LAN configurations based on its needs.
  For example, all members of newly formed task force team request to join the two or more existing 5G LAN Virtual Network since they wants to share the two isolated group’s networks.
5G LAN Virtual Network
Group A
Group B
5G LAN group configuration
(DNN, S-NSSAI)
A one 5G LAN group configuration is shared by multiple 5G LAN groups
Group A
5G LAN Virtual Network 1
5G LAN Virtual Network 2
5G LAN group configuration 1
(DNN1, S-NSSAI)
5G LAN group configuration 2
(DNN2, S-NSSAI)
A one 5G LAN group is allowed to access multiple 5G LAN Virtual Networks configured by 5G LAN group configurations

## Slide 6: Proposals
Proposal 1. It is proposed to add a separate a new application data records – titled as “5G LAN group configuration”, which is stored in UDR as a part of Application Data, is managed by NEF.
Proposal 2. It is proposed to add a reference of 5G LAN group configuration to the Group Subscription Data.
Proposal 3. It is proposed to define n:m relationship between the 5G LAN group configuration and 5G LAN group.