## Slide 1: URLLC Key Issue #7: Automatic GBR service recovery after handover / at GFBR establishment Suggested Way Forward after drafting session
Document for Approval
Source: Vodafone
SA WG2 Meeting #131 February 25 – March 1, 2019, Santa Cruz, Tenerife, Spain
Agenda item: 6.20
Tdoc S2-1902751
Rev of S2-1902739

## Slide 2: Results of offline session
An earlier offline session reviewed a set of questions in S2-1902185
The debate on some questions reached consensus, others were inconclusive.
This document attempts to summarise the status..
And proposes a way forward

## Slide 3: Questions + Answers (1)
a) is a core network timer based solution sufficient?
Concensus that some mechanism is needed in addition to any CN timer based solution.
b) is this an MBR>GBR case (as in V2X TR 23.786 solutions #16, #17, #27) or does this relate to the Bit Rate that the machine really needs?
Seem to need to solve at least the case when the minimum GBR can no longer be met.
c) Is it useful that the RAN can check over a time period [eg 2 seconds] before notifying the Core Network that the GFBR QoS level is now available again?
Seem to agree that the capability for the RAN to do some averaging over time is useful.

## Slide 4: Questions + Answers (2)
d) do we need to define a new QoS parameter or just re-use the R15 Notification Control parameter?
No concensus on this – but quite some interest in making the RAN aware that this is an “auto-restore GFBR” flow rather than a “traditional GBR bearer”
e) do we want the function to work at Flow Establishment (and Modification)?
Yes.
f) (when the QoS cannot be met) at handover, should the target reject the flow and then the core network request its (re-)establishment, or, does the RAN accept the flow and ‘notify’ the core network that QoS is not met?
No concensus. Some suggestions to revert R15 CR agreed in last meeting so that target cell could “optionally” admit the flow and immediately send ‘notification’. But this matched by opposition to having optional rather than deterministic RAN behaviour.

## Slide 5: Questions (3)
g) (when the QoS cannot be met) does the RAN map the GFBR flow into e.g. the same Logical Channel Group as the default flow, or, does it allocate the GFBR flow to a separate Logical Channel Group (LCGs are linked with uplink Buffer Status Reports)?
Not fully discussed.
h) Will the RAN continue allocating the uplink/downlink resource to the QoS Flow (after notifying the core network)
Not fully discussed.
i) Does the UE need to be informed by signalling that the GFBR can’t be guaranteed?
No concensus
j) (if g is yes) is this RRC or MM or SM signalling?
Not fully discussed

## Slide 6: Way Forward proposed by Vodafone to solve KI#7 part 1
A) Use a new parameter in the QoS related signalling to indicate to the RAN that this is an “auto-restore GFBR” flow rather than a ‘release when GBR cannot be met’ flow. 1) a new parameter (rather than new resource type) enables GFBR 5QI characteristics to be reused
2) the new parameter points to the new RAN functionality that is needed (see next few bullets).
B) At Flow Establishment and Handover the RAN performs “3 step admission control’
1) perform ‘legacy, Release 9 style’ GFBR admission control.
2) If step one is unsuccessful, the RAN checks that there is a reasonable chance to serve the request in the future (e.g. that the UE does not request more GBR resources than the complete cell can support).
3) if the request is “reasonable”, the RAN performs admission control as for a non-GFBR flow with arbitrary, low quality, QoS.
C) The core network AND UE are informed of the outcome of the admission control. Both are informed if subsequently the QoS cannot be guaranteed / when it can be guaranteed again. 1) RRC signalling is used to inform the UE of the lack of Guarantee / restoration of the Guarantee.
2) if the DRB and Logical Channel Group are configured for the GFBR flow, the UE discards uplink packets for that flow when their [survival time] expires

## Slide 7: Way Forward proposed by Vodafone to solve KI#7 part 2
D) Implementation specific RAN mechanisms attempt to restore the QoS As Soon As possible (e.g. re-attempt ‘legacy’ admission control every 250ms, and restart after 4 “successes”.)
E) Xn-AP (and N2-AP) Handover signalling parameters are added to allow the source RAN to consider handover to other target cells if the first target cell cannot Guarantee the GFBR flow.

## Slide 8: Backup

## Slide 9: After Kochi meeting, KI#7 has at least the following proposed solutions (List from S2-1901818, LG Electronics)
Solution #16 "Automatic GBR service recovery after handover"
Solution #20 "SMF starts the pending timer for the non-accepted GBR QoS flow" : proposed by S2-1901362 (CR#0010, Qualcomm)
Solution #21 "Extending notification control for QoS flow setup and handover" : proposed by S2-1901363 (CR#0011, CATT)
Solution #22 "Automatic GBR service recovery after handover" : proposed by S2-1901364 (CR#0013, LGE)
Solution #23 "Always On control for URLLC GBR QoS Flow" : proposed by S2-1901374 (CR#0015, Tencent)

## Slide 10: Key Issue #7; Automatic GBR service recovery after handover (TR 23.725 v1.2.0)
When a machine needs a Guaranteed Bit Rate service, it is likely to need that quality level in order to do its job. Hence if the QoS level cannot be maintained (e.g. handover into a congested cell; temporary cell overload due to higher priority services; etc), the QoS level should be restored as soon as possible, and, without a storm of signalling messages.
Release 15 5GC has partially solved this issue by introducing a "notification" mechanism that allows the core network to request the RAN to not release the radio bearer/QoS Flow when the QoS guarantee cannot be met, but, instead to notify the Core Network when the QoS drops, AND, when the RAN has restored the QoS level. This allows the controller of the machine (e.g. car/train) to adapt its behaviour (e.g. reduce speed) and ensures that the RAN continues to try to restore the QoS level while the device is in that cell.
However, at Xn or N2 handover, the target RAN node applies admission control and if it cannot support the required GBR QoS, the target RAN node does not establish that QoS Flow. In such a case, if, e.g. due to movement of the UE, the source RAN node has no choice but to handover to that target RAN node, then the target RAN node will complete the handover but will NOT notify the CN if and when the GBR QoS can be supplied to that UE.
As the machine needs to have its GBR service restored as soon as possible, the CN needs to repeatedly attempt to re-establish the GBR service. These re-attempts involve a considerable number of signalling messages, and are sent without any awareness of RAN congestion or potential link quality.
This is an inadequate solution for any mobile "non-human device" that needs to maintain a GBR data link during mobility (e.g. a car, a train, robots moving around a factory).

## Slide 11: End