## Slide 1
Vertical_LAN
TSC drafting session
TSC drafting session
Devaki Chandramouli
26-02-2019

## Slide 2
Architecture: Integration of 5GS with the TSN network
S2-1902008 - Discussion on Support of 5GS integration with TSN (Huawei)
S2-1902009 - 23.501 CR1001 (Rel-16, 'B'): Support of 5GS integration with TSN (Huawei)
S2-1902060 23.501 CR0871R2 (Rel-16, 'B'): TSC Architecture (Nokia)
Consensus:
TSN Translator exists on both the sides (UPF/UE). TT is assumed to support de-jittering functionality, collocated with the UPF. All other functionalities of TT is still FFS, reference point between UPF/UE and TT is left open.
Commonality between the CRs:
Architecture, presence of TSN Translator within the UPF
Differences between the CRs:
Presence of TT within the UE
UPF functionality description, TSN Translator potential impacts (2060)
Bridge management / port information
Way forward agreed:
- Need one merged paper to handle 5GS integration. Consider Bridge management aspects independently. Revise S2-1902060 and merge architecture aspects from 2009.

## Slide 3
List of all papers
TSC time synchronization
S2-1901637 23.734 CR0008 (Rel-16, 'C'): The synchronization precision requirement over Uu (Vivo)
S2-1901641 Discussion and proposal for Key Issue 3.2 Time Sync in TSN (OPPO)
S2-1901709 TSN Time Synchronization Solutions: Down-selection (QCOM)
S2-1901722 23.734 CR0012 (Rel-16, 'C'): 5G system support for multiple external time domains: Option 3 (Ericsson)
S2-1901723 23.734 CR0013 (Rel-16, 'C'): Evaluation of TSN Sync solns (Ericsson)
S2-1901924 23.734 CR0002R1 (Rel-16, 'B'): Evaluation for time synchronisation using TSN (key issue 3.2) (Samsung)
S2-1901927 23.734 CR0014 (Rel-16, 'B'): Conclusion for time synchronisation using TSN (key issue 3.2) (Samsung)
S2-1901999 Discussion and proposal on the Time Sync solutions (Ericsson)
S2-1902000 23.734 CR0015 (Rel-16, 'F'): Evaluation and proposal for the Time Sync solutions (ZTE)
S2-1902064 23.734 CR0016 (Rel-16, 'C'): Update to Solution 11 Option 2 TSN Time Synchronization (Nokia)
S2-1902065 Way forward proposal for TSN Synchronisation (Nokia)
S2-1902066 23.734 CR0017 (Rel-16, 'C'): Way forward proposal for TSN Synchronisation CR (Nokia)

## Slide 4
TSN Sync - Candidate solutions proposed for conclusion
Solution 11 Option 2
Solution 11 Option 3
Solution 28
RAN2 (unofficial) update:
RAN2 had a show of hands which showed 10 companies in favour of 11.2 and 8 companies in favour of 11.3 so it was a close vote
Discussion: time stamping in User Plane AS stack are not preferred due to high complexity in RAN.
Way forward:
Update solutions #2/#3/#28 (e.g. how it works with QoS aspects) and strive for a decision SA2#132
Agree that the time sync needs to be conveyed to the UE.
Notes: Eventually the choice will have to be done by SA2 among Solution 11.2, 11.3, 11.4 and 28.2 (which according to RAN2 understanding is the same as 11.3).
RAN2 will indicate that 28.1 and 17 are not feasible from RAN2 point of view while 19 and any other solution assuming

## Slide 5
TSC QoS
Hold and forward buffer for de-jittering
S2-1902062 23.501 CR1008 (Rel-16, 'B'): Introducing support Hold and Forward Buffers for TSC Deterministic QoS (Nokia)
QoS Assistance parameters:
S2-1901710 23.501 CR0946 (Rel-16, 'B'): New QoS parameter Time Offset (Qualcomm)
S2-1902061 23.501 CR1007 (Rel-16, 'B'): Introducing support TSC Deterministic QoS (Nokia)
S2-1902063 23.501 CR1009 (Rel-16, 'B'): Introducing support UE and UPF Residence Time for TSC Deterministic QoS (Nokia)
S2-1901928 Enhancements to 5GS QoS framework for support of deterministic communication (Samsung)
S2-1901932 23.501 CR0830R1 (Rel-16, 'B'): Deterministic Communication QoS Class (Samsung)
QoS negotiation and parameter mapping:
S2-1901717 TSN-5GS QoS mapping (Ericsson)
S2-1901718 23.734 CR0009 (Rel-16, 'C'): TSN-5GS QoS mapping (Ericsson)
S2-1902011 23.501 CR1003 (Rel-16, 'B'): QoS parameters mapping between TSN charicters and 5G QoS (Huawei)
S2-1901840 23.501 CR0970 (Rel-16, 'B'): User plane based QoS negotiation between 3GPP and TSN networks (HUA)
S2-1901720 23.734 CR0010 (Rel-16, 'C'): Support for IEEE 802.1Qbv scheduling (Ericsson)

## Slide 6
TSC QoS - QoS Parameters – RAN2 email discussion outcome/related CRs
S2-1901710 23.501 CR0946 (Rel-16, 'B'): New QoS parameter Time Offset
S2-1902061 23.501 CR1007 (Rel-16, 'B'): Introducing support TSC Deterministic QoS
S2-1901928 Enhancements to 5GS QoS framework for support of deterministic communication
S2-1901932 23.501 CR0830R1 (Rel-16, 'B'): Deterministic Communication QoS Class
Way forward:
Incoming LS from RAN2 – S2-1902723
S2-1902061 – used as a basis for QoS parameters, to be provided as TSN Assistance information (reference to S2-1902723).

## Slide 7
Other items to be discussed
Hold and Forward buffer for de-jittering (consensus in SA2 discussion)?
Other aspects:
  UE/RAN/UPF residence time
  Survival time
  Where should the mapping of IEEE TSN to 5GS parameters/QoS characteristics be done?
    Mapping of parameters: IEEE CNC <-> 5GS QoS
  Exposure of 5GS QoS characteristics to IEEE TSN System.
  Deriving QoS requirements via UP (support for SRP) -> this is also related to Bridge management discussion.
  Other critical points
Way forward:
------

## Slide 8
TSC deployment model
S2-1901839 Discussion on TSN protocols related to KI#3 (Huawei)
S2-1901998 Discussion on traffic pattern and QoS (ZTE)
S2-1901719 Support for IEEE 802.1Qbv scheduling (Ericsson)
Discussion points:
Support for fully distributed model in Rel-16?
Fully distributed model
  802.1Qat (SRP)
  802.1Qcc (SRP Enhancements)
  P802.1CS (ongoing project)
  P802.1Qdd (ongoing project)
Way forward:​
- IEEE Qbv (protocol), Centralized model is supported in Rel-16; hybrid model is partially supported in Rel-16. Implication of partial support is FFS Distributed model/IEEE Qcc not supported in Rel-16

## Slide 9
Bridge Management
S2-1901721 23.734 CR0011 (Rel-16, 'C'): Mapping of bridge port and QoS control in 5GS (Ericsson)
S2-1902010 23.501 CR1002 (Rel-16, 'B'): 5GS logical TSN bridge management (HUA)
S2-1902012 23.502 CR1097 (Rel-16, 'B'): System enhancement for TSN logical bridge management
S2-1901636 23.734 CR0007 (Rel-16, 'C'): TSN bridge Managed Objects (MO) collection for 5GS bridge (Vivo)

## Slide 10
Next steps agreed: Drafting session outcome
1. Architecture: Integration of 5GS with the TSN network:
Need one merged paper to handle 5GS integration. Consider Bridge management aspects independently. Revise S2-1902060 and merge architecture aspects from S2-1902009.
TSN Translator exists on both the sides (UPF/UE). TT is assumed to support de-jittering functionality, collocated with the UPF. All other functionalities of TT is still FFS, reference point between UPF/UE and TT is left open.
2. TSN Time Sync:
Update solutions #2/#3/#28 (e.g. how it works with QoS aspects) and strive for a decision SA2#132.
Agree that the time sync needs to be conveyed to the UE.
3. TSC QoS
Incoming LS from RAN2 – S2-1902723 - LS from RAN WG2: LS on assistance information for TSN traffic flows
Revise S2-1902061, used as a basis for QoS parameters, to be provided as TSN Assistance information (with reference to S2-1902723).
4. TSC deployment model and protocols supported
IEEE Qbv (protocol), Centralized model is supported in Rel-16; hybrid model is partially supported in Rel-16. Implication of partial support is FFS Distributed model/IEEE Qcc not supported in Rel-16. Capture this in a related CR to TS 23.501

## Slide 11
Way forward
Architecture (Integration of 5GS with the TSN bridge), QoS, Bridge management, deployment and other aspects –
  Progress CRs for TS 23.501/TS 23.502 for agreeable parts, add Editor’s notes or defer parts that are not agreeable
  For TSN QoS, we have CRs for TR 23.734 from Ericsson. Should convert them to CRs for TS 23.501/2 for agreeable parts during SA2#131.
TSN Time Synchronization –
  progress solution updates as CRs to the TR and strive to reach conclusion for TSN Time Sync (latest SA2#132).