## Slide 1: Discussion on EMC BS issue Azumi Matsusako, NTT DOCOMO
NG PACKET xx Doc abc
Restricted - Confidential Information
© GSM Association 2015
All GSMA meetings are conducted in full compliance with the GSMA’s anti-trust compliance policy

## Slide 2: Introduction
This discussion paper intends to:
  Explain the issue related to EMC BS
  Discuss the best way to avoid the problem
  Discuss if anything needs to be done in NG PRDs

## Slide 3: VoLTE Roaming and Emergency Call
There are operators (VPLMN) that deploy IMS Emergency Call for their domestic subscriber but CS Fallback Emergency Call for roaming users.
In this scenario, according to 3GPP and GSMA specification, “emergency bearer service indicator" (EMC BS) is expected to control Emergency Call domain.
However, NTT DOCOMO has observed and encountered (in our VoLTE roaming test phase) that there are other solutions that are based on EMC BS = 1, on the contrary to the above-mentioned specifications.
  And such solutions are not feasible.
This paper introduces such solutions, and proposes a way forward.

## Slide 4: What DOCOMO has observed/encountered (1)
As shown below, DOCOMO observed/encountered some alternative solutions for the UE to fall back to CS Emergency calls when the EMC BS is not relevant (e.g. EMC BS are indicated as supported while VPMN only supports CS Emergency calls) .
But any solutions are not feasible.
■Solution 1: PDN Connection Reject
MME
SGW
PGW
P-CSCF
E-UTRAN
GERAN/UTRAN
MSC/VLR
PSAP
VoLTE/IMS
UE
1. PDN Connectivity Request
(emergency)
2. PDN Connectivity Reject
3. UE falls back to 3G for EMC
3GPP | - Supported Rel-12 onwards - But it’s a optional feature
GSMA VoLTE | - No mention (i.e. follow 3GPP)
DOCOMO UE | - Most devices support this, but not universally supported
■Solution 1’: PDN Connection Timeout
MME
SGW
PGW
P-CSCF
E-UTRAN
GERAN/UTRAN
MSC/VLR
PSAP
VoLTE/IMS
UE
1. PDN Connectivity Request
(emergency)
2. PDN Connectivity Timeout
3. UE falls back to 3G for EMC
3GPP | - Supported Rel-12 onwards - But it’s a optional feature
GSMA VoLTE | - No mention (i.e. follow 3GPP)
DOCOMO UE | - As per our spec, it takes 40 seconds for DOCOMO UE to timeout - Most devices support CSFB after timeout, but not universally supported

## Slide 5
■Solution 3: INVITE Reject w/380
MME
SGW
PGW
P-CSCF
E-UTRAN
GERAN/UTRAN
MSC/VLR
PSAP
VoLTE/IMS
UE
4. UE falls back to 3G for EMC
2. Checks PLMN ID
3. SIP380
3GPP | - No mention (proprietary) for P-CSCF for PLMN ID check - 380  CSFB is described in TS23.167
GSMA VoLTE | - No mention (i.e. follow 3GPP)
DOCOMO UE | - INVITE does not necessarily have information that helps P-CSCF identify the operator ID (as a result, INVITE can go through without being rejected)
■Solution 4: Timeout → CSFB
MME
SGW
PGW
P-CSCF
E-UTRAN
GERAN/UTRAN
MSC/VLR
PSAP
VoLTE/IMS
UE
1. REGISTER or INVITE
2. Timer expires and UE falls back to 3G for EMC
3GPP | - No clear specification on SIP specs, except that UE is supposed to retry in CS domain when IMS EC fails (TS23.167)
GSMA VoLTE | - No mention (i.e. follow 3GPP)
DOCOMO UE | - Takes 2 minutes for IMS registration to timeout - UE performs INVITE after IMS registration timeout - Unclear if CSFB happens
1. INVITE
What DOCOMO has observed/encountered (2)

## Slide 6: Explanation of the issue related to EMC BS
When the EMC BS is not relevant, there are cases where Emergency calls can fail.
(e.g. A case the EMC BS indicated as supported without IMS infrastructure)
When the MME functionality to indicate the EMC BS based on subscriber is implementation specific, there is a case where the EMC BS cannot be indicated properly.
(e.g. IMS emergency procedures supported for domestic, not supported for
roaming users)
For the above reasons, it’s necessary to define about Emergency calls indicator in IR.88 and 3GPP more clearly. For 3GPP, it’s necessary to send them an Liaison Statement.