## Slide 1
3GPP TSG SA WG2#133
12 - 17 May 2019, Reno, USA
Source: | Samsung
Title: | Clarification on URSP in xBDT
Document for: | Discussion
Agenda Item: | 6.27
Work Item / Release | xBDT / Rel-16
Abstract of the contribution: This document proposed to clarify the UE operation with the location/time validity condition in URSP.
S2-1905396

## Slide 2: Introduction
Title: “Adding Support for Delivering Background Data Transfer Polices to the UE”
  Revision of CR0242 (S2-1904376)
Reason for Change
  During SA2#132 meeting, Route Selection Validation Criteria containing Time Window and Location Criteria has been agreed [S2-1904376]. In the CR, the following NOTE2 is ambiguous w.r.t. the UE operation
    NOTE 2: Once it is determined that the Location Criteria has been met, the location does not need to be checked again while the UE is in the Time Window.
  The intention is understood as follows:
    The URSP rule is evaluated and once the route selection (i.e., association of the traffic to the PDU session) is made, the change of UE location does not require the re-evaluation of the route selection.
    This condition does not preclude that the time window can be re-evaluated. It should be a new condition for the re-evaluation

## Slide 3: Proposed Text
Rephrase and relocate NOTE 2
  [FROM]
    NOTE 2: Once it is determined that the Location Criteria has been met, the location does not need to be checked again while the UE is in the Time Window.
  [TO]
    NOTE 2: Once the association of the application to the PDU Session is made, the change of UE location does not require the re-evaluation of the association.
Add a new re-valuation condition as follows:
  The UE may also re-evaluate the application to PDU Session association due to the following reasons:
    periodic re-evaluation based on UE implementation;
    an existing PDU Session that is used for routing traffic of an application based on a URSP rule is released.
    The expiration of Time Window in Route Selection Validation Criteria.