## Slide 1
3GPP TSG SA WG2#133
12 - 17 May 2019, Reno, USA
Source: | Samsung
Title: | Discussion on 5G-4G Interworking with UE policy
Document for: | Discussion
Agenda Item: | 7.1
Work Item / Release | Rel-17
Abstract of the contribution: This document discuss the problem and way forward for supporting 5G-4G interworking with traffic routing policies.
S2-1905422

## Slide 2: Introduction
Dedicated PDN/DN
Internet PDN/DN
Service 1
UPF-1/PGW-U-1
UPF-2/PGW-U-2
SMF/PGW-C
EPC
5GC
LTE-RAN
NG-RAN
DNN = dedicated.com
APN = dedicated.com
3GPP has introduced URSP for supporting operator controlled traffic routing in 5GS
URSP can be used to associate UE traffic (application, IP flow) with specific session/slice/etc
It is unclear how UE operators with the existing rel-15/16 solution(s), when the UE performs 4G-5G interworking, i.e., EPS to 5GS mobility (or visa versa)
Problematic Scenario (example)
  Operator wants to associate app #1 with DNN #A (e.g., dedicated.com)
  (Based on the coverage) UE may be attached to EPS firstly, and due to the lack of the proper policy in EPS, it associates app #1 with a default APN (i.e., internet)
  When the UE enters 5GS coverage, it can use URSP, and it associates app #1 with DNN #A as configured by URSP
  Session continuity of app #1 cannot be provided because of APN change during EPS to 5GS mobility

## Slide 3: Justification and Objectives
Justification
  In Rel-15, the behavior of UE supporting EPC interworking for URSP aspect is not defined
  Once the UE made an association between the UE application and the dedicated DNN in 5GC, the UE moves from 5GC to EPC, the UE may not support the service continuity due to lack of UE support of the relevant solution (e.g., URSP) in EPC.
  Once the UE made an association between the UE application and the internet APN in the EPC due to lack of UE support of URSP in EPC, the UE moves from the EPC to 5GC, the UE may re-evaluate the URSP and may not support service continuity.
Objective
  Support the interworking UE with EPC and 5GC for the traffic routing perspective where the operator wants to configure UE with routing rule for certain applications. The study may include the following aspects:
    Delivery of EPC-compliant part of URSP over user plane (e.g., similar to ANDSF)
    Service continuity of EPC-5GC interworking

## Slide 4: Proposal
It is proposed to study the problem/objective discussed in this paper in the UE policy study item in rel-17.
  There is on-going discussion on the rel-17 study item: the study on enhancement of UE policy