## Slide 1: UE Policy handling in EPS and 5GS interworking
Qualcomm Incorporated

## Slide 2: UE Policies available to the UE
What has been specified in Rel-15 (stage 2 & stage 3)
  EPS uses user plane OMA-DM to provision configuration parameters to UE, e.g. ANDSF rules. Other means including storing in USIM, or using implementation specific means.
  5GS allows C-plane provisioning of configuration of UE Policy (via PCF) only for:
      Access Network Discovery & Selection Policy (ANDSP); and
      UE Route Selection Policy (URSP)
  5GS still allows other configuration parameters via OMA-DM, e.g.:
      PS Data Off configurations;
      IMS MOs

## Slide 3: Interworking of EPS and 5GS policies in Rel-15
Principles specified already in TS 24.526
  For non-3GPP access node selection, always use ANDSP if available:
    When UE is registered to 5GCN via 3GPP access; or
    UE is registered to EPC via 3GPP access; or
    UE is not registered to any CN via 3GPP access
  For PDU session management, use URSP when:
    UE is registered to 5GCN via 3GPP access, but not registered via non-3GPP access; or
    UE is registered to 5GCN via both 3GPP and non-3GPP access
  For PDN connection management, use ANDSF and RAN rules, when:
    Registered to EPC via 3GPP access, and not registered via non-3GPP access; or
    Registered to EPC via both 3GPP and non-3GPP access;
  When UE is registered to 5GC via 3GPP access, and EPC via non-3GPP access
    Use ANDSF rules and RAN rules for traffic goes via ePDG
    Use URSP for all other traffic
  When UE is registered to EPC via 3GPP access, and 5GC via non-3GPP access
    Use URSP only for traffic goes via N3IWF
    Use ANDSF rules and RAN rules for all other traffic
5GC
UE
3GPP access
Non-3GPP access
URSP
EPC
ePDG
ANDSF rule
ANDSP
EPC
UE
3GPP access
Non-3GPP access
ANDSF rule
5GC
N3IWF
URSP
ANDSP

## Slide 4: Reasons for the design in Rel-15
Use URSP for traffic to 5GC, and ANDSF rules for traffic to EPC
  Per TS 23.503 definition, the URSP rules (the RSDs) defines parameters that are 5GC specific:
        Ethernet PDU, Unstructured PDU session type;
        SSC modes
        Network Slice selection
  The other parameters cannot be used in EPS, e.g. DNN cannot be used without considering S-NSSAI.
Route selection components | This part defines the route selection components | Mandatory (NOTE 2) |  | 
SSC Mode Selection | One single value of SSC mode. | Optional | Yes | UE context
Network Slice Selection | Either a single value or a list of values of S-NSSAI(s). | Optional | Yes | UE context
DNN Selection | Either a single value or a list of values of DNN(s). | Optional | Yes | UE context
PDU Session Type Selection | One single value of PDU Session Type | Optional | Yes | UE context
Non-seamless Offload indication | Indicates if the traffic of the matching application is to be offloaded to non-3GPP access outside of a PDU Session. | Optional (NOTE 3) | Yes | UE context
Access Type preference | Indicates the preferred Access Type (3GPP or non-3GPP) when the UE establishes a PDU Session for the matching application. | Optional | Yes | UE context

## Slide 5: Reasons for the design in Rel-15
ANDSP has been designed to be applicable to both EPC and 5GC
  ANDSP for 5GS contains a superset of WLANSP rules in ANDSF for EPS and other info for 5GS use:
        parameters that can be included in WLANSP rules in ANDSP is the same as that which can be included in WLANSP rules in ANDSF for EPS
        ANDSP contains information for both N3IWF and ePDG selection
  ANDSP should be always used for non-3GPP node selection when available, to allow UE select the best node (either for ePDG or N3IWF)
Information name | Description | Category | PCF permitted to modify in a UE context | Scope
WLANSP rules | 1 or more WLANSP rules as specified in 4.8.2.1.6 of TS 23.402 [9] | Mandatory | Yes | UE context
ePDG identifier configuration | The UE uses this information to select ePDG as defined in clause 6.3.6.1 of TS 23.501 [2] | Optional | Yes | UE context
N3IWF identifier configuration | The UE uses this information to select N3IWF as defined in clause 6.3.6.1 of TS 23.501 [2] | Optional | Yes | UE context
Non-3GPP access node (N3AN) selection information | The UE uses this information to select ePDG or N3IWF as defined in clause 6.3.6.1 of TS 23.501 [2] | Optional | Yes | UE context

## Slide 6: Conclusions
Rel-15 UE Policy design already allows proper interworking
  With Rel-15 design, the UE could already properly operate under either EPS or 5GS
  For URSP, it cannot be directly used/mapped to parameters to be used in EPS
  A properly drafted ANDSF rule set will provide an easier way to have consistent control in EPS
    Changing URSP or UE behavior to allow its use in EPS would bring complexity for stable 5GS operation, and may break URSP design (that is already complicated).