## Slide 1
3GPP TSG-SA WG2 Meeting #134
S2- 1907070 Sapporo, Japan, 24 - 28 June, 2019 Source: Ericsson , AT&T
Title: Support for IAB in CN
Document for: Agreement
Agenda Item: 6.29
Work Item / Release: TEI16/Release 16
Abstract of the contribution: This document provides an analysis of IAB for overall architecture and concludes on technical direction and agreement for the normative work.

## Slide 2: Background Integrated Access and Backhaul (IAB)
3GPP Study Item on Integrated Access and Backhaul (IAB) completed at RAN#2 in December (3GPP TR 38.874)
At the same meeting a WI was agreed (RP-182882) with target completion December 2019
Objectives and requirements:
Specify support for NR based wireless self-backhauled base stations (called IAB nodes)
Support for
  Multi-hop (> 1 hop)
  Topology adaptivity incl. redundant connectivity
  QoS enforcement of backhaul traffic
  Inband and outband relaying using any bands
  Wireless backhaul using either EN-DC with EPC and SA-mode with 5GC
    In both cases the backhaul user plane will be over NR only
  Legacy Rel-15 UEs

## Slide 3: Overview / Terminology
IAB-node:
An NR base station terminating the gNB-DU functionality towards the UEs (access link) and towards gNB-CU
IAB node also support a sub-set of the UE functionality towards its parent nodes and CN (referred to as MT functionality)
IAB-donor:
An NR base station which terminates gNB-CU functionality towards IAB-node and N2/Xn interfaces towards rest of the network.
The IAB-donor is also terminating RRC/PDCP of the MT functionality of the IAB node as well as lower layers (donor DU) in case of single hop.

## Slide 4: IAB architecture and protocols
  The IAB node terminate the full F1 interface towards the donor gNB-CU including (F1-AP/SCTP/IP and GTP/UDP/IP)
  The donor gNB-DU provide a “routing” functionality for the IAB node, meaning it forwards any IP packets addressed to the IP address of the IAB node
    An adaptation layer called BAP handles the internal forwarding within the IAB network

## Slide 5: QoS enforcement on wireless backhaul link
The Donor IAB (CU function) will setup a number of BH RLC channels between the IAB node and the IAB nodes parent (e.g. an intermediate IAB node or the Donor DU)
The BH RLC channels will not be visible in the CN
The BH RLC channels will be associated with different QoS profiles and support backhauling of end user traffic and signaling towards the IAB node.
Both aggregated mapping (of UE bearers with similar QoS) (left) and 1:1 mapping (right) between end user DRBs and BH RLC channels will be supported.

## Slide 6: Support both for SA NR and EN-DC
In addition to SA NR, it has been agreed that IAB should also be supported using EN-DC to setup the backhaul link.
In this case the IAB node will initially connected to LTE/EPC and then the LTE side will trigger the setup of the NR link.
Once the NR link is up and running this link will be used for IAB data traffic.
The LTE link may still be supported for control signaling.

## Slide 7: Current RAN3 agreement impacting the CN
It has been agreed that the CN should indicate to the RAN that the IAB node has been authorized as an IAB node. This has been captured in R3-192619 and R3-192622 for EPC and 5GC.
It has also been agreed that the IAB node will initially connect to the network as a UE (i.e. using NAS registration). The IAB node will then perform authentication to the CN. This has been captured in in R3-193176.
At last RAN3 meeting it was also agreed that RAN node should send an IAB node indication to CN in INITIAL UE MESSAGE (details FFS).

## Slide 8: Analysis of impacts on 5GC and EPC to support IAB nodes
Assumptions:
The CN will receive an indication from RAN in the initial message that the UE is an IAB node
The CN should verify that the IAB has the right to access as an IAB node
Once verified the CN should setup the “UE” context in the RAN and indicated to the RAN that the IAB node authorized as an IAB node
Features:
Since the user plane backhaul for IAB nodes is setup locally in the RAN, it is not required to setup any PDU session / PDN connections in the CN for user plane backhaul.
  This is different from LTE Rel-10 relaying where the backhaul bearers was managed by the CN.
  IAB node is allowed to setup UP resources in the CN for other purposes (e.g. for OAM connectivity)
IAB nodes are expected to always be CONNECTED (always on), meaning there is no requirements in Rel-16 to support IAB nodes “camping” in IDLE state.
IAB nodes are network nodes fully under operator control, connecting to the operators internal network and do not require support for roaming.

## Slide 9: Proposals

## Slide 10: Needed functionality in CN to support IAB nodes
It is proposed that the following functionality should be specified for supporting IAB nodes in the CN:
Mechanism to support authentication and authorization of IAB nodes in the CN. Including:
  Mechanism to verify the IAB node based on subscription information and authorize the use of the IAB functionality.
  Mechanism to determine that the IAB node wants to become active as an IAB and a mechanism to inform RAN that the IAB node is authorized.
Mechanism in RAN and CN to allow AMF selection based on IAB support.

## Slide 11: Proposals for supporting the functionality on earlier slide (1/2)
Proposal 1: Existing UE authentication methods defined in Rel-15 should be reused as is for IAB nodes to minimize standardization and network impact.
Proposal 2: Both USIM based methods and any EAP based methods (as described in 33.501). For EAP based methods it should be allowed to use NAI based SUPIs.
Proposal 3: A subscription parameter indicating IAB node should be added to UDM/HSS signaling.
Proposal 1 and 2 are depended on SA3

## Slide 12: Proposals for supporting the functionality on earlier slide (2/2)
Proposal 4: The IAB should indicate on RRC level (e.g. RRCSetupComplete) that it is an IAB node and the RAN will if it support IAB nodes include this indication in the Initial UE message (as per existing RAN3 agreement).
Proposal 5: The CN will when it has verified the IAB node include an “IAB node authorized” IE in the Initial Context Setup/Modification to the RAN (as per existing RAN3 agreement).
Proposal 6: The AMF/MME should during NG/S1 setup indicate that it supports IAB nodes, making it possible for the RAN to select an AMF/MME that support IAB nodes.

## Slide 13: Endorsement
Supporting companies propose to endorse Proposals in slides 10-12 as the basis for normative stage 2 specification development.