## Slide 1: Candidate way forward option to delegated discovery
Huawei
SA WG2 Meeting #134 S2-1908045
Sapporo, Japan, 24 - 28 June 2019

## Slide 2: Option A (Original Working Agreement)
SMF selection:
1. AMF does not use delegated discovery in HR roaming, or if the PLMN is configured to support ETSUN.
PCF selection:
2. In the roaming case, delegated discovery and selection is not used for UE policy association establishment procedure.

## Slide 3: Option B (Huawei, Ericsson)
SMF selection:
AMF sends the service request to the SCP with the related selected parameters(UE location as preferred parameter).
SCP do the H-SMF discovery/selection and returned the related the selected NF profile.
AMF check whether the service area cover the UE location.
AMF use the selected H-SMF/SMF ID and re-initiate the service request.
PCF selection
Always the AM association established first.
UE policy association establishment :
  If the SCP allow to change the message, the H-PCF discovery and association establishment will be done at the same time.
  Otherwise, the H-PCF ID is to be selected first. After that, the association is to be established.

## Slide 4
AMF
1. Request (selection and discovery parameters for H-SMF)
4. Request
6. Response
3. Error Response (insert H-SMF ID)
2. Discovery of H-SMF
Option B----SMF selection
SCP
V-SMF
8. Request
7. Response
SCP
H-SMF
5. Request
9. Request
10. Response

## Slide 5: Option C (NTT Docomo,Oracle)
SMF selection:
V/I-SMF, PCF is required to support delegated discovery and registered to the NRF.
  ETSUN:
  AMF send all parameter to SCP and SCP try to discovery the SMF match all condition if possible .
  If the SMF can not find, the AMF try to populate parameter for the I-SMF support the delegated discovery.
    If the I-SMF support the delegated discovery can be found, then SCP select the I-SMF. After that I-SMF generate a new discovery/selection parameter for SMF selection.
    If the I-SMF support the delegated discovery can not be found, the SCP return error to AMF. AMF do the direct discovery to find the SMF.
  HR roaming case :
  The AMF start from step 2 above (red colour).
PCF selection:
Always the AM association established first.
UE policy association establishment :
  The AMF start from the step 2 above(red color)

## Slide 6
AMF
1. Request (selection and discovery parameters for H-SMF)
4. Request(delegated discovery )
3.1. Request
3.2. Error Response
2. Discovery of SMF match all parameter?
Option C----SMF selection
SCP
V-SMF
6.4 . Request
6.2 Error Response
SCP
H-SMF
Y
6.5. Request
7.1 Request
Y
5. Delegated DS suported NF found ?
6.3. A new dscovery paramter generation
6.1. Request
7.2 Request

## Slide 7: Proposed way forward
Option A is preferred to be adopted in this release, simple and give more room for further improvement.
If not some principle need be checked first,
  SMF selection logic should not be added to the V/I-SMF ?