## Slide 1
Huawei
Discussion paper on further support of location information for UE behind 5G-RG via wireline access

## Slide 2: (1) Background
Current specification about location information when UE behind 5G-RG connected via W-5GAN:
Architecture that UE behind 5G-RG via W-5GAN,
5G-RG act as TNAP in the architecture!
In this case, TNAP ID, i.e.5G-RG ID, is regarded as the location information for UE behind 5G-RG.

## Slide 3: (2) Problem
There is problem if TNAP ID is only used as location information:
E.g. TNAP(i.e. 5G-RG in this case) is moved from your home to your neighbor’s home, the TNAP ID is unchanged, but the location do change. As a result, the network may get a incorrect location information.
Proposal:
For W-5GBAN, Line ID, which is static and more accurate, can be used as the location information in this specific scenario.
Similarly, for W-5GCAN, HFC node ID can be used as the location information in this specific scenario.

## Slide 4: (3) Proposed Solution
The idea is:
Step 1: During 5G-RG Registration procedure, W-AGF located in W-5GAN provide the Line ID to 5G-RG, i.e. TNAP;
Step 2: During UE Registration procedure, 5G-RG(i.e. TNAP) provide Line ID to TNGF via AAA interface and TNGF provide the Line ID to AMF for UE.
As a result, AMF regard the Line ID as the location for UE.
Take W-5GBAN as example,

## Slide 5: Annexes