## Slide 1: V2X Uu Alternative QoS Profiles: Notes on Tuesday lunchtime drafting session on open issues. Red text reflects the outcome of the discussion on that issue.
Document for discussion
Source: Vodafone (Convenor – Chris Pudney)
SA WG2 Meeting #135 Oct 14-18, 2019, Split, Croatia
Agenda item: 7.1, eV2XARC
Tdoc S2-1910006

## Slide 2: Points to agree or disagree or answer (1)
The 5GC may provide the NG-RAN with a set of QoS profiles for a GFBR flow with Notification Control.
yes
(how the “set” is encoded is for stage 3 work) A new, unanswered question is whether the set can contain profiles with different QFIs.
The 5G Core indicates its preference order for the profiles in the set. yes
The NG-RAN continuously attempts to deliver a more preferred QoS profile. yes

## Slide 3: Points to agree or disagree or answer (2)
Whenever the NG-RAN selects a better or worse QoS profile, the NG-RAN sends a Notification to the Core Network that indicates the new QoS Profile. Yes (some wordsmithing of the above point is requested by some companies)
Upon sending this Notification, the NG-RAN shall start to deliver the QoS of the QoS Profile indicated in the notification. yes
If the NG-RAN sends a Notification with both a reference to an Alt QoS Profile AND a GBR/PDB/PER, which of these two is it now delivering? Wrong understanding. Instead, in the Notification, the NG-RAN sends EITHER a reference to an Alt QoS Profile OR the GDB/PDB/PER that can be supported.

## Slide 4: Points to agree or disagree or answer (3)
If the NG-RAN is unable to even deliver the least preferred Alternative QoS Profile, then the NG-RAN sends a Notification to the 5GC indicating this situation No decision yet. This may depend on details of the solution (e.g. if an Alt QoS of 0 bit/s is allowed or not.)
The NG-RAN is expected to apply some hysteresis to changes of Alternative QoS Profiles Hysteresis only for upgrade: downgrade is done promptly. Sensible hysteresis can avoid undue signalling load on the CN.

## Slide 5: Points to agree or disagree or answer (4)
The UE shall be informed about changes in the GBR Yes. (No immediate conclusion reached about informing the UE of changes in MBR & 5QI)
Does the UE need to be informed at the 3GPP layer (e.g. why does the existing NAS carry GBR? Are there requirements in 5GS caused by the multiplexing of multiple flows onto one Data Radio bearer?) - The UE uses the signalled MBR for data rate enforcement in non 3GPP. -> compromise achieved: agree to have 3GPP signalling of the new QoS profile to UE -> agree tentatively to go with NAS signalling rather than RRC/RLC/MAC as R15 NAS ought to avoid UE impacts. -> agree to use Downlink NAS Transport to signal to the UE and NOT N2/N1 PDU Session Modification procedure. (Hence the RAN keeps the original “Requested QoS Profile”, and the Alternative QoS Profiles should all be ‘less preferred’ than the Requested QoS Profile)
The above compromise meant that points 11 and 12 below did not need to be discussed.
Can we mandate that the Application Function informs the UE via User Plane Data (on a default flow)?
Do we prohibit the SMF from triggering N2 session modification carrying N1 signalling with new GBR to the UE?

## Slide 6: The convenor summarised the main remaining contentious topics as below and invited discussion to continue on one of the 3GPP SA2 email reflectors: a) the questions related to Alt QoS Profile of 0 bit/s or other mechanisms for fully congested RAN node b) initial flow Admission control c) operation with RAN that is not 100% supporting Alternative QoS. The session ended at 14:00.

## Slide 7: Points to agree or disagree or answer (5)
At Xn/N2 handover, the target RAN node shall be informed of the ordered list of QoS Profiles by the source RAN node.
Depending on radio conditions, the Target RAN Node may change to a worse alternative QoS profile from the Set of QoS profiles…
…or the Target RAN node may change to a better QoS Profile….
if the handover is completed and the QoS Profile is changed, then the NG-RAN informs the 5GC of the new QoS Profile along with (for Xn handover) the Path Switch Request or (for N2 handover), the Handover Notify.
FFS (see later points on admission control) whether these handover messages are extended or a Notification message is sent immediately after they are sent

## Slide 8: Points to agree or disagree or answer (6)
At X2/N2 handover, if the Target NG-RAN node is unable to even deliver the least preferred QoS Profile, release of the GBR flow is undesirable as it is difficult for the CN to re-establish it in a congested RAN node.
How to avoid GFBR release in a congested cell? E.g. an alternative QoS profile of 0 bit/s, or, the target RAN notifies that it can only guarantee 0 kbit/s (with x PDB and y PER), or ???

## Slide 9: Points to agree or disagree or answer (7)
At initial establishment of the GFBR flow, the 5GC shall be able to request that the establishment is queued in a congested NG-RAN
How to do the above request? Use a least preferred Alternative QoS Profile of 0kbit/s, or a new “queuing indication”, or ??
At initial establishment of the GFBR flow, the use of an acknowledgement promptly followed by a notification of a change of QoS Profile is undesirable as the initial acknowledgement can trigger actions that assume the most preferred QoS profile is being fulfilled.
Hence, at initial establishment of the GFBR, the NG-RAN shall use a single message to acknowledge the establishment of the flow AND the QoS Profile that is now in use.

## Slide 10: Points to agree or disagree or answer (8)
At least due to RAN sharing, (and also due to roaming) ensuring that 100% of RAN nodes support a feature in a wide area (e.g. as used by Automotive) is not practical.
A solution is needed to re-enable alternative QoS profile handling after handover from a non-supporting RAN node to a supporting NG-RAN node.
.

## Slide 11
7.1 | S2-1909266 | CR | Approval | 23.501 CR1785 (Rel-16, 'F'): Corrections to handling of Alternative QoS Profiles | Huawei, HiSilicon | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909595 | CR | Approval | 23.501 CR1855 (Rel-16, 'F'): Clarification to handling of Alternative QoS profiles | Ericsson | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909681 | CR | Approval | 23.501 CR1874 (Rel-16, 'F'): Alternative QoS Handling during handover | Samsung | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909688 | CR | Approval | 23.502 CR1844 (Rel-16, 'F'): Alternative QoS Handling support | Samsung | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909268 | CR | Approval | 23.501 CR1786 (Rel-16, 'B'): Handling of Alternative QoS Profilesd at handover | Huawei, HiSilicon | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909593 | CR | Approval | 23.501 CR1854 (Rel-16, 'F'): Managament of GBR QoS Flows at handover | Ericsson | Rel-16 | 5G_URLLC |  | Open
7.1 | S2-1909869 | CR | Approval | 23.501 CR1911 (Rel-16, 'F'): Alternative QoS Profile Handling for V2X Communication Over Uu Reference Point | Vodafone | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909580 | CR | Approval | 23.501 CR1851 (Rel-16, 'C'): Signalling the QoS Flow level QoS parameters of the Alternative QoS profile to UE | Qualcomm Incorporated | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909048 | CR | Approval | 23.503 CR0323 (Rel-16, 'F'): Enhancements to QoS Handling for V2X Communication Over Uu Reference Point | Ericsson | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909267 | CR | Approval | 23.503 CR0331 (Rel-16, 'F'): Corrections to handling of Alternative QoS Profiles | Huawei, HiSilicon | Rel-16 | eV2XARC |  | Open
7.1 | S2-1909526 | CR | Approval | 23.503 CR0337 (Rel-16, 'F'): Notification to AF on the Alternative QoS | Nokia, Nokia Shanghai Bell | Rel-16 | eV2XARC |  | Open