## Slide 1
Discussions on UP firewalling (“UP gateway” or IPUPS”) on Inter PLMN N9
S2-2000474
S2-2000474

## Slide 2
Discussions on UP firewalling (“UP gateway” or IPUPS”) on Inter PLMN N9
Discussions un-conclusive
SA3 view
Initial SA2 view
S2-1910799 23.501 CR1848 (Rel-16, 'F'): Introduction of the Inter PLMN UP functionality in the architecture Agreed in SA2 135;
S2-2000474
S2-2000474

## Slide 3
Dedicated IPUPS acting as GTP-u switch or as GTP-u pass-through?
If IPUPS is transparently added in the path)
  The UPF sends traffic targeting (F-TEID) the remote UPF
  All IPUPS need to be configured when a new PDU Session is created / released (modified?)
  If stateful IPUPS is needed, IP routing capabilities (on both side of the IPUPS(s)) need to ensure that the same IPUPS handles the traffic of a PDU Session
SMF
UPF
IPUPS 3
Remote UPF
IPUPS 1
IPUPS 2
N4
IP
IP
N4
Local PLMN
S2-2000474

## Slide 4
Dedicated IPUPS acting as GTP-u switch or as GTP-u pass-through?
If IPUPS is GTP-u switch, the remote UPF sends traffic targeting (F-TEID) one IPUPS that is controlled to modify the target F-TEID to target the local UPF
  All traffic of the PDU Session go via the same IPUPS which can have stateful FW capabilities
SMF
UPF
IPUPS 3
Remote UPF
IPUPS 1
IPUPS 2
N4
IP
IP
N4
Local PLMN
S2-2000474