## Slide 1: 5G CIoT MT-EDT Discussion
Source: Qualcomm Incorporated
3GPP TSG SA2 Meeting #137E S2-2002014
Elbonia, February 24 – 27, 2020

## Slide 2: Background
MT-EDT has been introduced to EPC CIoT (NB-IoT/WB-EUTRAN connected to EPC).
  Provides power & signaling reduction mechanism
  Particularly useful for one DL data packet.
However, this feature was not agreed for 5G CIoT.
  One particular difference with EPC is the requirement for 5G GUTI reallocation.
  This requires further optimization compared to EPC to avoid additional signalling
Qualcomm View:
  5G CIoT features should be a superset or at the very least achieve feature parity with EPC CIoT.
  5G CIoT should provide at least equal or even better performance than EPC CIoT, particularly in battery life and signalling reduction performance.
    Other important performance parameters like coverage, capacity, and reduced complexity are implicitly by reusing NB-IoT/eMTC.
  5G CIoT shall provide an MT-EDT solution comparable to EPC CIoT.

## Slide 3: 5G GUTI Reallocation Requirement in 5GS
SA3 requirement:
  The AMF shall send a new 5G-GUTI to the UE after receiving Service Request message sent by the UE in response to a Paging message.
  This requires AMF to initiate UE Configuration Update procedure to allocate a new 5G GUTI.
  From S3-193838 (From SA3 to CT1)
    CT1 Question to SA3: CT1 kindly asks SA3 to confirm whether the allocation of a new 5G-GUTI will still be required for MT EDT for CP CIoT 5GS optimization and UP CIoT 5GS optimization.
    SA3 Response: User privacy protection is one of the main enhancements made in 5GS to address the privacy issues raised by the research community. SA3 confirm that the allocation of a new 5G-GUTI is required for MT EDT for CP CIoT 5GS optimization and UP CIoT 5GS optimization.
Observations:
  The 5G requirement of 5G GUTI allocation at every Network initiated service request procedure from CM IDLE state, increases signalling overhead and power consumption for 5G CIoT MT data compared to EPC CIoT MT data
  This issue is general for 5G CIoT, and it is not introduced by 5G MT-EDT.

## Slide 4: 5G CIoT inefficiency due to 5G reallocation
Consider Control Plane CIoT 5GS optimization used for one DL message initiated when the UE is in CM-IDLE.
Then the following steps occur when the UE receives the paging message
  RRC connection establishment is completed, UE in RRC connected. (4 messages)
  UE responds with service request message (1 message)
  AMF sends DL NAS transport with data (1 message)
  AMF also sends UE Configuration Update for GUTI reallocation (1 message)
  UE responds to UE Configuration Update response (1 message)
  AMF releases N2 connection / RAN releases RRC connection (1 message)
The CP CIoT 5GS optimization procedure requires 9 over-the-air messages to send only one DL data packet

## Slide 5: MT EDT proposal for CP CIoT optimization
Key steps:
  Step 7:
    AMF allocates a new 5G-GUTI and transmits along with NAS data PDU within the NAS Service Accept message.
    The AMF considers both the new 5G-GUTI and the old 5G-GUTI valid until any subsequent UE NAS signalling using the new 5G-GUTI, in which case the AMF considers the old 5G-GUTI invalid.
    If AMF does not expect any other data or signalling with the UE, the AMF sends the DL N2 message by including the DL data and End Indication to indicate that no further data or signalling is expected with UE.
  Step 8:
    The NAS container is included in RRC message sent to the UE. If the RRC Early data message is received in step 8, UE will store the new 5G-GUTI without send NAS response message.
  Step 8b:
    If the RAN node cannot delivery the NAS PDU containing service accept message with 5G-GUTI, the RAN node shall send N2 NAS Non Delivery Indication message to AMF.

## Slide 6: AMF 5G GUTI handling and paging behavior
The UE does not provide any ACK at NAS layer to Service Accept with new 5G GUTI.
  Therefore the AMF needs to still keep the old 5G GUTI as valid, until considered expired.
    i.e. until the AMF receives NAS signaling from UE with new 5G GUTI.
  Note:
    AMF handling 2 5G GUTIs and trying to page using both is not a new behavior in the AMF. (See Annex)
One potential issue is how to minimize the chances of AMF using a different 5G S-TMSI for paging than what the UE is using.
  E.g. the AMF is using new 5G S-TMSI for paging (before trying old 5G-S-TMSI) but the UE never received the new 5G GUTI and is using the old 5G S-TMSI.
QC proposal:
  Leverage the indication of NAS Non-delivery Indication as defined in TS 38.413, clause 8.6.4.
  Using the indication the AMF will (except extreme rare cases) page with the same 5G S-TMSI the UE is using with the paging behavior described in next slide.

## Slide 7: AMF paging behavior after GUTI reallocation in MT-EDT
If the AMF previously assigned a new 5G-GUTI during MT-EDT, the AMF did not receive a N2 NAS Non Delivery Indication from NG-RAN and the old GUTI is still considered valid, the AMF may proceed with the following paging strategy:
  The AMF uses the new 5G-S-TMSI from the new 5G-GUTI for paging for an implementation dependent number of paging attempts.
    NOTE: Since the AMF did not receive NAS Non Delivery it knows with extremely high probability that the UE did receive the new 5G GUTI.
If the AMF previously attempted to assign a new 5G-GUTI during MT-EDT, but the AMF received a N2 NAS Non Delivery Indication from NG-RAN, the AMF follows the behaviour for lower layer failure when attempting to assign a new 5G GUTI as defined in TS 24.501 (see Annex).
  I.e. the AMF tries old 5G-S-TMSI first.

## Slide 8: 5G MT-EDT for CP optimization performance
Control Plane CIoT 5GS optimization with MT-EDT for one DL message initiated when the UE is in CM-IDLE:
Then the following steps occur when the UE receives the paging message
    UE responds with service request (3 message)
    AMF sends NAS message with data and GUTI reallocation in N2 release message
    RAN sends RRC release message with NAS message (GUTI reallocation,data) (1 message)
The proposed procedure requires only 4 over-the-air messages to send one DL data packet using MT EDT for CP CIoT 5GS optimization procedure. This is a reduction of 5 over-the-air messages compared to the case with no optimization.

## Slide 9: MT-EDT for UP optimization
Key steps:
  Step 5:
    Based upon the received DL packet size NG-RAN determines whether to initiate MT-EDT transmission as defined in TS 38.300 [9]. The NG-RAN sends the paging message to the UE with an MT-EDT indication.
    After the UE receives a paging with MT-EDT indication, UE initiates the MO EDT procedure for UP optimization.
  Step 9:
    AMF allocates a new 5G-GUTI which is encapsulated in a NAS container included in N2 Resume response message.
    The AMF considers both the new 5G-GUTI and the old 5G-GUTI valid.
  Step 10:
    The NAS container is included in RRC message sent to UE. If the RRC release message is received in step 10, UE will store the new 5G-GUTI without sending NAS response message.
  Step 10b:
    If the RAN node cannot delivery the NAS PDU containing service accept message with 5G-GUTI, the RAN node shall send N2 NAS Non Delivery Indication message to AMF.

## Slide 10: Annex
AMF current behavior when handling old and new 5G GUTI

## Slide 11: AMF 5G GUTI handling and paging behavior (1)
From 24.501, the error case for UCU with GUTI reallocation:
  b) Lower layer failure.
    If a lower layer failure is detected before the CONFIGURATION UPDATE COMPLETE message is received and:
      1) if the CONFIGURATION UPDATE COMMAND message includes the 5G-GUTI IE, the old and the new 5G-GUTI shall be considered as valid until the old 5G-GUTI can be considered as invalid by the AMF. If a new TAI list was provided in the CONFIGURATION UPDATE COMMAND message, the old and new TAI list shall also be considered as valid until the old TAI list can be considered as invalid by the AMF.
      During this period the AMF:
      i) may first use the old 5G-S-TMSI from the old 5G-GUTI for paging within the area defined by the old TAI list for an implementation dependent number of paging attempts for network originated transactions. If a new TAI list was provided with old 5G-GUTI in the CONFIGURATION UPDATE COMMAND message, the new TAI list should also be used for paging. Upon response from the UE, the AMF may re-initiate the CONFIGURATION UPDATE COMMAND. If the response is received from a tracking area within the old and new TAI list, the network shall re-initiate the CONFIGURATION UPDATE COMMAND message. If no response is received to the paging attempts, the network may use the new 5G-S-TMSI from the new 5G-GUTI for paging for an implementation dependent number of paging attempts. In this case, if a new TAI list was provided with new 5G-GUTI in the CONFIGURATION UPDATE COMMAND message, the new TAI list shall be used instead of the old TAI list. Upon response from the UE the AMF shall consider the new 5G-GUTI as valid and the old 5G-GUTI as invalid.
      ii) shall consider the new 5G-GUTI as valid if it is used by the UE and, additionally, the new TAI list as valid if it was provided with this 5G-GUTI in the CONFIGURATION UPDATE COMMAND message; and

## Slide 12: AMF 5G GUTI handling and paging behavior (2)
Difference between current error case handling and new AMF behavior for MT-EDT.
  For current error case, AMF tries old S-TMSI first.
    The reason is this occurred due to lower layer failure so it’s likely the new GUTI never made it to the UE.
  For MT-EDT with GUTI reallocation, AMF tries new S-TMSI first by default.
    The reason is most of the time the UE would receive the new GUTI, i.e. most of the time MT-EDT procedure would be completed successfully. Furthermore if there is an issue with delivering service accept, the RAN node would send NAS non-delivery indication.
    If the AMF does receive NAS non-delivery, then AMF behavior the AMF tries old S-TMSI. Note that since the AMF knows the new 5G GUTI was not delivered, it doesn’t even try it for paging.