## Slide 1
SA WG2 Meeting #137E (e-meeting) S2-2002042
Feb 24 - 27, 2020, Elbonia
Nokia, Nokia Shanghai Bell
Support of different slices over different Non 3GPP access

## Slide 2
N3GPP access and (slicing, ETSUN)
Per Current 3GPP specifications,
the AMF receives from the 5G AN (in N3GPP case: N3IWF / TNGF / W-AGF) information on the slices (S-NSSAI) supported by the 5G AN TA(s). This is done as part of NG set up request (38.413) § 9.2.6.1
all the 5G AN (N3IWF / TNGF / W-AGF) correspond to the same unique TA
This mean that support of slices has to be homogeneous between N3IWF/TNGF ((Un)trusted Non 3GPP access) and wireline access (W-AGF) as well as between different wireline AN of a PLMN;
This looks an un-necessary restriction
>Supported TA Item |  | 1..<maxnoofTACs> |  |  | - | 
>>TAC | M |  | 9.3.3.10 | Broadcast TAC | - | 
[….] |  |  |  |  | - | 
>>>>TAI Slice Support List | M |  | Slice Support List 9.3.1.17 | Supported S-NSSAIs per TA. | - | 

## Slide 3: Proposed solution and remarks
Support the possibility for operators to allocate a TAI per non 3GPP 5G AN (e.g. N3IWF / TNGF / W-AGF) : each non 3GPP 5G AN is locally configured with its own TAI whose value is provided (as in case of 3GPP access) to AMF over NGAP/N2 in NG SET UP message.
Different non 3GPP 5G AN (e.g. different N3IWF / TNGF / W-AGF) can thus advertise different TAI values.
Then the same algorithm than in case of 3GPP access can apply for the determination of the supported S-NSSAI over Non 3GPP access
Does it require extra standard work for 5G AN, AMF and SMF?
  SMF shall not determine access type so shall be transparent on whether there are multiple TAI for N3GPP coverage in a PLMN
  Passing the TAI supported by a 5G AN is a baseline R15 feature (neither protocol work nor even RAN3 is needed)
  Passing the slice supported by a 5G AN in a TA is a baseline R15 feature (neither protocol work nor even RAN3 is needed)
  AMF is to determine Access Type / RAT Type based on 5G AN node Id type, not based on a constant TAI value (see CR agreed in Incheon)

## Slide 4: Proposal for endorsement
..
It is proposed to endorse a TEI17 per the WID and draft CR submitted