Pre SA2#138E e-meeting Email Discussion

Source: 	<TBD>

Title: 	Email Discussion on Non-homogeneous support for ATSSS in Rel-16

# 1.	Non-homogeneous support for ATSSS in Rel-16

## 1.x	Non-homogeneous support for ATSSS in Rel-16

### 1.x.1	Description

ATSSS in Rel-16 is an optional feature.  During the inter-PLMN roaming scenario, it is possible that the two access legs which are hosted by different PLMNs may not BOTH support ATSSS.  When such scenario arises, the non-ATSSS capable AMF will not recognize the UE’s ATSSS capability to select the ATSSS capable SMF to support the MA PDU Session establishment.

After many weeks of online and offline discussions, a tentative agreement has been reached to address this issue in Rel-16 based on the following solution principles as proposed by Ericsson in Proposal#3 in the presentation (ftp://www.3gpp.org/Email_Discussions/SA2/ATSSS%20Non-homogenous%20Support%20-%20Mar.%2013th%202020.ppt): i.e.

(1) During the UE registration, the serving AMF will inform the UE with network capability indicator for the support of ATSSS, if supported, and

(2) During the N2 mobility handover, following the similar procedures as in ETSUN for the handling of incompatible source and destination network capability support, the MA PDU session will be released accordingly (further technical details will be captured in the CRs to be submitted to SA2#138e eMeeting).

### 1.x.2	Companies View

Question: Should the support of non-homogeous support for ATSSS based on the solution principles as described in (1) & (2) above based on the Proposal#3 in the presentation?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |

### 1.x.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.x.4	Porposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.