Pre SA2#138E e-meeting Email Discussion

Source: 	FS_5G_ProSe Rapporteur (CATT)

Title: 	Email Discussion on FS_5G_ProSe SID Scope

# 1.	Issues for FS_5G_ProSe

## 1.1	Service continuity for UE-to-Network Relay

### 1.1.1	Description

As part of Rel-17 prioritization by SA#86 (Dec 2019) the scope of 5G Proximity Services study (FS_5G_ProSe) was reduced by removing the work task on “path switch”, which led to different interpretations. Please see work Task paper (SP-191371) for more details.

Some companies understand that what was deprioritised is only the “path switch” of a UE-UE connection between direct path and network-based path. Other companies understand that, in addition to the previous, the deprioritized “path switch” also includes the switch between relayed and non-relayed UE-network connection.

There is no consensus whether the support of service continuity for UE-to-Network Relay is to be de-scoped from Rel-17 FS_5G_ProSe SID (as per WT paper endorsed at SA#86)

### 1.1.2	Companies View

Question: Should the support of service continuity for UE-to-Network Relay be de-scoped from Rel-17 FS_5G_ProSe SID?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| LGE | No | The de-prioritized WT#2.7 (Path switching) is not about UE-to-Network Relay. We think that the support of service continuity for UE-to-Network Relay is scope of the study. |
| MediaTek Inc. | No |  |
| KPN | No |  |
| Lenovo/Motorola Mobility | No |  |
| Nokia | Yes | The de-prioritized WT#2.7 (Path switching) is global. Service continuity for UE-to-Network Relay de-scoping from Rel-17 FS_5G_ProSe SID need not be debated by SA2 as it had been already been removed by SA plenary de-prioritization last December. |
| Intel | No | Service continuity is part of the key issue#3, since there was no change to this KI, it should be kept in the scope of Rel-17. |
| Huawei | No |  |
| Spreadtrum | No |  |
| ZTE | No |  |
| Telecom Italia | No |  |
| Sony | No |  |
| Futurewei | No |  |
| FirstNet | No | We don’t believe that the service continuity capability for the ProSe UE-Network relay should be impacted by the descoping of WT#2.7 (Path switching). Service continuity of “UE-Network relay” is being addressed as part of key issue #3 and again should have not been impacted by the descoping of WT#2.7. From a public safety perspective, it is crucial for us to provide minimal interruption to their services as that saves lives. |
| AT&T | No | Service continuity is an essential feature to support public safety use cases |
| Convida Wireless | No |  |
| Interdigital Inc. | No | Service continuity is important for ProSe traffic, especially for public safety service. |
| Apple | No |  |
| CATT | No | The down scoped WT#2.7 (Path Switching) has no dependency on WT#2.8 (UE-to-Network Relay). |
| Fraunhofer HHI | No |  |
| Airbus | No | This view is not based on a semantic nor grammatical analysis of the decision made in SA#86 for SID downscoping, but only on the interest in that capability from a Mission Critical solutions perspective |
| China Mobile | No |  |
| China Unicom | No |  |
| Tencent | No |  |
| OPPO | No | The supported scenario needs to be coordinated with RAN WG. |
| Ericsson | Yes | -We believe the question is misleading/wrong, since service continuity in any form has never been in scope: - WT2.6 (path selection): TUs were reduced (SI TU) - WT2.7 (path switching): TUs were removed with the corresponding WT down-scoped. - WT2.10 (multi-hop enh. UE/NW Relay): TUs were removed with the corresponding WT down-scoped. Nowhere does it explain or add any exception to the Path Switch for PC5 with Relays. In addition, please note that (SP-191371) for QoS, there is a dedicated WT (2.5) and in addition for Relay it is also mentioned that QoS is included within the Relay WTs (2.8 and 2.9), whereas for Path Switch the same has not been done. -Decoupling Path Switching from Service Continuity and adding restriction on developing only certain scenarios is wrong way forward. As the problem description above shows, UE to Network Relay includes Uu and as such any partial scope as pushed forward here can influence potential Path Switch development in future adversely. -We should focus on the current scope of the study without adding new partial requirements in Rel-17. Path Switch/Service continuity needs to be addressed together to provide a complete solution in future releases. The urgency is not evident to us as we expect this work can be achieved at a later release. |
| The Police of the Netherlands | No | Service continuity is essential in Public Safety scenarios of UE-to-Network relays |
| Qualcomm | Yes | No TU should be allocated for this topic. Service continuity has no clear definition and can be considered met or not met depends on various application layer requirements. Additionally, the exact scope of the "service continuity" is not defined as well. For example, in a typical deployment, especially for the Public Safety, does it also cover the case the UE-to-Network Relay moves from 5GS to EPS while continues providing the service? Overall, this is not suitable for Rel-17 study. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.