Pre SA2#138E e-meeting Email Discussion

Source: 	5G_CIoT rapporteur

Title: 	Email Discussion on support of MT-EDT for 5GC

# 1.	MT-EDT for 5GC

## 1.1	Whether and how to support MT-EDT for 5GC in Rel-16

### 1.1.1	Description

#### 1.1.1.1	Whether to support MT-EDT for 5GC in Rel-16

Mobile Terminated Early Data Transmission (MT-EDT) enables power and signalling efficient delivery of single downlink data transmission.

MT-EDT has already been introduced for NB-IoT/WB-EUTRAN connected to EPC. MT-EDT has on the other hand not been agreed yet for NB-IoT/WB-EUTRA connected to 5GC due to concerns on how to support 5G-GUTI reallocation during MT-EDT procedures.

The background of this is the following difference between 5GC and EPC: In 5GC there is an SA3 requirement to reallocate a new 5G GUTI also during MT-EDT for CP CIoT 5GS optimization and UP CIoT 5GS optimization procedures.

Solutions were proposed in earlier meetings to support GUTI re-allocation as part of MT-EDT procedures but no solution has been agreed yet.

#### 1.1.1.2	Support of GUTI re-allocation during MT-EDT procedure

It has been proposed to support 5G GUTI re-allocation as follows:

-	AMF sends a new 5G-GUTI to the UE during MT-EDT for CP CIoT 5GS optimization and UP CIoT 5GS optimization procedures in RRC Message 4;

-	UE stores the new 5G-GUTI without sending an immediate NAS acknowledgement;

-	AMF considers both the new 5G-GUTI and the old 5G-GUTI valid until it receives the next NAS message from the UE that uses the new 5G-GUTI (i.e. the next NAS message from the UE that uses the new 5G-GUTI acknowledges the new 5G-GUTI).

#### 1.1.1.3.	AMF paging strategy after MT-EDT with 5G-GUTI re-allocation

AMF paging strategy is typically up to implementation; however in the context of MT-EDT with 5G-GUTI reallocation paging strategy enhancements could be considered.

As per clause 1.1.1.2, AMF has an old and a new 5G-GUTI that AMF considers valid for the UE after MT-EDT with 5G-GUTI reallocation. If AMF needs to page the UE then AMF has to select with which 5G-GUTI to page the UE (first).

Two options exist:

Option 1: Leave it up to AMF implementation with which 5G-GUTI to page the UE first.

Option 2: Specify the following enhancement:

-	If the RAN cannot deliver the NAS container with the new 5G-GUTI to the UE (see clause 1.1.1.2), then the RAN node shall send a N2 NAS Non Delivery Indication message to AMF.

-	If the AMF has to page the UE after MT-EDT for CP CIoT 5GS optimization or UP CIoT 5GS optimization was the last procedure, i.e. if a new 5G-GUTI has been reassigned using the scheme described in clause 1.1.1.2, then depending on whether AMF received a N2 NAS Non Delivery Indication:

-	if the AMF did not receive an N2 NAS Non Delivery Indication then AMF first uses the new 5G-S-TMSI from the new 5G-GUTI for paging for an implementation dependent number of paging attempts;

-	if the AMF did receive an N2 NAS Non Delivery Indication then AMF first uses the old 5G-GUTI for an implementation dependent number of attempts.

#### 1.1.1.4	Local 5G TMSI derivation using an offset

As an alternative to the solution described in clause 1.1.1.2, the following has been proposed (see S2-2002259):

-	UE and AMF negotiate as part of the Registration procedure that during MT-EDT new 5G-TMSI values will be derived locally in UE and AMF using an offset value selected by AMF;

-	Based on this, UE and AMF locally derive a new 5G-TMSI value by offsetting the previous 5G-TMSI during each MT-EDT procedure.

### 1.1.2	Companies View

Question 1: Should MT-EDT be supported for 5GC in Rel-16?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| Huawei | No | Not a valid question at this stage. The fact is there is no reasonable solution to resolve the GUTI reallocation issue. The solution is not justified considering the very limited benefit and huge impact on the system including UE, RAN and CN for 5GC. |

Question 2: Should 5G-GUTI re-allocation be supported as described in clause 1.1.1.2?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| Huawei | No | This created huge principle impact on existing 5G-GUTI re-allocation over NAS. For 1st bullet in the proposal, it impacts the current 5G-GUTI allocation over NAS: (a) For CP, it has to include the 5G-GUTI (14 octets) and data in the service accept message which created unnecessary message overload for CP optimization. Note that CT1 has taken long time to optimize the message overload for CP optimization and if so CT1 feedback on this is required. (b) For UP, it is unclear to use which NAS message to carry the new 5G-GUTI, we believe there is no existing NAS message can be reused and hence needs to define a NAS message for this, which created huge NAS impacts. This clearly overwhelms the benefits from MT-EDT. For 2nd bullet in the proposal, the 5G-GUTI re-allocation without ack will create huge impact on existing 5G-GUTI re-allocation over NAS: Currently it is mandatory to ack the 5G-GUTI re-allocation. This principle is there since 2G/3G/4G and now in 5G. The impacts of changing this to optional does overwhelm the benefits from MT-EDT. For 3nd bullet in the proposal, it also created huge impacts on AMF handling on 5G-GUTI re-allocation: (a) Currently only in abnormal cases the AMF can have two valid 5G-GUTIs but this proposal will make this happened very often in normal cases, this is not a good network KPI for operators; (b) For per subsequent paging, the AMF has to decide to use which 5G-GUTI for paging but finally the UE will only respond for one 5G-GUTI, this impacted the AMF paging strategy, added unnecessary AMF complexity and created signalling overload over air. All these overwhelm the benefits from MT-EDT. |

Question 3: Should AMF paging strategy after MT-EDT with 5G-GUTI re-allocation be left for implementation (Option 1 in clause 1.1.1.3) or should Option 2 described in clause 1.1.1.3 be specified?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| Huawei | Option 1: No Option 2: No | We believe AMF paging strategy shall not be impacted just due to MT-EDT. Any updates on AMF paging strategy will overwhelm the benefits from MT-EDT. The option 2 links to the “N2 NAS Non Delivery Indication” but technically it is wrong. Without the Indication, it does not mean UE receives the NAS message. The lower layer failure case described in the 24.501 is something different from the “N2 NAS Non Delivery Indication”. Option 2 is deviated from the current AMF paging strategy in two valid 5G-GUTIs abnormal cases with further change but this proposal will make this happened very often in normal cases, this is not a good network design. |

Question 4: Should local 5G TMSI derivation using an offset as described in clause 1.1.1.4 be supported instead of explicitly signaling the new 5G-GUTI (as described in clause 1.1.1.2)?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| Huawei | No | The solution has privacy issue, because An attacker could capture two 5G-GUTIs in two adjacent RR message, then the attacker could derive offset according to two 5G-GUTIs. Attacker can still track the UE with new 5G-GUTI using derived offset and latest 5G-GUTI. In general the expertise from SA3 is needed to evaluate this solution. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.