Pre SA2#138E e-meeting Email Discussion

Source: 	5G_CIoT rapporteur

Title: 	Email Discussion on support of MT-EDT for 5GC

# 1.	MT-EDT for 5GC

## 1.1	Whether and how to support MT-EDT for 5GC in Rel-16

### 1.1.1	Description

#### 1.1.1.1	Whether to support MT-EDT for 5GC in Rel-16

Mobile Terminated Early Data Transmission (MT-EDT) enables power and signalling efficient delivery of single downlink data transmission.

MT-EDT has already been introduced for NB-IoT/WB-EUTRAN connected to EPC. MT-EDT has on the other hand not been agreed yet for NB-IoT/WB-EUTRA connected to 5GC due to concerns on how to support 5G-GUTI reallocation during MT-EDT procedures.

The background of this is the following difference between 5GC and EPC: In 5GC there is an SA3 requirement to reallocate a new 5G GUTI also during MT-EDT for CP CIoT 5GS optimization and UP CIoT 5GS optimization procedures.

Solutions were proposed in earlier meetings to support GUTI re-allocation as part of MT-EDT procedures but no solution has been agreed yet.

#### 1.1.1.2	Support of GUTI re-allocation during MT-EDT procedure

It has been proposed to support 5G GUTI re-allocation as follows:

-	AMF sends a new 5G-GUTI to the UE during MT-EDT for CP CIoT 5GS optimization and UP CIoT 5GS optimization procedures in RRC Message 4;

-	UE stores the new 5G-GUTI without sending an immediate NAS acknowledgement;

-	AMF considers both the new 5G-GUTI and the old 5G-GUTI valid until it receives the next NAS message from the UE that uses the new 5G-GUTI (i.e. the next NAS message from the UE that uses the new 5G-GUTI acknowledges the new 5G-GUTI).

#### 1.1.1.3.	AMF paging strategy after MT-EDT with 5G-GUTI re-allocation

AMF paging strategy is typically up to implementation; however in the context of MT-EDT with 5G-GUTI reallocation paging strategy enhancements could be considered.

As per clause 1.1.1.2, AMF has an old and a new 5G-GUTI that AMF considers valid for the UE after MT-EDT with 5G-GUTI reallocation. If AMF needs to page the UE then AMF has to select with which 5G-GUTI to page the UE (first).

Two options exist:

Option 1: Leave it up to AMF implementation with which 5G-GUTI to page the UE first.

Option 2: Specify the following enhancement:

-	If the RAN cannot deliver the NAS container with the new 5G-GUTI to the UE (see clause 1.1.1.2), then the RAN node shall send a N2 NAS Non Delivery Indication message to AMF.

-	If the AMF has to page the UE after MT-EDT for CP CIoT 5GS optimization or UP CIoT 5GS optimization was the last procedure, i.e. if a new 5G-GUTI has been reassigned using the scheme described in clause 1.1.1.2, then depending on whether AMF received a N2 NAS Non Delivery Indication:

-	if the AMF did not receive an N2 NAS Non Delivery Indication then AMF first uses the new 5G-S-TMSI from the new 5G-GUTI for paging for an implementation dependent number of paging attempts;

-	if the AMF did receive an N2 NAS Non Delivery Indication then AMF first uses the old 5G-GUTI for an implementation dependent number of attempts.

#### 1.1.1.4	Local 5G TMSI derivation using an offset

As an alternative to the solution described in clause 1.1.1.2, the following has been proposed (see S2-2002259):

-	UE and AMF negotiate as part of the Registration procedure that during MT-EDT new 5G-TMSI values will be derived locally in UE and AMF using an offset value selected by AMF;

-	Based on this, UE and AMF locally derive a new 5G-TMSI value by offsetting the previous 5G-TMSI during each MT-EDT procedure.

### 1.1.2	Companies View

Question 1: Should MT-EDT be supported for 5GC in Rel-16?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| ZTE | No | ZTE supports MT-EDT for 5GC in Rel-16 or later version, if there is a proper solution. |

Question 2: Should 5G-GUTI re-allocation be supported as described in clause 1.1.1.2?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| ZTE | No | The solution increases system complexity and reduces paging efficiency. As EDT features are not used for transmitting NAS signaling, whether a new 5G-GUTI can be sent to UE via RRC Message 4 need to be further discussed or confirmed by RAN. |

Question 3: Should AMF paging strategy after MT-EDT with 5G-GUTI re-allocation be left for implementation (Option 1 in clause 1.1.1.3) or should Option 2 described in clause 1.1.1.3 be specified?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| ZTE | Option 1: No Option 2: No | The same as Question2. |

Question 4: Should local 5G TMSI derivation using an offset as described in clause 1.1.1.4 be supported instead of explicitly signaling the new 5G-GUTI (as described in clause 1.1.1.2)?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| ZTE | No | Potential security risks exist in this solution. Suggest to be confirmed by SA3. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.