Pre SA2#138E e-meeting Email Discussion

Source: 	Vertical_LAN Rapporteur (Nokia)

Title: 	Email discussion on Vertical_LAN

# 1.	Issues for Vertical_LAN

## 1.1	Support for PSFP based Hold and Forward Buffering rule

### 1.1.1	Description

Determine the need to support PSFP based Hold and Forward Buffering rule that is provided on a per TSC stream basis to NW-TT and DS-TT. This is for buffering the TSC stream that earlier arrived at the egress port to their scheduled transmission time (reference S2-2002164).

### 1.1.2	Companies View

Question: Do you foresee the need to support PSFP based Hold and Forward Buffering rule that is provided on a per TSC stream basis to NW-TT and DS-TT?

If your answer is YES, please indicate if you would support approving a revision of S2-2002164?

| Company Name | Company View Yes/No | Notes |
| --- | --- | --- |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.2	VLAN ID configuration for bridge management

### 1.2.1	Description

Editor’s Note: Brief description of the Issue.

It is unclear how VLAN ID should be configured for bridge management. Following are some options considered:

- Solution Option 1: As soon as the TSN AF knows the port numbers, the VLAN configuration can be performed via SNMP from a OAM/CNC similar as for the LLDP configuration. The TSN AF transfers then the VLAN configuration to the UPF using the additional parameters defined in the CR.

- Solution Option 2: The VLAN configuration per port is also pre-configured together with the port numbers of the Ethernet in NW-TT and will be provided to the TSN AF. Then the VLAN pre-configuration may be reported together with the port numbers.

### 1.2.2	Companies View

Question: Should Solution Option 1 or Option 2 or some other option (if so, what?) be selected as solution for issue described in 1.2.1?

| Company Name | Company View (Option 1/Option 2/some other option) | Notes |
| --- | --- | --- |

### 1.2.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.2.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.3	Assumptions on the number of ports per NW-TT within the UPF

### 1.3.1	Description

Varying assumptions on the number of ports per NW-TT within the UPF.

Following are the possible options:

- Option A: There is only one NW-TT per UPF. Each NW-TT can have one or more ports. This option implies that the spec should be updated to include Bridge management and LLDP topology discovery to be done a per port basis.

- Option B: There is only one NW-TT per UPF. Each NW-TT can have at most one port. This implies that the Static Filtering Entry information that was agreed to determine the NW-TT egress port for forwarding UL TSC traffic becomes useless

### 1.3.2	Companies View

Question: Do you agree with option A or option B?

| Company Name | Company View (Option A/Option B) | Notes |
| --- | --- | --- |

### 1.3.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.3.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.4	System Configuration that is not PDU Session specific

### 1.4.1	Description

Misuse of PCF procedures for invoking system configuration that is not PDU Session-specific. Refer to draft CRs from Intel circulated in the SA2 discussion list on March 31st, 2020 that updates this to use NEF procedures for invoking system configuration that is not PDU-session specific, also uploaded as S2-2002671, S2-2002672, S2-2002673 and S2-2002674.

### 1.4.2	Companies View

Question #1: Do you prefer to introduce NEF procedures (instead of misuing PCF procedure) for invoking system configuration that is not PDU Session specific?

Question #2: If so, would you be OK to work on revision(s) of the Intel CRs circulated in the SA2 discussion list with the view of approving them in SA2#138E?

| Company Name | Company View YES/NO to Q1 YES/NO to Q2 | Notes |
| --- | --- | --- |

### 1.4.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.4.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.5	Support for CAG specific Access control

### 1.5.1	Description

Refer to incoming LS from RAN2 in S2-2002656; It states:

‘Although at least one operator has indicated that UAC Parameters should also specify CAG ID, to date there is no agreement in RAN2 on the required granularity of UAC parameters broadcasted in a cell in case of PNI-NPNs with multiple CAG IDs for the same PLMN. More specifically whether it is sufficient to broadcast the Unified Access Control (UAC) parameters per PLMN or there is need to broadcast CAG ID specific configuration of UAC parameters. RAN2 observed that SA2 has specified in TS23.501 Section 5.30.3.4 that “In order to prevent access to NPNs for authorized UE(s) in case of network congestion/overload, existing mechanisms defined for Control Plane load control, congestion and overload control in clause 5.19 can be used, as well as the access control and barring functionality described in clause 5.2.5, or Unified Access Control using the access categories as defined in TS 24.501 [47] can be used”. RAN2 was not able to conclude whether this means that using the operator-defined access categories with access category criteria type set to the S-NSSAI used for PNI-NPN is sufficient to provide CAG specific access control.’

It should also be noted that TS 23.501 states:

- As network slicing does not enable the possibility to prevent UEs from trying to access the network in areas which the UE is not allowed to use the Network Slice allocated for the NPN, Closed Access Groups may optionally be used to apply access control.

- A Closed Access Group identifies a group of subscribers who are permitted to access one or more CAG cells associated to the CAG.

- CAG is used for the Public network integrated NPNs to prevent UE(s), which are not allowed to access the NPN via the associated cell(s), from automatically selecting and accessing the associated cell(s).

Note: Although two related questions in RAN2 LS are for CT1/SA1, this is also relevant for SA2 discussion based on the quote from TS 23.501 in RAN2 LS, also the fact that SA2 identified that the CAG feature may optionally be used to apply access control.

- Question 1: 
Is there a requirement to enable PNI-NPN (CAG ID) specific access control in cells that are shared among PNI-NPNs belonging to the same PLMN?

- Question 2: 
If there is a requirement to enable PNI-NPN (CAG ID) specific access control in cells that are shared among PNI-NPNs belonging to the same PLMN, then is it sufficient to broadcast the Unified Access Control (UAC) parameters per PLMN (assuming that using the operator-defined access categories with access category criteria type set to the S-NSSAI used for PNI-NPN is sufficient to provide CAG specific UAC) or there is need to enable the broadcast of CAG ID specific configuration of UAC parameters?

LS states:

“RAN2 understanding is that after manual CAG ID selection by UE NAS the UE AS shall select a cell that supports the manually selected CAG ID in order to perform the registration procedure triggered by UE NAS. RAN2 is seeking further guidance on the manual CAG ID selection issue. RAN2 has the following questions:”

Question 3: 
If a UE performs manual CAG selection and a successful registration, then whether the UE shall stay on cells supporting the manually selected CAG ID in RRC_CONNECTED state especially in the case when after registration the Allowed CAG List in the UE does not contain the manually selected CAG ID?

Question 4:
Shall a UE prioritize for cell reselection the cells supporting the manually selected CAG ID over other suitable cells that do not support the manually selected CAG ID after a successful registration?

### 1.5.2	Companies View

Answer to Questions 1, 2, 3, 4, 5 above.

| Company Name | Company View YES/NO to Q1 YES/NO to Q2 YES/NO to Q3 YES/NO to Q4 | Notes |
| --- | --- | --- |
| Ericsson | NO to Q1 YES to it is sufficient and NO to last question of Q2 NO to Q3 NO to Q4 | Q1: The question, even though not clear, is related to UAC. The UAC requirements are specified by SA1, and there are no such requirements. The question is addressed to SA1 i.e. SA1 need to answer it. However, it has been discussed by SA2 and the reason for adding CAG functionality was the requirement (from TS 22.261) "The 5G system shall support a mechanism to prevent a UE with a subscription to a non-public network from automatically selecting and attaching to a PLMN or non-public network it is not authorized to select.", and slicing could not prevent that at cell selection as stated in above referenced text (from 23.501) "As network slicing does not enable the possibility to prevent UEs from trying to access the network in areas where the UE is not allowed to use the Network Slice allocated for the NPN, Closed Access Groups may optionally be used to apply access control.". UAC is simply not something that is used to control the UEs cell selection by a non-overloaded network. The UAC aspect is also clarified in Annex D2 of 23.501 with " In order to prevent access to NPNs for authorized UE(s) in the case of network congestion/overload and if a dedicated S-NSSAI has been allocated for an NPN, the Unified Access Control can be used using the operator-defined access categories with access category criteria type (as defined in TS 24.501 [47]) set to the S-NSSAI used for an NPN." Q2: CAGs define areas for accessing the PLMN. The PLMN may use slicing to support one or more NPNs, e.g. each NPN may get their own S-NSSAI and for areas where more than one S-NSSAI are available, the same CAG ID may be used. If UAC for S-NSSAIs is required, then it can be enabled by e.g. an ODAC used for the specific or group of S-NSSAIs. There is therefore no need for CAG ID specific UAC. Q3: The network will provide the UE with updated CAG information when it has changed in the network. If the CAG ID that was manually selected is not part of the Allowed CAG list, then the UE shall not stay on the cell (unless in limited service). In CM-CONNECTED the NG-RAN ensures this by AMF providing an up to date Mobility Restriction List that includes the CAG information. Q4: There is no priority among the CAG IDs of a PLMN, i.e. there is no need to prioritize the manually selected CAG ID. As long as the UE finds a cell from where there UE can access the network, any of the CAG cells gives the same access. If the UE would prioritize one CAG ID and some of the CAG IDs in the Allowed CAG list gets available with better performance the UE would try to access the network from a non-optimal cell. Once the UE has been updated with the current CAG info as available in the network, the UE shall use the network provided CAG information during cell reselection (and disregards the manually selected CAG ID). The reason to use manual selection is to cover cases when the UE has not yet been updated with the latest CAG information by the network. |

### 1.5.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.5.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.