Pre SA2#138E e-meeting Email Discussion

Source: 	ETSUN Rapporteur (Nokia)

Title: 	Email Discussion on ETSUN open issues

# 1.	Issues for ETSUN

## 1.1	ETSUN and ATSSS interworking

### 1.1.1	Issue Description

Only solution 1 is now on the table as per the minutes of the Conf Call held on Friday March 27th, 2020;

BUT During this Conf Call, the question has been raised on whether the extent of specification change [to define ETSUN and ATSSS interworking at this point of time]  is suitable considering that these would be late  changes to R16; NO firm conclusion has been taken BUT, not supporting these changes would prevent ATSSS from being offered (even in  non-roaming case) by a PLMN that deploys ETSUN. It has been requested by the rapporteur that any company willing to object to this feature should indicate it as soon as possible.

### 1.1.2	Companies View

Question 1: Should ETSUN and ATSSS interworking be defined in R16?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| Huawei | Yes | It should be considered how to support ATSSS in ETSUN scenario. |

Question 2: if yes, is answered to Question 1 should this interworking be defined according to overall solution described in the documents submitted to the Conf Call held on Friday March 27th, 2020 (possibly improved for some second order aspects)

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| Huawei | Yes | We agree to move forward with solution 1 (i.e. separated CP connections and UP connections for different access types). However, the proposed documents need to be further revised to support the switching between “same I-SMF” case and “different I-SMFs” case. Also it is possible in the non-3GPP access, there are no I-SMF/I-UPF, but the I-SMF/I-UPF is required in the 3GPP access. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.