Pre SA2#138E e-meeting Email Discussion

Source: 	eNA Rapporteur (Huawei)

Title: 	Email Discussion on eNA open issues

# 1.	Issues for eNA

## 1.1	Whether/how to support abnormal behavior related network data analytics for target of analytics reporting being any UE

### 1.1.1	Description

In TS 23.288, clause 6.7.5.1 specifies that "any UE" can be requested as "Target of Analytics Reporting" for abnormal behaviour related network data analytics, but the procedure in clause 6.7.5.4 does not specify the case “any UE”.

It is also incomplete with regards to data collection depending on the abnormal behaviour to be detected (Exception ID).

### 1.1.2	Companies View

Question:  How abnormal UE behavior related network data analytics should support target of analytics reporting being any UE? If NOT feasible, why?

| Company Name | Company View Feasible (Yes/No) | Notes |
| --- | --- | --- |
| NEC | Yes |  |
| Ericsson | Yes | - It is feasible to provide analytics on Abnormal UE behavior targeting “any UE”. - There is a need to indicate that a request for analytics for “any UE” causes heavy load and then discuss how to decrease it, such as recommend using Analytics filters. - It is feasible to provide analytics on Abnormal UE behavior targeting “any UE”. - There is a need to indicate that a request for analytics for “any UE” causes heavy load and then discuss how to decrease it, such as recommend using Analytics filters. - If the request for Abnormal UE behavior targets Events from AMF or SMF only then the Target for Event Reporting is set to “any UE” can be included. However, if the request for Abnormal UE behavior targets Events from both SMF and AMF and then our proposed solution includes an optimization is as follows: - The NWDAF subscribes to AMF to EventReporting, Target for Event Reporting set “Any UE”, Event ID set to “Number of UEs served by the AMF and located in Area Of Interest"; Event Filter set to “Area of Interest”. The Area of Interest is assigned the value requested by the NWDAF consumer. Example of Area of Interest is a TAI. - The NWDAF receives the list of SUPIs in the Area of Interest served by the AMF. - The NWDAF subscribes to SMF(s) that serves the Area of Interest and the target for Event Reporting set “list of SUPIs”, Event ID set to Abnormal UE behavior, This solution reduces the signaling compared with a request for “any UE” in an Area of Interest to those SMFs located in the Area of Interest. |
| Orange | Yes | Clause 6.7.5 to be updated to clarify that the NWDAF detects abnormal behaviour compared to one or more of (a) Expected UE Behaviour parameters (see TS 23.502 clause 4.15.6.3), (b) expected UE behaviour provided in Analytics Filter Information of the analytics request, (c) past observation made by the NWDAF; only (b) and (c) apply for "any UE". The procedure in clause 6.7.5.4 needs to be updated along the following principles: - Add "any UE" in step 1. - In step 2 (Namf_EventExposure_Subscribe), add "any UE" as Target of Event Reporting. In Rel-16 according to TS 29.518, "any UE" is possible Target for Communication-Failure-Report and UEs-In-Area-Report. If the NWDAF needs to use other events, the NWDAF may perform subscriptions for individual UEs on a sample of UEs that it knows are likely to be in the AoI according to data previously collected; in this case the size of the sample should be reasonable to avoid generating excessive load. - Add a Note in step 2 to clarify that the NWDAF selects the AMF instances according to the Analytics Filter Information (e.g. AMF Region ID intersecting with Area of Interest). - In step 3 (Nsmf_EventExposure_Subscribe), add "any UE" as Target of Event Reporting. In Rel-16 according to TS 29.508, "any UE" is possible Target for all events. - Add a Note in step 3 to clarify that the NWDAF selects the SMF instances according to the Analytics Filter Information (e.g. SMF Area Identity intersecting with Area of Interest). |
| China Mobile | Yes | The "any UE" case may potentiallly lead to more signalling, that we need to figure out how to avoid. |
| Tencent | Yes | We also think it is feasible e.g. by reducing the load using the analytics filter |
| Spreadtrum | Yes |  |
| Intel | Yes |  |
| Huawei | Yes | It is beneficial to support any UE for abnormal behavior but need to clarify to how reduce the signaling. |
| LGE | Yes | Reducing signaling load needs to be considered. |
| ZTE | Yes |  |
| Sandvine | Yes | Requesting for abnormal behavior analytics for “any UE” may causes heavy load. Especially if the whole traffic is being inspecting/analyzing at the same time. However for instance searching abnormal behavior per each Application Id present in the traffic one per time is feasible and may allow to find UEs with abnormal behavior in an specific Application Id |
| Samsung | Yes(feasible) | Support of abnormality detection for any UE is considered as one of important scenarios and we have discussed and almost reached the way forward in the former meeting. This feature can be supported based on a combination of the expected analytics type (or the list of exception IDs) and event filter information. SA2#138E is right place to resume and complete technical discussions between interested parties. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.