Pre SA2#138E e-meeting Email Discussion

Source: 	China Mobile (Rapporteur)

Title: 	Email discussion on eSBA open issues

# 1.	Issues for eSBA

## 1.1	SBA multiple SCPs support

### 1.1.1	Issue Description

For an indirect communication between a consumer and a producer, it is possible that an SCP1 is deployed in the consumer’s end (e.g. site, region), while another SCP2 is deployed in the producer’s end (e.g. site, region). It is also possible with more than 2 SCP to support a more advanced signaling network. This means that in a routing path between a consumer and a producer there may be multiple SCPs. Currently the specifications has not detailed the support for multiple SCPs in the path.

At the last e-meeting SA2#137E, 4 documents from different companies addressing missing aspects of support for multiple SCPs.  We did not converge on a way forward during the e-meeting and instead postponed the documents. A CC is held on 23rd March, where Ericsson and NOKIA proposal are discussed. Some initial feedback is obtained.

### 1.1.2	Companies View

Question 1: SCP for producer and consumer and intermediate SCP, should we address them separately?

Question 2: If we should also address SEPPs aspect?

Question 3: Instance selection (at the beginning or at the end)?

Question 4: Whether to decouple route calculation from NF Profile and make it based on:

Option 1) request to be routed

Option 2) origin point

| Company Name | Company View Q1: (Yes/No) Q2: (Yes/No) Q3: (Yes/No) Q4: (Option 1/Option 2) | Notes |
| --- | --- | --- |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.