Pre SA2#138E e-meeting Email Discussion

Source: 	China Mobile (Rapporteur)

Title: 	Email discussion on eSBA multiple SCPs support

# 1.	Issues for  eSBA

## 1.x	SBA multiple SCPs support

### 1.x.1	Issue Description

Editor’s Note: Brief description of the Issue.

For an indirect communication between a consumer and a producer, it is possible that an SCP1 is deployed in the consumer’s end (e.g. site, region), while another SCP2 is deployed in the producer’s end (e.g. site, region). It is also possible that more than 2 SCP are in a communication path to support a more advanced signaling network. This means that in a routing path between a consumer and a producer there may be multiple SCPs. Currently the specifications has not detailed the support for multiple SCPs in the path.

At the last e-meeting SA2#137E, 4 documents from different companies addressing missing aspects of support for multiple SCPs.  We did not converge on a way forward during the e-meeting and instead postponed the documents. A CC is held on 23rd March, where Ericsson and NOKIA proposal are discussed. Some initial feedback is obtained.

### 1.x.2	Companies View

| Question | Company Name | Company View (Yes/No) / (Option A/Option B) | Notes |
| --- | --- | --- | --- |
| 1. Currently, if a deployment requires multiple SCPs for a given SBI message or messages, it is not specified how the HTTP/2 requests are routed between the SCPs (e.g. determination of Next Hop SCP). Do you see the need for SA2 to specify message routing between SCPs? | Nokia | Yes |  |
|  | ZTE | Yes |  |
|  | Deutsche Telekom | No | We do not really see the problem of configuring a distributed network of HTTP proxies as neither something new nor something that would require architectural work from SA2 perspective. In addition, very deployment-dependent. However, it seems like we are the only onew with this view. Any solution should at least not impact deployments that do not require this feature |
|  | Ericsson | Yes |  |
| 2. Given HTTP/2 request routing is standardized, should we provide procedures to convey to an SCP how to route SBI messages through two SCPs in the path (Option A) or should we provide procedures to convey to an SCP how to route SBI messages through more than one SCP in the path not restricted to max two. (Generalized “multiple SCPs” case)? (Option B) | Nokia | A and B | While two SCPs in the path are a likely scenario, multiple SCPs cannot be ruled out. Question is a bit ambiguous, thus some clarifications on my views: + It might collide with the intention of question 8. We need procedures to cover more than two SCPs, but we do not need procedures to provide the full path to the first SCP. + Also, procedures should also be usable for NF service consumers, not only SCPs. |
|  | ZTE | Option A |  |
|  | Deutsche Telekom | Option B | If this is indeed the way forward, the solution should be generic (i.e. not limited to a specific number) |
|  | Ericsson | Option B preferred | A generic solution is preferred, not limited to two SCPs. |
| 3. Should we also address SEPP aspects? | Nokia | Yes | Most likely a very similar solution can be used to discover egress SEPPs, and it beneficial f a network has multiple SEPs to cone to different PLMNs. However, I dpo not intend to cover routing from the egress SEPP in one PLMN to the ingress SEPP of another PLMN, as I assume that SEPPs already have suitable databsaes |
|  | ZTE | No |  |
|  | Deutsche Telekom | No | This would be a separate discussion altogether. Furthermore, one would first need to clarify what “SEPP aspects” are |
|  | Ericsson | No | Orthogonal discussion |
| 4. Should we also address where Instance selection is performed? If yes, where? At service consumer (Option A), first SCP in the path (Option B), last SCP in the path (Option C), other option (Option D) | Nokia | We need to support at least Option A and C | Model C allows instance selection either at NF service consumer or SCP. For model D it is only SCP .(In both cases it is so far open which SCP) It is beneficial to do instance selection at last SCP because this SCP can have up-to-date information about load, overload, and availability of instances (compare e.g. with CT4 work on load and overlaod control and consider that a serving SCP will have frequent exchanges with the served NFs). We assume that it will be up to operator policy to select where instance selection is done in the network. |
|  | ZTE | Option A and Option C | Option A is for model C, Option C is for Model C and D. |
|  | Deutsche Telekom | Option D | Selection should be based on what is included in the headers/URI. If a selection has been performed (does not matter by whome), the URI (root element, as defined by Stage 3) will point to a specific target. A receiving end (e.g. SCP) should stick to what is in the request. If the endpoint is not available, reselection may take place. Whether an extra header to notify further hops could be added to signal that selection was performed could be discussed though. But “who performs selection” is not in our view part of “route calculation” |
|  | Ericsson | Option A (for SCP model C is mandatory) Option B | In most cases the selection of routing path will depend on the selected target, that is, prior to find the right path we need to perform selection. Then, selection fits in consumer (option A, mandatory for SCP model C) and in the first SCP. Although selection may be considered in other SCPs in the paths, we think the extra complexity (e.g. selection parameters conveyed and extra logic in all SCPs) it implies does not compensate the benefit, that in fact is not clearly identified. |
| 5. Should we also address discovery of SCP serving an NF? (Such a first-hop SCP is currently assumed to be configured in the NF service consumer) | Nokia | Open | "Yes" allows for more dynamic assignment of serving SCPs to an NF but comes with some extra complexity: For instance, we might then want to indicate multiple hops in HTTP messages (question 8). Also, to support Model D we would probably need to extend NF registration procedures |
|  | ZTE | Yes |  |
|  | Deutsche Telekom | No | We doubt that SCPs are going to be a very dynamic part of the network. SCPs expose no API, so one would need to describe what is required to be in the NF profile and the selection criteria in 23.501. This work item would be even bigger. The impression we had was “the issue” was the “route calculation” |
|  | Ericsson | Preferrably yes | Once we implement the logic to determine a NextHop, this could easily be applied to the first SCP serving the NF as well. |
| 6. Should the calculation of the route to be taken by an SBI message take into account dynamic informaion about SCP availability? | Nokia | Yes | We anticipate that quite many SCPs can be in a network, and that their availability can thus change dynamically |
|  | ZTE | Yes |  |
|  | Deutsche Telekom | Open | Among many other parameters that are very deployment-specific (e.g. topology). We do not see the need to mandate the use of any specific parameters |
|  | Ericsson | Yes | This is crucial to determine a valid route. |
| 7. Given address discovery of SCP serving an SCP is addressed, what parameter(s) should an SCP selection be based on? Querying entity (Option A), Destination NF instance (Option B), Destiation IP address or Domain (Option C). Destination NF set (Option D), Destination Slice (Option E), Destination Location, e.g. compute center or geographical area (Option F), Served NF types (Option G), Remote PLMNs reachable through SCP (Option F)? | Nokia | All of the Options | I assume that it will be up to operator policy to how to set up routeing in its network. |
|  | ZTE | Optional G Option C | For model C, the NF performs NF discovery and then SCP discovery. The NF can use Served NF type and 3gpp-Sbi-Target-apiRoot to select the first SCP. The first SCP use 3gpp-Sbi-Target-apiRoot to discover the next/last SCP. For model D, the NF uses Served NF types (Option G) to discover the SCP. The first SCP performs the NF discovery and then use 3gpp-Sbi-Target-apiRoot to select the next SCP. |
|  | Deutsche Telekom | N/A | The whole point of the SCP is that the NF service consumer should send the request to the SCP and the SCP then decide where to send it. It sounds really strange that it is here proposed to standardize how an SCP can decide what the next SCP hop should be and then the first thing that a NF service consumer should do is decide what SCP to send the request to. The SCP should be able to find out where to send incoming requests to. |
|  | Ericsson | Option A + others | The route will be found based on the parameters today are known by SCP/NF, to avoid not required extra complexity. That is described in Erisson proposed CR S2-2001851: Inputs, Required: Network element identity of consumer and a target. Where network element identity is: NF ID; or SCP address. Where target is: - NF service in case of indirect communication with delegated discovery and requester is an NF. - NF service instance address if requester is SCP or NF using indirect communication without delegated discovery - Notification Target Address in case of a notification request. |
| 8. If procedures for routing through more than one SCP are defined, should we only address discovery of next-hop SCP (Option A), or of full path (Option B)? or both (Option C) | Nokia | Option A | Option B brings extra complexity as new routeing information is required in HTTP messas and limits the freedom of subsequent SCPs. |
|  | ZTE | Option A | This question doesn’t apply when only two SCPs are involved |
|  | Deutsche Telekom | Option A | It seems simpler and allows for easier implementation of distributed architecture (the whole topology may not be known) |
|  | Ericsson | Option A | Option B has extra complexity that is not required. |
| 9. If procedures for routing through more than one SCP are defined, should the entity for route calculation be the NRF (Option A) or new entity (Option B), or some other method (option C, then which)? | Nokia | Option A | I assume that existing NRF procedures (registration, heartbeat, discovery, can be reused if SCP and SEPP profiles are defned). A clarification on my vision: NRF will provide information on available SCPs, but SCPs of NF consumers can do a selection out of the available SCPs- |
|  | ZTE | Option B |  |
|  | Deutsche Telekom | Option B | Else, NRF implementations and vendors implementing NRFs may be impacted |
|  | Ericsson | Option A preferred Option B is OK | NRF already defines a hierarchy solution and provides information NF service endpoints. As well it will be simpler to extend this NF with a new service. |
| 10. If the NRF would be chosen as the entity for route calculation: Should we extend existing services with new SCP profiles (Option A), or by adding serving SCP address to or define new service (Option B)? | Nokia | Option A | Option A has minimal impacts and offers flexibility: Registration and heartbeat procedures can be used to obtain dynamic information about SCP availability in the NRF. Discovery procedure can be used to discover SCP profiles. As optimisation to reduce signalling, Nokia also proposes that discovery requests for NFs or services can return SCPs to reach them. Routing database could still contain configured elements that are added to SCP profiles, and are selected based on querying NF (or its location), SCP profiles offer a lot of flexibility to opearors: Which information is provided in SCP profiles could be up to operator policy (question 7). SCP profiles can also be extended in future releases or with proprietary information of operators. |
|  | ZTE | Option B | If NRF is chosed we support to add new service for routing calculation and add SCP profile. |
|  | Deutsche Telekom | N/A | Either option seems like an overcomplication of NF profiles. Whose NF profile would that be? The one of the NF? The NF may not even be aware at application layer that it is using an SCP (e.g. HTTP proxy sidecar). This would make the separation between application and PaaS more difficult |
|  | Ericsson | Option B | SBA services are defined to encapsulate specific functionality, so extending Discovery will convert this service in a service-for-all what will be more costly and complex for maintenance and evolution. A clean and specific new service is very much preferred. |
| 11. If the SEPP is also part of the route calculation, what of the options defined in Q10 would be preferred? | Nokia | Option A | Nokia proposes that a SEPP profile is also defined and used in a similar manner as the SCP profile. |
|  | ZTE | No |  |
|  | Deutsche Telekom | No |  |
|  | Ericsson | No | No reason to include SEPP as part of the route calculation. |
| 12. If this issue find a way forward, should it be pursued in Rel’16 (Option A) or Rel’17 (Option B)? | Nokia | Option A preferred | Seems to be an issue as soon as SCPs are deploied |
|  | ZTE | Option A |  |
|  | Deutsche Telekom | Whatever is more agreeable | As long a modular, clean, simple solution is possible. It should solve the problem some have and not make the architecture more complex for the others |
|  | Ericsson | Option A preferred | On the contrary only one SCP is supported. |
| 13. Should NF need to be aware that multiple SCPs are deployed | Nokia | No | To avoid complexity at this late stage. |
|  | ZTE | No |  |
|  | Deutsche Telekom | No | NF need even not be aware that there is a single SCP deployed. If we would have wanted to be non-transparent, we would have given it an exposed API. |
|  | Ericsson | No |  |

### 1.x.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.x.4	Porposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.