Pre SA2#138E e-meeting Email Discussion

Source: 	ZTE

Title: 	Email Discussion on Non-homogeneous support for ATSSS in Rel-16

# 1.	Non-homogeneous support for ATSSS in Rel-16

## 1.x	Non-homogeneous support for ATSSS in Rel-16

### 1.x.1	Description

ATSSS in Rel-16 is an optional feature.  During the inter-PLMN Home Routed roaming scenario, it is possible that the PLMN for the 3GPP access leg and the PLMN for the non-3GPP access leg for a given MA-PDU session may be different and may not both support ATSSS.  When first access leg is successfully established with MA PDU session with its serving PLMN, and the serving PLMN of the second access leg does not support ATSSS, the ATSSS capability provided by the UE will not be recognized by the serving PLMN of the second leg.  As a result, the selected target NF in the PLMN of the second leg may not be ATSSS capable to support the MA PDU Session establishment.  Furthermore, such inconsistent ATSSS support within and across PLMN for MA PDU session will also impact N2 and idle mode mobility handover for the continuation of the MA PDU session.

After many weeks of online and offline discussions, a tentative agreement has been reached to address this issue in Rel-16 based on the following principles: i.e.

(1) During the UE registration, the serving AMF will inform the UE with network indication for the support of ATSSS, if supported, and

(2) During the N2 mobility handover or idle mode mobility for MA PDU session, when network detects that the destination network no longer supports ATSSS, the MA PDU session will be released accordingly (further technical details to determine whether AMF triggered or SMF triggered for the MA PDU session release will be captured in the CRs to be submitted to SA2#138e eMeeting).

### 1.x.2	Companies View

Question: Should the handling of non-homogeneous support for ATSSS be based on the solution principles as described in (1) & (2) above?

| Company Name | Company View (Yes/No) | Notes |
| --- | --- | --- |
| ZTE | Yes – (1) & (2) | ZTE supports serving AMF to indicate to the UE for the support of ATSSS as described in (1) ZTE supports the solution principles as described in (2), more specifically, we prefer the AMF triggered approach to release the MA PDU session when the destination network/NF(s) do not support ATSSS. |
| Qualcomm | Yes to both principles (1) & (2) | Qualcomm supports the serving indication from the serving AMF to the UE during the registration to indicate the support of ATSSS. NOTE: Qualcomm believes it is necessary to clarify that such indication applies to the current Registration Area. |
| Huawei | Yes – (1) & (2) | Huawei supports serving AMF to indicate to the UE for the support of ATSSS as described in (1) Huawei supports the solution principles as described in (2), more specifically, we prefer the AMF triggered approach to release the MA PDU session when the destination network does not support ATSSS. |

### 1.x.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

Summary on April 3rd, 2020:

- 3 companies (ZTE, Qualcomm and Huawei) expressed their views and all support the solution principles as described in (1) & (2) above.

- both ZTE and Huawei prefer AMF based approach to release the MA PDU session in the target network

- Qualcomm believes that it is necessary to clarify the scope of the network indicator applied to the current registration area

### 1.x.4	Porposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.