## Slide 1
Ming Ai
CATT
Way forward on
Reply to LS on Local NR positioning in NG-RAN
for SA2 CC on April 20th, 2020

## Slide 2: Related T Docs
7.6 | S2-2002612 | LS In | Action | LS from TSG RAN: LS on Local NR positioning in NG-RAN | TSG RAN (RP-193262) |  | Postponed S2-2001782 from S2#137E. Responses drafted in S2-2002893 and S2-2003117
7.6 | S2-2002893 | LS OUT | Approval | [DRAFT] Reply LS on Local NR positioning in NG-RAN | Nokia, Nokia Shanghai Bell | Rel-16 | Revision of (postponed) S2-2002184 from S2#137E. Response to S2-2002612
7.6 | S2-2003117 | LS OUT | Approval | [DRAFT] Reply LS on Local NR positioning in NG-RAN | Huawei, Hisilicon | Rel-16 | Response to S2-2002612

## Slide 3: Question in S2-2002612/RP-193262
1. Overall Description:
RAN3 has studied the feasibility and specification impact of local LMF (i.e., LMC) in NG-RAN as per the SA2 conclusion from the study (Study on Enhancement to the 5GC Location Services, TR 23.731), as well as the RAN2 conclusion (Study on NR Positioning Support, TR 38.855). RAN3 also concluded as below (see TR 38.856 for more details).
  RAN3 has studied the feasibility and specification impact of local LMF (i.e., LMC) in NG-RAN.
  Three architecture alternatives have been studied. It is concluded that support of LMC in NG-RAN is feasible
  Architecture 3 seems like the most promising option among the ones studied. RAN3 did not evaluate the benefits of any of the architecture options in terms of latency towards the core network, RAN3 also did not fully evaluate, e.g., mobility issues associated with the introduction of the LMC.
  RAN3 could not reach consensus on any recommendation for normative work.
RAN discussed LMC, but has not reached consensus on any follow-on work. Questions were raised during the discussion about the benefit and deployment scenario.
2. Actions:
To SA2:
TSG-RAN would like to ask SA2 to take this situation into account and provide feedback to TSG-RAN on e.g., benefit and deployment scenario of this feature.

## Slide 4: Some Highlights of Pervious 2 Meetings
The LS in and two draft Replies (one from Nokia, one from HUAWEI) has been discussed during SA2 meetings this Q1;
Some agreements reached:
  Confirm RAN WG that the requirements on positioning latency, refer to SA1
  Some architecture e.g. LMF functionality in RAN or LMF and LMF located closer to RAN, could reduce the latency.
Open issues:
  Consensus couldn’t be reached on the quantitative evaluation of the latency reduction.

## Slide 5: Way forward proposal
Observations:
  Nokia/Sherry initiated an email discussion on this, and proposed how to merge two Draft LS back ;
Way forward proposal :
  LS back to RAN should not be delayed anymore. i.e. we/SA2 should reply RAN within Q2;
  In the LS back, agreement reached (in pervious and this meetings) should be captured, e.g.:
    Confirm RAN WG that the requirements on positioning latency, refer to SA1;
    Some architecture e.g. LMF functionality in RAN or LMF and LMF located closer to RAN, could reduce the latency.
    (further agreements…..)