## Slide 1: SA WG2 Meeting #139-e S2-2004299
1st to 12th June 2020, Online
Source: Sandvine
Title: QoS sustainability low latency Use case
Document for: Informative
Agenda Item: 8.1
Work Item / Release: FS_eNA_ph2 / Rel-17
Abstract of the contribution: This paper ilustrates a QoS sustainability low latency Use case related to S2-2004274 Key Issue #11: User-plane specialized NWDAF to minimize data collection to the TR 23.700-91.

## Slide 2: Background S2-2004299
QoS sustainability low latency Use case
The TS23.501 states to support low latency services and access to local data networks, UP functions can be deployed close to the Access Network.
For the network to support, low latency services is crucial that: It performs analytic-predictions based on the recent traffic behaviour. It takes and enforces the derived decisions, right there where the network is delivering the service.
For the NWDAF, the latency in collecting data and delivering the Oucomes matters for low latency services.

## Slide 3: 5G Introduction Use case: Self driving vehicle S2-2004299
Two alternatives of QoS sustainability solution. With analytics and without analytics
TA1
TA2
TA3
TA4
TA6
TA7
TA5
TA15
TA17
TA21
TA22
TA19
TA18
TA20
TA23
TA24
TA9
TA10
TA8
TA13
TA12
TA11
TA16
TA14
5G promise high throughput and ultra low latency in every where.
Analytics to assure low latency and throughput SLA
Densed traffic road
Use case requrimets
A self driving vehicle needs to stablish permanent connectivity with their operation center with the follow SLA
Throughput:
20 Mbps, symetrical
Round trip Latency:
5 milliseconds

## Slide 4: 5G Introduction Use case: Full self driving vehicle S2-2004299
Solution of maintaining a premium QoS across the network without using Analytics
TA1
TA2
TA3
TA4
TA6
TA7
TA5
TA15
TA17
TA21
TA22
TA19
TA18
TA20
TA23
TA24
TA9
TA10
TA8
TA13
TA12
TA11
TA16
TA14
Once the vehicle arrives to a cell’s coverage the network
Prioritizes vehicle’s traffic in that cell to sustain the QoS. The prioritization is done based on the Apps Id identified in that TA. No need to impact traffic in the rest of TAs
Once the vehicle left each cell, the cell is released of special traffic priority management.
Pros: Simplicity
Cons: Latency is not managed at all
Throughput may not be guarantee all time
SLAs can not be based on latency and throughput
In this solution the network react once the vehicle is detected by the cell

## Slide 5: 5G Introduction Use case: Full self driving vehicle S2-2004299
Analytics to assure low latency and throughput SLA
TA1
TA2
TA3
TA4
TA6
TA7
TA5
TA15
TA17
TA21
TA22
TA19
TA18
TA20
TA23
TA24
TA9
TA10
TA8
TA13
TA12
TA11
TA16
TA14
Assurance of QoS sustainability
TS 23.288 clause 8.9
NWDAF collecting Applications traffic info (per App Id) and predicting Cells occupation across the predefined mobility path
Reducing QoS for non-essential traffic (per App Id) assuring QoS sustainability & low latency previously to the vehicle arrives to the cell
Once the vehicle left each cell, the cell is released of special traffic priority management. Subscribers does not perceive the momentary de-prioritization of background traffics.
In this solution predictions are implemented to realize how much the background traffic in advance should be shaped in each cell
QoS is sustained (throughput and latency) all time without important disturbances of the regular customers.

## Slide 6: QoS Sustainability S2-2004299
Low latency use case
The QoS sustainability implementation requires analytics services of high performance; with low latency on data-collection and outcomes delivery.
The QoS sustainability implementation requires to consume analytics services of statistics related to Applications Id that are present and very short term predictions of occupation per TA.