3GPP TSG-SA WG2 Meeting #139E			S2-2003805

# June 01 - 12, 2020, Elbonia

Title:	Reply LS on NAS Non delivery for RRC Inactive state

Response to:	LS on NAS Non delivery for RRC Inactive state (S2-2003531 / R3-201362)

Release:	Rel-15

Work Item:	NR_newRAT-Core

Source:	SA2

To:	RAN3, CT4

Cc:

Contact Person:

#### Name:	Irfan Ali

E-mail Address:	irfaali (at) cisco (dot) com

Attachments:	-

SA2 thanks RAN3 about the LS on NAS Non delivery for RRC Inactive state (R3-201362). SA2 discussed the questions and agreed the following answers.

Q1/ RAN3 would like to ask SA2 to clarify the meaning of the above statement in TS 23.501 for the considered scenario and clarify whether option 1/ or option 2/ is the expected behaviour?

Ans 1: N1N2Transfer failure notification from AMF to SMF is not needed. Thus, NG-RAN node trigger of the NAS Non delivery procedure for PDU Session Release is not required. For PDU session Resource Release Command, there should be a PDU Session Resource Release response from RAN before UE context release occurs.

Q2/ In general, does SA2 see any other scenario for which the 5GC expects the NAS-non-delivery report in addition to those failed NAS-PDUs in the DL NAS Transport message?

Ans 2: For "Initial Context Setup Request" & "PDU Session Resource Setup" which have non-PDU session related NAS messages, indication from RAN of failure of these non-PDU session related NAS messages may be needed.  SA2 requests RAN3 to decide how to handle the failure notification to AMF of these non-PDU session related NAS messages.

SA2 will consider updates to their specifications based on RAN3 response.

2. Actions:

To RAN3 group:

ACTION: SA2 kindly requests RAN3 to take the above information into account. Also, SA2 kindly requests RAN3 to inform SA2 once they have a solution for the issue in Ans 2 above.

To CT4 group:

ACTION: SA2 kindly requests CT4 to take the information in Ans 1 above into account and update their specifications if needed.

3. Date of Next TSG-SA2 Meetings:

TSG SA WG2 Meeting  140		19 August - 2 September	Electronic meeting