## Slide 1: LS on which features cannot interwork with ETSUN
Nokia

## Slide 2: Related papers
4.1 | S2-2003549 | LS In | LS from CT WG4: LS on which features cannot interwork with ETSUN | CT WG4 (C4-202536)
4.1 | S2-2003706 | LS OUT | [DRAFT] Reply LS on which features cannot interwork with ETSUN | Nokia, Nokia Shanghai Bell
4.1 | S2-2004124 | LS OUT | [DRAFT] LS response on which features cannot interwork with ETSUN | Huawei,HiSilicon
4.1 | S2-2004125 | CR | 23.501 CR2375 (Rel-16, 'F'): Interworking between ETSUN and URLLC/TSN | Huawei, HiSilicon, China Mobile
4.1 | S2-2004126 | CR | 23.502 CR2322 (Rel-16, 'F'): Interworking between ETSUN and URLLC/TSN | Huawei, HiSilicon,China Mobile
4.1 | S2-2003705 | CR | 23.501 CR2371 (Rel-16, 'F'): URLLC - TSN interworking with ETSUN | Nokia, Nokia Shanghai Bell

## Slide 3: Background
CT4 asks SA2 to clarify which features cannot interwork with ETSUN add the clarification in relevant specification if needed, and to confirm in particular whether URLLC applies to PDU session with I-SMF.
Within input papers
  Following points seem to be agreed
    no support for TSN interworking with ETSUN
    Redundant User Plane Paths (23.501 § 5.33.2) is only supported when the UE is in the SMF service area (no ETSUN).
  For URLLC Different views on whether the QoS monitoring and dynamical CN PDB can be supported.
    Not supported because they require changes to N16a in order to carry QoS monitoring and dynamical CN PDB from SMF to I-SMF and because PDU Sessions with timing constraints do not fit with remote configurations related with I-SMF
    VS
    Features To be supported in ETSUN case. This is because only parameters need be transferred via the I-SMF and no special I-SMF function is required. For the dynamic CN PDB provision SMF can use the QoS monitoring measurement result to set the CN PDB and notify to NG-RAN.
  For NPN, TBD, as no requirement to I-SMF, by default it support.
  For other feature depending on whehter that feature add new requirment to I-SMF to determine whether it support or not.

## Slide 4: Proposed way forward
Proposed Way Forward: in this Release,
  WF1: QoS monitoring and dynamical CN PDB can be supported for PDU Sessions with I-SMF
  WF1 XOR (Either OR) WF2
  WF2: QoS monitoring and dynamical CN PDB cannot be supported for PDU Sessions with I-SMF
  WF3:
    no support for TSN interworking with ETSUN
    Redundant User Plane Paths (23.501 § 5.33.2) is only supported when the UE is in the SMF service area (no ETSUN).
  WF4: For other feature depending on whether that feature add new requirement to I-SMF to determine whether it support or not
SA2 139eCC#1 output: