## Slide 1: LS on which features cannot interwork with ETSUN
Nokia

## Slide 2: Background and related papers
CT4 asked SA2 to clarify which features cannot interwork with ETSUN and add the clarification in relevant specification if needed, and to confirm in particular whether URLLC applies to PDU session with I-SMF.
4.1 | S2-2003549 | LS In | LS from CT WG4: LS on which features cannot interwork with ETSUN | CT WG4 (C4-202536)
4.1 | S2-2003706 | LS OUT | [DRAFT] Reply LS on which features cannot interwork with ETSUN | Nokia, Nokia Shanghai Bell
4.1 | S2-2004124 | LS OUT | [DRAFT] LS response on which features cannot interwork with ETSUN | Huawei,HiSilicon
4.1 | S2-2004125 | CR | 23.501 CR2375 (Rel-16, 'F'): Interworking between ETSUN and URLLC/TSN | Huawei, HiSilicon, China Mobile
4.1 | S2-2004126 | CR | 23.502 CR2322 (Rel-16, 'F'): Interworking between ETSUN and URLLC/TSN | Huawei, HiSilicon,China Mobile
4.1 | S2-2003705 | CR | 23.501 CR2371 (Rel-16, 'F'): URLLC - TSN interworking with ETSUN | Nokia, Nokia Shanghai Bell

## Slide 3: TSN, redundant user plane Paths
Following points seem to be agreed thus Proposed way forward
WF1 : in this release
  no support for TSN interworking with ETSUN
  Redundant User Plane Paths (23.501 § 5.33.2) is only supported when the UE is in the SMF service area (no ETSUN).
SA2 139eCC#1 output:

## Slide 4: QoS monitoring and dynamical CN PDB
Different views on whether the QoS monitoring and dynamical CN PDB can be supported.
  (WF2) Features To be supported in ETSUN case. This is because only parameters need be transferred via the I-SMF and no special I-SMF function is required. For the dynamic CN PDB provision SMF can use the QoS monitoring measurement result to set the CN PDB and notify to NG-RAN.
  versus
  (WF3) No need to support theses features in ETSUN case: PDU Sessions with timing constraints do not fit with remote configurations related with I-SMF and these features do not come for free as they require changes to N16a in order to carry QoS monitoring and dynamic CN PDB from SMF to I-SMF
    No additional functionality is specified for URLLC in order to support Home Routed roaming scenario in this Release
Only one of following way forward to be endorsed: in this release
  WF2: QoS monitoring and dynamical CN PDB is supported for PDU Sessions with I-SMF
  WF3: QoS monitoring and dynamical CN PDB is not supported for PDU Sessions with I-SMF
SA2 139eCC#1 output:

## Slide 5: NPN
For NPN
  NID is neither defined for HR roaming nor is defined over N16. SNPN roaming etc… is for R17
  Complex NPN deployments could be deferered to R17
  BUT diverging views
Only one of following way forward to be endorsed: in this release
  WF4: no NPN interaction with ETSUN is defined.
  WF5: NPN interaction with ETSUN is defined.
SA2 139eCC#1 output:

## Slide 6: Other features
  WF5: In this release, any other feature (except the features defined in previous slides or features already documented in 23.501 / 23.502) that would add I-SMF requirements or induce N16a modification (wrt current April 2020 specifications) cannot be supported when an I-SMF needs to apply for a PDU Session; for a PDU Session needing such feature the SMF releases the PDU Session when an I-SMF has been inserted;
SA2 139eCC#1 output: