## Slide 1: Early UE capability retrieval for eMTC
Qualcomm Incorporated

## Slide 2: Related papers
4.1 | S2-2003575 | LS In | Action | LS from RAN WG2: LS on early UE capability retrieval for eMTC | RAN WG2 (R2-2003935) | Rel-16
4.1 | S2-2004188 | LS OUT | Approval | [DRAFT] Reply LS on early UE capability retrieval for eMTC | Qualcomm Technologies Int | Rel-16
4.1 | S2-2004189 | CR | Approval | 23.501 CR2377 (Rel-16, 'B'): Truncated 5G S-TMSI for early UE capability retrieval | Qualcomm Incorporated | Rel-16
4.1 | S2-2004193 | CR | Approval | 23.401 CR3603 (Rel-16, 'B'): Early UE capability retrieval support | Qualcomm Incorporated | Rel-16

## Slide 3: Background
RAN2 sent an LS in R2-2003935 with the following action for SA2:
  To consider feasibility of introducing enhancements to enable the (ng-)eNB for early UE capability retrieval for eMTC UEs connected to EPC and 5GC in Rel-16, and if confirmed feasible, specify the required changes based on truncated 5G-S-TMSI solution in their specifications.
For EPS support of early capability retrieval for eMTC is straightforward as the same procedure already exists for NB-IoT.
For 5GS it is important to highlight that even though RAN2 LS asks about eMTC UEs only, RAN2 assumes that truncated 5G-S-TMSIs will be used by all UEs in the call (“same UE identity shall be used by all UEs in the cell.”)
Various companies raised concerns during pre-e-meeting discussions on the reflector that this reduces the available AMF Set ID /Pointer/TMSI number space (due to truncation) for all UEs that connect to 5GC via E-UTRA.

## Slide 4: Proposed way forward
For EPS:
  Agree CR in S2-2004193 to clarify that Early UE capability retrieval is supported also for eMTC (note: it is already supported for NB-IoT).
For 5GS:
  Send a reply LS to RAN2 (see S2-2004188r01) to
    illustrate the concern on AMF Set ID/AMF pointer/TMSI number space if 5G-S-TMSI truncation was applied to all UEs connecting to 5GC via E-UTRA;
    confirm that AMF could provide the truncated 5G-S-TMSI configuration to LTE-M UEs;
    request RAN2 to evaluate whether it is feasible to enable ng-eNBs to determine whether the UE identifier signaled in Msg3 is a truncated 5G-S-TMSI or not and to inform SA2 accordingly.