SA WG2 Meeting #S2-139E	S2-200XXXX

01 - 12 June, 2020, Electronic, Elbonia

Source:	Interdigital

Title:	Evaluation for Solution #6: Layer-3 UE-to-Network Relay

Document for:	Approval

Agenda Item:	8.6

Work Item / Release:	FS_5G_ProSe / Rel-17

Abstract of the contribution: This contribution proposed an evaluation for solution 6: Layer-3 UE-to-Network Relay.

# 1	Proposal

It is proposed to add the following evaluation for solution #6 in TR 23.752.

* * * * First Change * * * *

# 7	Overall Evaluation

Key Issue#1:

-	Solution #6: Layer-3 UE-to-Network Relay:

-	The solution proposes a layer 3 solution for the support of UE-to-Network Relay. The UE-to-Network Relay acts as an IP router between the Remote UE and the 5GC, and provides Remote UE Report messages to the core network;

-	The solution works for both public safety services and commercial services;

-	The solution has no impact on the RAN;

-	The solution works when the UE-to-Network Relay connects to 5GC using NR/E-UTRA and also works when the UE-to-Network Relay UE connects to EPC using E-UTRA. The radio access type and core network type are agnostic to the Remote UE.

* * * * End of Change * * * *