## Slide 1: FS_MUSIM CC agenda and rapporteur’s summary of way forward proposals
Intel

## Slide 2: FS_MUSIM CC Agenda (06 Aug 2020)
Way forward contributions to be presented in the order of submission
    LG Electronics
    Intel
    Samsung
    Huawei
    MediaTek
    Ericsson
    Qualcomm
    Charter Communications
    vivo
  Other contributions
    Vodafone

## Slide 3: Summary of way forward proposals
Company | KI#1 | KI#2 | KI#3
LG Electronics | Paging Cause (Sol#1) plus Filtering Rules. Solutions w/o RAN impact (Sol#7, Sol#12) should be supported. | Solutions with RAN impact to be considered by RAN. Solutions w/o RAN impact (Sol#7, Sol#12) should be supported. | NAS-based
Intel | Paging Cause (Sol#1) and Push Notif (Sol#7) for solutions with and w/o RAN impact. Decide later whether both are needed. Send LS OUT to RAN (“busy message”) and SA3 (privacy). | 5GS: MRU with no Assistance Info (Sol#20), or possibly with AI (Sol#14). Confirm with RAN. EPS: UE ID offset (Sol#16). | 5GS: RRC-based. Confirm local release with RAN EPS: NAS based
Samsung | Paging Cause (Sol#1) as baseline solution. Other solutions can be discussed on case by case basis. | Leave solution to RAN. If needed, SA2 will align | EPS: NAS-based Sol#5. 5GS: NAS-based Sol#5 + any RRC solution deemed necessary by RAN Feedback from RAN2 on “short duration leaving”.
Huawei | No solution needed in SA2. Solutions where UE is allowed to ignore paging are not acceptable | Leave solution to RAN. If needed, SA2 will align (e.g. any assistance for Sol#18 – consecutive POs) | RRC-based (Sol#6). No solution for EPS?
MediaTek | Paging Cause (Sol#1). No need for « busy msg » (but can be discussed in RAN) | 5GS: MRU with no Assistance Info (Sol#20), or possibly with AI (Sol#14). Confirm with RAN. | 5GS: RRC-based (Sol #22) EPS: NAS-based
Ericsson | Paging Cause (Sol#1). Network may use UE-provided Assistance Info (which solution?) | Request RAN feedback on UE-steered POs, implementation-based, gap-based and paging in consecutive POs | NAS-based as baseline and optionally RRC-based « when Inactive supported and it is NR » (why not for 5GC/E-UTRA?)
Qualcomm | Paging Cause (Sol#1). RAN to decide on “busy message” | Issues with NAS-based solutions. Prefers RAN-only solution. Send LS OUT to RAN2 before concluding | Sol#5 as baseline. NAS solution for both EPS and 5GS. Confirm local release with RAN. Both RRC- and NAS-based for 5GS?
Charter Communications | Paging Cause (So#1) | Leave solution to RAN | Both NAS- and RRC-based. Is RRC-based also for EPS?
Potential interim conclusions? | Paging Cause? Continue work on solutions w/o RAN impact? Send LS OUT to RAN (“busy message”) and SA3 (privacy). | Request RAN feedback for selected solution principles. Continue work on solutions w/o RAN impact? | NAS-based for EPS and RRC-based for 5GS? Request RAN feedback on “short duration leaving” and “RRC local release”