## Slide 1: Proposed way forward for MUSIM Key issue#3 (Coordinated leaving for Multi-USIM device)
Samsung

## Slide 2: High level requirements for Key issue#3
For EPS no changes in access stratum are expected as per the MUSIM RAN SID.
When UE is leaving the network it can be for:
  Short duration:
    UE shall precisely know what is the longest duration it will not be available with current network for example to read paging message on target system, perform periodic TAU etc.
    Its reasonable to expect UE to remain in connected state for short duration leaving. The network block to send data to the UE during this short period.
    As its for a short duration and UE is expected to remain in connected mode, in our view keeping NAS unaware could be good way forward. i.e. using AS based procedure.
  Long duration:
    UE have no idea for how long UE is leaving source system or time duration is long.
    Its reasonable to expect UE to be moved to IDLE mode or INACTIVE state by source system.

## Slide 3: Discussion:
For EPS:
Because of requirement 1, it becomes imperative that NAS based solution is progressed in SA2 at least for EPS. Thus we propose NAS based solution is selected as a way forward for EPS.
For 5GS:
In our view, its preferable to have common solution between 5GS and EPS (from maintenance and development perspective) thus we propose to select NAS based solution in 5GS too for long duration leaving.
Additional optimizations, for short duration leaving(when UE will remain in connected mode) can be explored by RAN WG so that NAS is unaware of complete process. Action item will be on RAN WG.
Following the above discussion from SA2 perspective, we have only sol.4 (NAS based) and sol.5(NAS based) as a possible way forward candidates for Interim agreements in SA2#140e. We provide the comparisons from our perspective between this two solutions in Annex A and propose the way forward in next slide.

## Slide 4: Way forward for KI#3
We propose to:
  Select solution.5(Graceful NAS based leaving and resumption) as a way forward for interim agreement for KI#3; and
  Send an LS to RAN WG2 with requirements for “short duration leaving” in the SA2#140e meeting.

## Slide 5: Annex A

## Slide 6
We have slight preference for Sol.5(NAS) over Sol.4(NAS) for following reasons:
Its graceful. Future compatibility to include any critical IEs will have no problem.
Response message is provided in connected mode and then release, thus time difference comparatively is negligible.
If type of service pending is not critical, the UE may retry to send the message if no acknowledgement for the sent message is received.
If no response message is received, UE may do local release and go to target system at least in this case UE is aware that source network is not aware of UE leaving. UE may decide to comeback in its first opportunity.