## Slide 1: Way forward on “LDNSR placement ”
Hui Ni (Rapporteur)

## Slide 2: Background
Solution 22 uses a “LDNSR” to:
  1) receive DNS queries from UE
  2) obtain ECS option/L-DNS server IP from the SMF
  3) insert ECS option into DNS query then send to other DNS servers for EAS resolve, or, send a DNS query to L-DNS server for EAS resolve
  4) trigger SMF to perform ULCL/BP insertion
Solution 22 is proposed by multiple companies as conclusion of DNS based EAS discovery in session breakout case. But one key EN on LDNSR placement should be resolved:
  Editor's note: It's FFS whether the LDNSR can be integrated into SMF or UPF.
3 papers updated solution 22 with different options
  S2-2004963(Ericsson) assumes LDNSR is in SMF
  S2-2005048(NTT DCM) assumes LDNSR is a standalone NF
  S2-2005364(Huawei) assumes LDNSR is in UPF
Pros/cons of each option are analyzed in
  Ericsson S2-2004955
  DCM S2-2005046
  CMCC S2-2005195
  HW S2-2005364
  VDF S2-2005855
C-DNS server
UE
L-DNS resolver
SMF
(1)
LDNSR
Remote PSA
ULCL/BP
(2)
Local PSA
Option 1
Option 2
Option 3
(3)
Obtain ECS option
Trigger ULCL insertion
L-DNS Server

## Slide 3: Way forward proposal
Show-of-hands on LDNSR placement in CC#2
  Option 1: LDNSR in SMF
    Support:
    Object:
  Option 2: LDNSR as standalone AF
    Support:
    Object:
  Option 3: LDNSR in UPF
    Support:
    Object:
Update solution 22 based on the majority position:
  If option 1 is agreed, take S2-2004963(Ericsson) as baseline for solution 22 update.
  If option 2 is agreed, take S2-2005048(NTT DCM) as baseline for solution 22 update.
  If option 3 is agreed, take S2-2005364(Huawei) as baseline for solution 22 update.
whether the show-of-hands is needed depends on the email discussion before CC#2