## Slide 1: FS_MUSIM evaluation and conclusions
Intel
SA2#140E, Electronic meeting, 12 – 23 October 2020
S2-2007085

## Slide 2: Outline
Conclusion proposals for KI#1, including aspects that were not handled in SA2#140E:
    Notification type of solutions (7, 8, 12, 13, 27)
    MUSIM (Release) Assistance Information (content and whether/how/when it is used), paging filtering (content and whether/how/when it is used)
    Different Paging Cause values based on Caller ID (9)
    Upper bound timer (11)
    Optimizations for “on the same network” (24, 26)
    Optimizations in presence of non-3GPP access (23, 25)
  Revisited KI#1 conclusion
  Revisited KI#3 conclusion

## Slide 3: Notification type of solutions (1/3)
Solution #7 | Solution #7 additionally addresses "Key Issue 2: Enabling Paging Reception for Multi-USIM Device". The solution is based on the deployment of an internet facing IP based service protocol that the UE accesses via the current serving network to receive push notifications of paging. The protocol used for the push notifications is to be defined. The UE must maintain a connection to the paging server via the serving network while it is in CONNECTED. The protocol used for paging via the paging server is not defined. The details of the authentication are to be defined. The NAS layer in the UE has to support IP communications and be triggered to respond to paging based on traffic via IP. The solution requires paging the UE in network A and after some delay via network B. If the UE monitors paging in both networks, there is a possibility that the UE does not receive either paging. If the UE only monitors paging in network B, the UE can receive the paging. The solution introduces some delay for paging and paging resource wastes. The MNO has to maintain a new internet facing service for the UEs to register with. The AMF/MME in the network also has to connect to the external facing server. It is not defined what protocol is used for the AMF/Paging Server. When actively communicating with one network the UE does not need to listen to paging in the other network. The solution prevents unnecessary interruptions of the current service to receive paging. The user, depending upon service plan from serving network, may be charged by the serving network for the data required for the paging server i.e. control plane signaling in one network (typically not charged to the end user) may end up being charged to the user in the other network. The solution has UE and core network impacts. It requires deployment of a paging server as well as necessary secure interactions between this server, the UE and the network. | Impacts UE, AMF New entity: Paging Server | Editor's note: The security aspects of the communication between UE and Paging Server, including the details for the assignment of UE identity and credential which enable the UE to establish a secure connection with the Paging Server via the Internet, as well as any privacy issues, will be addressed by SA WG3.
Solution #8 | This solution uses N3GPP access to register with an N3IWF on the non-serving network and a new paging indication is sent via the N3GPP service to inform the UE about paging. The AMF can determine whether the UE is reachable via the 3GPP access based on the N3GPP registration. Additional information to enable paging filtering by the network for each PDU Session may be provided. The solution requires the UE to support N3GPP access and register and maintain a connection to the N3IWF while the UE is in CONNECTED on the serving network. The solution may prevent unnecessary interruptions of the current service and the level of service differentiation is at the PDU Session level. Depending upon how services map onto PDU Sessions broad categories for how the user/UE determines what is unnecessary may only be possible. The solution prevents unnecessary interruptions of the current service to receive paging. The user, depending upon service plan from serving network, may be charged by the serving network for the data required for the N3GPP access. The solution has UE and core network impacts. It requires deployment of N3IWF as well as necessary (secure) interactions with the UE and the network. | Impacts UE, AMF New entity: Paging Server | Editor's note: Further clarifications on how UE determines the time period and MUSIM- RAI are FFS. For example, are they determined based on the set of active services on USIM1? Does this information need to be updated to PLMN2 whenever there is a change in the set of active services on USIM1?. Editor's note: the details of the NAS procedures are FFS. Editor's note: the details and its related charging aspect of the PDU session that provides UP in PLMN 1 is FFS.

## Slide 4: Notification type of solutions (2/3)
Solution #12 | Solution #12 additionally addresses "Key Issue 2: Enabling Paging Reception for Multi-USIM Device". When the UE is paged, if there is no response an SMS is sent to the UE using MSISDN of the serving network. The UE has to provide the non-serving network with the MSISDN the UE uses on the serving network. There may be privacy issues with providing the non-serving network the MSISDN from the serving network. SMS is not a time critical service therefore the SMS based paging notification maybe delayed without warning. The solution requires paging the UE in network A and after some delay via network B. If the UE monitors paging in both networks, there is a possibility that the UE does not receive either paging. If the UE only monitors paging in network B, the UE can receive the paging. The solution introduces some delay for paging and paging resource wastes. The NAS layer in the UE has to support being triggered to respond to paging based on receiving SMS messages from another network. The solution does not introduce any mechanisms for the UE to perform any activity with the other network that is not actively communicating with (e.g. listen to paging, respond to paging, perform mobility update etc.), however the UE does not need to listen to paging. The solution may prevent unnecessary interruptions of the current service but only for very broad categories for how the user/UE determines what is unnecessary (i.e. voice call but not who from, data arrival but not what etc.). The service categories and how they are determined is not defined. The solution may not prevent paging escalation, as the SMS may be delayed. The user, depending upon service plan from serving network, may be charged by the serving network for paging notification SMS. The solution has UE and core network impacts. | Impacts UE, AMF, NEF | Q3 (S2-2006011): Please confirm whether from security perspective you see any blocking issues for the principle of Push Notification via SMS and please provide feedback on the use of the USIM credential to validate the SMS carrying the Push Notification and any privacy issue due to exposing MSISDN to other operator.
Solution #13 | The solution targets asymmetric scenarios where a "serving" network provides data services and a "non-serving" network provides IMS voice and SMS-over-IMS. It does not intend to support data services on the non-serving network. The UE registers with the non-serving network via its ePDG/N3IWF using an IP connection through the serving network. Prior to registering the UE detaches/enters MICO mode on the non-serving network. When a MT IMS voice call or SMS is received, SIP signaling is initiated towards the UE via the ePDG/N3IWF. The solution relies on existing mechanisms (e.g., paging) when in IDLE mode in the serving network to inform the UE of MT services on the non-serving network. The solution prevents unnecessary interruptions of the current service to receive paging and to respond for non-serving network's IMS voice and SMS services. When the user accepts the voice call from the "non-serving" network, the media plane can be established over the top of the "serving" network or directly over 3GPP access in the "non-serving" network. In the case of the media plane being established directly over the 3GPP access (step 10A in Figure 6.13.3-1) the "non-serving" network temporarily becomes the "serving" network for the duration of the voice call and the solution does not explain how MT services on the previous "serving" network are handled. Charging records may be generated by the serving network for the data required. The solution has UE and core network impacts. | Impacts UE, SCC AS (T-ADS?) | Editor's note: SA WG5 will need to be involved if any IMS user and control plane traffic is sent over a PDU session that is carrying data traffic.

## Slide 5: Notification type of solutions (3/3)
Solution #27 | Similar evaluation as Solution #7 with the following differences: Different security mechanism for the user plane connection between UE and Paging Server Choice of « Master PLMN » which allows the AMF in the « non-master PLMN » to immediately send Push Notification without trying to page the UE first. Hence, in comparison to Sol #7 there is no delay and waste of paging resources | Impacts UE, AMF New entity: Paging Server | 
Comments
    The solutions address both KI#1 and KI#2
    Potential issues with charging of IP traffic for the Push Notifications or the SMS by the serving network (applies to all solutions)
    Paging delay and waste of paging resources (Sol#7 and Sol#12)
    Pending exchange with SA3 on any privacy issues (Sol#7 and Sol#12)
    Information granularity in the Push Notification comparable to Paging Cause (except for Sol#13)
    Asymmetric solution (Sol#13)
    Other unresolved Editor’s notes (Sol#8)
  Proposal 1: Whether Push Notification type of solutions are to be pursued for normative work in Rel-17 will be decided in SA2#142E (Nov 2020).

## Slide 6: MUSIM (Release) Assistance Information (Sol #5, Sol#10) (1/2)
Comments
    MUSIM (R)AI proposed for both KI#1 and KI#3.
    Unresolved content: “PDU Sessions” or “MT services” (with PPI granularity?)
    Can UE always determine the time period for the leave?
    What about MO procedures (e.g. periodic TAU)?
Solution #10 (KI#1) | The solution uses PPI to enable the network to filter paging for the UE. The UE provides the rules for filtering in the Registration procedure. When the network pages the UE, the network determines whether to page based on the PPI and filtering rules provided by the UE. The filtering rules are expected to be coarse (voice, data, SMS etc.). How and when the filtering rules are updated is not defined. The rules apply at all times including when the UE is in IDLE or CONNECTED on the serving network, therefore incoming services maybe filtered whether needed or not. A more dynamic update from the UE will introduce significant additional signaling and it is not clear how that signaling interacts with the state of the serving network. While performing the establishment of new filtering rules, some service interruption may occur in the other USIM (depending upon service).If the filtering is only updated when the UE leaves the network some overhead ay be reduced. The solution may prevent unnecessary interruptions of the current service but only for very broad categories for how the user/UE determines what is unnecessary (i.e. voice call but not who from, data arrival but not what etc.). The solution requires the UE to respond to paging and avoids the network to page services that are filtered out, thus preventing paging escalation (under normal conditions). The solution makes the UE unreachable for services that are filtered out. The solution has UE RAN and core network impacts. The solution may require user interaction and related MMI impacts are expected.
Solution #5 (KI#3) | The optional Release assistance info for MUSIM is used to assist the network to handle the MT data and decide whether to trigger paging to the UE during the UE leaving. In the MUSIM-RAI as described in solution#5, it states that the UE decides "PDU sessions that the UE want network to trigger (or not trigger) MT service delivery indication". In general, the PDU session can carry different kind of services. Further clarification is needed on which scenario can be applied for not delivering the data of the whole PDU session and how the UE make a decision on it. In current MUSIM-RAI as described in solution#5, it is also proposed "Services that the UE wants network to trigger (or not trigger) MT service delivery indication" and "no MT data shall be delivered at all" (e.g. due to specific service in another network and can't answer paging request). The network can discard/block MT data or attempt normal MT service delivery and paging based on the MT service. In current MUSIM-RAI as described solution#5, it is also proposed "The time period expected by the UE that will be away from this serving network".

## Slide 7: MUSIM (Release) Assistance Information (Sol #5, Sol#10) (2/2)
Comments
    MUSIM (R)AI should be considered only for KI#3 (otherwise it is a Do Not Disturb feature and is not MUSIM-related)
    The use of “PDU Sessions” may not be useful due to the mix of services provided via the same PDU Session (e.g. IMS)
    If “MT services” are defined with PPI granularity, then the only practically identifiable service seems to be “voice”
    In certain scenarios the UE can estimate the absence duration (e.g. pick up a MT SMS or perform Periodic TAU in the other network) or can determine that it is potentially a long absence (e.g. when paged for “voice”)
      The UE would need to have an indication of the MT service (e.g. “SMS”, “voice”) to determine whether the absence is long or short
    How can the network use the information about “short absence” or “ page me for voice only”
      If UE indicates “page me for voice only” when leaving, the network may decide to:
        Suspend the user plane immediately
        Page the UE only for MT “voice” service, but not for other types of MT service
      If UE indicates “short duration”, the network may decide to not suspend the user plane data
      For cases where the UE does not provide an indication, the network can use a guard timer before suspending the user plane
Proposal 2: Support indication of “page me for voice only” and “short duration” as part of the Leaving procedure.

## Slide 8: Different Paging Cause values (Sol #9)
Comments
    Add-on to Paging Cause
    Unresolved Editor’s note on whether the solution works in roaming case. To make it work, specific roaming agreement needed
    May have privacy issues
  Proposal 3: Different Paging Cause values based on the Caller ID will not be pursued for normative work in Rel-17
Solution #9 | This solution is intended to be used in addition to solution #1 to filter paging into different groups based on the incoming callers identity. The identities are provided to the non-serving network to enable the grouping and each of the groups provide a different paging cause to the UE. There may be privacy issues providing the grouping of preferred and non-preferred for each incoming caller to the network. The additional benefit of grouping by preferred and non-preferred is not clear. The total number of groups is unclear as some identities may not be included is either of the groups and the behaviour in this case is not clear. The solution has UE and core network and IMS services impacts. The solution requires user interaction to determine the callers identities and whether preferred/not preferred and to update the settings in the network. Additional MMI impacts are expected. | Impacts UE, P-CSCF, TAS (on top of Paging Cause Sol#1 impact) | Editor's note: it is FFS whether this solution can work if there is no guarantee the DSCP cannot change between TAS and UPF in transport networks outside operators control between TAS in HPLMN and the P-CSCF in VPLMN. Impact on IPX especially is to be considered in roaming case and any requirement on NG.113 by GSMA shall be specified.

## Slide 9: Upper bound timer (Sol #11)
Comments
    Add-on solution. Does not propose additional information in paging
    Complements Busy Indication (Sol#3) by providing upper-bound timer for UE to send the Busy Indication
    Unclear whether this timer needs to be negotiated or whether it can be fixed
  Proposal 4: If Busy Indication is pursued for normative work, it is left to CT1 to determine whether a fixed or dynamically signalled Upper bound timer value is to be used.
Solution #11 | This solution adds an upper time bound for when the UE must respond to (NAS) paging and provides a response to paging to inform the paging network that the UE/user has received the page but does not want to / cannot fully respond at this time. No additional information is proposed in paging. The solution does not prevent unnecessary interruptions of the current service (service dependent), as it requires the UE to respond, however the response may be delayed for a period of time. The solution prevents paging escalation (under normal conditions). The solution is expected to only need a short duration gap. The solution has UE and core network impacts. | Impacts UE, AMF | 

## Slide 10: Optimizations for “on the same network”
Solution #24 | When the two UEs are served by the same serving network and by the same AMF, the AMF uses NAS Notification over UE1 to deliver the indication of MT service to UE2. AMF reallocation can be used to force the two UEs to “land” on the same AMF, which creates additional signalling. The solution can potentially save paging resources relying on NAS Notification instead. The solution can potentially extend battery life by allowing the UE to not monitor the paging channel, however there is no quantitative analysis provided. | Impacts UE, AMF | Q4 (S2-2006011): Please confirm whether from security perspective you see any blocking issues in this solution: The registration request message of UE-2 includes the GUTI of UE-1. The UE-1 and UE-2 are part of same MUSIM UE. Editor's note: The handling for the case of different AMF and if there is any impact due to mobility restriction is FFS.
Solution #26 | Similar to Sol#24 with the addition that solution addresses also the scenario where the two UEs are served by different AMFs. In this case the two AMFs exchange signalling to link the two UE contexts. When AMF1 needs to page UE1 in Idle state, it first checks the linked UE (UE2) state and if the latter is in Connected state, AMF1 delivers the NAS Notification intended for UE1 via AMF2 and and UE2. This creates additional complexity and signalling. | Impacts UE, AMF | The same Editor's notes should apply as for Sol#24
Comments
    Optimization that works in a specific case
    Pending exchange with SA3. Can we make a decision based on other criteria (not security related)?
    Noting that there is a need for a solution that works in all scenarios (not only when the two UEs are served by the same AMF) it is questionable whether the additional benefits (saving paging resources, extended battery life) are worth the additional complexity.
  Proposal 5: The optimizations for “on the same network” are not pursued for normative work in Rel-17.

## Slide 11: Optimizations in presence of non-3GPP access
Solution #23 | This solution is applicable only when UE is in coverage of N3GPP access and therefore cannot be considered as a complete solution for KI#1 and KI#3. Based on MUSIM policy received from the PCF the UE preferably establishes PDU Session over non-3GPP access and/or uses MA PDU Session. | Impacts UE, AMF, PCF, SMF | 
Solution #25 | This solution is applicable only when UE is in coverage of N3GPP access and therefore cannot be considered as a complete solution for KI#1. After AMF learns that UE has left 3GPP access based on NAS leaving or RRC leaving procedure, and if the AMF has another N1 registration with the UE via non-3GPP access, the AMF shall use NAS Notification for MT service delivery | Impacts UE, AMF | Editor's Note: Whether and how to handle the scenario where the UE is registered over 3GPP and non-3GPP access in different PLMNs is FFS.
Comments
    Optimizations that work in a specific case
    Sol#23: Unclear why the UE needs to receive MUSIM-specific policy in order to establish a PDU Session over non-3GPP access. Couldn’t this be done by implementation?
    Sol#25: This seems to be simply an additional condition on AMF behaviour.
  Proposal 6: Clarify AMF behaviour for the specific case where UE has performed NAS/RRC leaving, while it has a non-3GPP registration in parallel.

## Slide 12: Summary of proposals
  Proposal 1: Whether Push Notification type of solutions are to be pursued for normative work in Rel-17 will be decided in SA2#142E (Nov 2020).
  Proposal 2: Support indication of “page me for voice only” and “short duration” as part of the Leaving procedure.
  Proposal 3: Different Paging Cause values based on the Caller ID will not be pursued for normative work in Rel-17.
  Proposal 4: If Busy Indication is pursued for normative work, it is left to CT1 to determine whether a fixed or dynamically signalled Upper bound timer value is to be used.
  Proposal 5: The optimizations for “on the same network” are not pursued for normative work in Rel-17.
  Proposal 6: Clarify AMF behaviour for the specific case where UE has performed NAS/RRC leaving, while it has a non-3GPP registration in parallel.

## Slide 13: Revisited KI#1 conclusion
Among the KI#1 solution principles the following principles at least shall be considered for further evaluation:
    A Paging Cause for both EPS and 5GS indicating at least “voice” and “SMS” service, pending RAN and SA3 feedback.
      Editor’s note: It will be further confirmed with RAN2 whether a value “other service” is needed to allow the UE to discriminate between gNBs supporting the Paging Cause from those that do not.
      Editor’s note: It will be determined whether the Paging Cause is applied only for UEs that have indicated MUSIM capability or to all UEs indiscriminately.
    A Negotiated Short Absence for 5GS, evaluated together with RRC-based coordinated leaving, pending feedback from RAN WGs.
    A Busy indication pending feedback from RAN WGs and SA3. If Busy Indication is pursued for normative work, a fixed Upper bound timer value will be used (to be defined by CT1).
    When AMF is aware that UE has left 3GPP access using the procedure for coordinated leaving, and if the UE has a non-3GPP registration with the same AMF, the AMF shall use the NAS Notification procedure for MT service delivery
Different Paging Cause values based on the Caller ID (as in Sol#9) will not be pursued for normative work in Rel-17.
The optimizations for “on the same network” (as in Sol#24 and Sol#26) are not pursued for normative work in Rel-17.

## Slide 14: Revisited KI#3 conclusion
Change the following:
    UE may provide information to the network in the leaving procedure regarding MT data/signalling handling in the CN. The details of this information and of the MT data/signalling handling in the network (with or without assistance info) are FFS.
Into the following:
    UE may provide assistance information to the network in the leaving procedure regarding MT data/signalling handling in the CN. The assistance information may include the following:
      an indication that the UE is leaving for a “short duration”, or
      an indication that the UE would like to be paged for “voice“ service only