## Slide 1
Discussion on LDNSR placement
Source: Huawei, HiSilicon
Title: Discussion on LDNSR placement
Document for: Discussion
Agenda Item: 8.3
Work Item / Release: FS_enh_EC / Rel-17

## Slide 2: Background
For KI#1, Solution 22 is proposed by multiple companies as conclusion of DNS based EAS discovery in session breakout case. One key EN on LDNSR placement needs to be resolved:
Editor's note: It's FFS whether the LDNSR can be integrated into SMF or UPF.
In SA2 #140E meeting, it was agreed the group should continue discussing on whether option 2 or option 3 should be selected as conclusion.
  Option 1: LDNSR in SMF
  Option 2: LDNSR as standalone AF, may be collocated with PSA UPF
  Option 3: LDNSR in PSA UPF
  Option 4: DNS proxy in SMF, Decryption in UPF

## Slide 3: LDNSR as standalone AF
SMF
NEF
UE
C-DNS
Remote PSA
L-DNS
ULCL/BP
DNS Query
Local PSA
LDNSR AF
LDNSR as a standalone AF
  The LDNSR is a standalone NF.
  From 5GC User Plane point of view, the LDNSR is a standalone UP entity that performs the role of DNS Resolver.
  From 5GC Control Plane point of view, the LDNSR acts as AF to invoke services from the SMF. For this purpose the LDNSR AF needs to hold a PDU session state.
Procedures to support LDNSR as a standalone AF
  The LDNSR, acting as AF, subscribes to the NEF to “PDU Session Status” events for the UE using the GPSI as described in clause 6.22.2.1.
  At PDU session establishment, the SMF notifies the LDNSR AF (without involving NEF or PCF) on PDU Session Status including SMF ID and UE IP address.
  The LDNSR AF contacts the SMF using its SMF ID in its PDU Session context.
Central Site
Local Site
PDU Session Status including SMF ID and UE IP address

## Slide 4: LDNSR as part of PSA UPF
LDNSR as part of PSA UPF
  Configure UE with the address of LDNSR as the DNS server during PDU session establishment via PCO.
  Considering the Remote PSA will not be changed during the lifetime of PDU session, it is proposed that the functionality of LDNSR is integrated with Remote PSA.
    Additionally, the Remote PSA as LDNSR has no impact on the UE in case of UL CL. Otherwise, if Local PSA is configured as the DNS server to the UE, the address of DNS server sent the UE need to be updated upon the insertion or removal of UL CL.
  Extend N4 messages for interaction between LDNSR and SMF.
SMF
UE
C-DNS
Remote
PSA
L-DNS
ULCL/BP
DNS Query
Local PSA
LDNSR
Central Site
Local Site

## Slide 5: Details on “LDNSR as part of PSA UPF”
Procedures to support LDNSR as part of PSA UPF, mainly abstracted from solution 22, further optimization may be discussed later:
  During AF influence traffic routing procedure, the AF may provide EAS deployment information including FQDNs, IP addresses/prefixes, Local DNS server IP address per DNAI.
  The PCF provides the SMF with a PCC rule that is generated based on the AF request. The PCC rule includes the following information:
      Option 1: The mapping relationship between the DNAI and the ECS option(IP address accessing to edge computing platform for N6).
      Option 2a: The address of Local DNS server serving each DNAI.
      Option 2b: The forwarding rule for DNAI which has no direct connectivity to LDNSR.
  Based on the PCC rule and UE’s location, the SMF instructs the LDNSR how to handle DNS message via the N4 session during PDU session establishment.
      The SMF indicates LDNSR to perform DNS packet detection based on the e.g. destination address, destination port number and FQDNs by providing Packet Detection Rules (PDR) as defined in the Clause 5.8.2.11.3 from TS 23.501.
      The SMF also provide to the LDNSR a Forwarding Action Rules (FAR) as defined in the Clause 5.8.2.11.6 from TS 23.501 to trigger the action applicable to the DNS packet, such as adding ECS option or forwarding the DNS packet to the L-DNS server, which depends on the options listed in the Solution#22.
Clause 4.3.6 Application Function influence on traffic routing in TS 23.502
FQDNs, IP addresses/prefixes, Local DNS server IP address per DNAI.
PDR and FAR for DNS packet

## Slide 6: Issues for LDNSR as a standalone AF
Only one LDNSR per DNN+S-NSSAI may not be sufficient for big operators, it is not clear how it works with multiple LDNSRs.
The LDNSR needs to subscribe PDU session status before the PDU session is established. i.e. the subscription is performed before the SMF selects a LDNSR for the PDU session. It’s not clear how to guarantee the selected LDNSR has already subscribed the PDU session status of the same UE.
UDM needs to keep PDU session status subscription for all UEs that may use EC services.
The “PDU Session Status” events subscription requires the GPSI is mandatory for UE. For UE without GPSI, how to subscribe the “PDU Session Status” is FFS.
SMF
NEF/UDM
UE1
Remote PSA
L-DNS
ULCL/BP
DNS Query
Local PSA
LDNSR AF1
Local Site
LDNSR AF3
LDNSR AF2
UE2
UE3
1. Subscribes PDU session status for UE 1
2. Selects LDNSR for UE 1

## Slide 7: Proposal
It is proposed to place LDNSR as part of PSA UPF.
The corresponding changes are proposed in S2-200xxxx.