## Slide 1
Source: Nokia, Nokia Shanghai Bell, Ericsson
Title: Key Issue 3 “Network Information Provisioning to Local Applications with low latency”
Document for: Discussion
Agenda Item: 8.3
Work Item / Release: FS_enh_EC / Rel-17

## Slide 2: Key Issue 3 “Network Information Provisioning to Local Applications with low latency”
  Current status.
  The current work done so far has focused on how to deliver information but not on which information to provide
  The solution endorsed limits the information being delivered to R16 Qos Monitoring information, which is latency of UE<->UPF
  Applications need QoS information that is averaged over time
    Otherwise they would over-react to instantaneous QoS values leading to service and network instability
  R16 supports delivery of QoS info to App
    Inband as packet drops or ECN (tag in IP header so in User Plane)
    Via notification Control (SMF is notified. May modify QoS. AF is informed over Npcf so in Control Plane)
    Via QoS Monitoring (RAN-UPF measurements to SMF to PCF to AF via Npcf? so in Control Plane)
  There is no proposal stating what information is needed by applications and how low latency for this information should be
    No example application use case has been presented showing benefits
  What is the need to add to R16 considering that Mechanisms defined as part of KI 3 would deliver the same (QoS) information with similar delay
    As (QoS) information is to be time-integrated (order of magnitude a few Seconds) sending directly from UPF to local NEF (instead of sending via SMF and PCF) does not really provide a lower latency

## Slide 3: Key Issue 3 “Network Information Provisioning to Local Applications with low latency”
  Re-16 QoS Monitoring Reporting recap
    Supports calculation of uplink/downlink and RTT in UPF
      GTP ECHO requests for the GTP path ( or in band packet marking) and RAN reporting of UE-NG-GRAN delay measurements
    The Re-16 QoS Monitoring reporting can be periodic or event/threshold based
      The frequency for periodic reporting is enumerated in seconds
      If event/threshold based reporting is used there is a minimum wait time between subsequent reports, the minimum wait time is enumerated in seconds
UE
NG-RAN
UPF
CN-CP
Local NEF
Measure
Measure
Report
?
UPF measures and calculates the path delay and RTT and reports with a maximum frequency of once a second
AF

## Slide 4: Proposal
  To agree on the TR 23.748 conclusions documented in Tdoc S2-2008484