Pre SA2#143E e-meeting Email Discussion

Source: 	<Jinguo Zhu/ZTE>

Title: 	<Email discussion on FS_eNS_Ph2>

# 1.	Issues for FS_eNS_Ph2

## 1.1	Key Issue #3: limitation of data rate per network slice in UL and DL per UE

### 1.1.1	Issue Description

For key issue 3 we have categorized the solutions into 3 categories

-	Category A1: Those enforcing the Slice-MBR in the UPF, in CN i.e. solution #13.

-	Category A2: Enforcing SMBR in the RAN and also admitting GFBR aggregate for the slice only up to the SMBR at the admission control time in the RAN, i.e. solution #22,

-	Category B: Those ensuring that the Slice-MBR limits the aggregated MBR and GBR for QoS flows of established PDU sessions and related QoS flows, i.e. solution #20, #21 and #37. Enforcement is done using the existing QoS parameter

### 1.1.2	Companies View

Question 1) Whether UPF based solution (Category A1) should be supported for KI#3。

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| Nokia | NO | It is not so that UPFs can always be shared across UPFs |
| Ericsson | No | Enforcing the Slice-MBR in the UPF may require same UPF is selected. It is difficult to foresee the selection of same I-UPF/UPF for all PDU sessions in a slice, since it is possible to have different UPFs towards different DNNs, for example, towards IMS and internet. |
| Samsung | No | It is hardly foreseen to use the same UPF for differerent DNNs. |
| AT&T | NO |  |
| NTT DOCOMO | No |  |

Question 2) Whether RAN based solution (Category A2) should be supported for KI#3:

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| Nokia | YES | It is the solution that allows UL and DL control similarly to UE AMBR. |
| OPPO | Yes | The slice-AMBR can be enforced similarly to UE-AMBR. |
| Ericsson | No | Feedback from RAN WGs needs to be considered before any agreement can be made. UL Slice-MBR enforcement, without dropping packets, in RAN using existing mechanisms is not feasible. A RAN based solution would make the scheduling at RAN level inefficient, and it would require RAN to drop packets already transmitted over the air. UL rate-shaper/policer in the gNB or CN could enforce a per-slice MBR provided that the application and transport protocol are responsive to congestion signals (packet loss/drop), but as that cannot be assumed it is preferred to not perform such packet drop in UL by NG-RAN. Only a UE based rate shaper/policer could ensure that other slices/bearers of the same UE get their fair share of resources even if applications on one slice are not responsive to congestion signals. |
| Samsung | Yes | Based on RAN feedback, it seems feasible to perform slice based data rate enforcement in RAN. |
| AT&T | YES | If RAN WGs allow it |
| NTT DOCOMO | Yes | If RAN WGs agree to support it. |

Question 3) Whether PCF based solution (Category B) should be supported for KI#3:

| Company Name | Company View (Yes/No) / (Option A/Option B) | Notes(Justifications) |
| --- | --- | --- |
| Nokia | Only if RAN does not agree to support the solution category in question 2 | It fragments the rate. If this was a good option it would have been adopted for UE AMBR also, |
| Ericsson | Yes | A PCF based solution has minimal impacts (impacts only PCF and entity providing the quota e.g. O&M), while it can be enhanced in a generic way e.g. providing accuracy by considering the inactivity in UP to know whether a PDU session is active or not. |
| Samsung | Yes | Based on RAN feedback, it’s not clear if UL enforcement can be done by RAN. If not, CN assistance is needed. |
| AT&T | YES |  |
| NTT DOCOMO | Yes | If RAN WGs does not agree to support the RAN-based solution in Q2 above. |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.2	Key Issue #5: Dynamic adjustment to meet the limitation of data rate per network slice in UL and DL

### 1.2.1	Issue Description

For key issue 5 we have categorized the solutions into 3 categories

-	Category A with enforcement of Slice max bit rate for each UE in RAN (#14,#25).

-	Category B with enforcement of Slice max bit rate in control plan function to control that the accumulate bit rate for all PDU sessions within the Slice do not exceed the Slice max bit rate.(#12,#18, #19, #20, #24).

-	Category C with enforcement of slice max bit rate in the user plane by distributing a quota to UPF for enforcement.(#16).

### 1.2.2	Companies View

Question 1) Whether RAN based solution (Category A) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Nokia | YES | It is allowing UL control and limit fragmentation more than solutions relying on session AMBR. The alternative could be to just enforce at an interconnection point (outside scope of 3GPP) |
| Ericsson | No | Feedback from RAN needs to be considered. A RAN based solution would make the scheduling at RAN level inefficient, and it would require RAN to drop packets already transmitted over the air. See comments to KI3 question 2). |
| Samsung | No | It is based on authorized bit rate. |
| AT&T | YES | If RAN WGs allow it |
| NTT DOCOMO | Yes | If RAN WGs agree to support it. |

Question 2) Whether PCF based solution (Category B) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Nokia | Only if RAN does not agree to support the solution category in question 2 | We should choose a solution reusing KI#3 The alternative could be to just enforce at an interconnection point (outside scope of 3GPP) |
| Ericsson | Yes | PCF based is solution is preferred, instead of other control plane-based functions. |
| Samsung | No | It is based on authorized bit rate. |
| AT&T | YES |  |
| NTT DOCOMO | Yes | If RAN WGs does not agree to support the RAN-based solution in Q2 above. |

Question 3) Whether UPF based solution (Category C) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Nokia | NO | This is notallowing UL control over the Radio interface The alternative could be to just enforce at an interconnection point (outside scope of 3GPP) |
| Ericsson | No | A description on how the PCF learns about the service distribution in a slice, that is, the amount of traffic that each UPF handles is not mentioned. |
| Samsung | Yes | UPF based solution can support enforcement of actual bit rate. |
| AT&T | NO |  |
| NTT DOCOMO | No |  |

### 1.2.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.2.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.3	Key Issue #6: Constraints on simultaneous use of the network slice

### 1.3.1	Issue Description

For this key issue several solutions(#26, #27, #28,#39) propose that UE is provided with a new rejection cause value of the S-NSSAI, to indicate that it is mutually exclusive to one or more of the S-NSSAIs in the Allowed NSSAI.

Serveral solutions(#27,#28, #41,#42) proposes that the UE is provided with network slice incompatible information per slice so the UE can efficiently use them to determine the Requested NSSAI. The network slice incompatible information per slice is provided together with Configured NSSAI or together with the Allowed NSSAI

Solution#40 proposes that the UE is provided with network slice incomptible information per SUPI/GPSI.

Some solutions proposes that the slice incompatible information is determined based on SLA, or on UE subscription. There is need to decide  how this slice incompatible information is determined.

Question to rapporteur: Solution #26 provides information to the network to enable a more efficient network selection of S-NSSAIs. However, there is no question regarding such type of solutions e.g. "Assuming the network is in control of selection of Allowed NSSAI, does the network benefit of getting more information from the UE to enable an efficient selection of S-NSSAIs for the Allowed NSSAI?". Is it assumed to leave such discussions to the SA2#143E meeting?

### 1.3.2	Companies View

Question 1) In addition to the current Rel-15/16 support in the network,whether the UE should additionally be provided with a rejection cause value of the S-NSSAI, to indicate that it is mutually exclusive to the Allowed NSSAI?

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| Nokia | yes | This is needed to avoid the UE assuming this is not a supported slice in PLMN or in the RA. |
| NEC | YES | This is needed to reject the UEs that has requested access to use a network slice that is incompatible with an already another one in use. This use case also applies to UEs that have been provided with the per slice incompatibility information. |
| Ericsson | Yes. See comments | If the slices that have mutual exclusivity usage are PLMN wide, then depending on the number of slices, available for a specific UE, a reject cause is sufficient. Providing more information to the UE would only be beneficial if there are many UEs that have many subscribed S-NSSAIs that are mutually exclusive from each other or if there is also a need to separate the handling in the UE. |
| LGE | Yes | To help the UE understand the cause on a reject |
| MediaTek | Yes | Cause value indicating the reason for rejection could be useful so the UE is still able to request the SNSSAI later |
| Samsung | No (additional information can be provided to the UE, but it’s not rejection) | We think slice coexistence can be ensured during SM procedure, and minimum impact on MM procedure is preferred. The Allowed NSSAI can be determined as it is, i.e. those S-NSSAIs which are not compatible each other can be included in the Allowed NSSAI. The UE logic already supports selection of S-NSSAI among Allowed NSSAI to request a PDU session. In addition, additional information regarding slice compatibility can be provided to the UE, so that the UE can also refer to the slice compatibility information when selecting a S-NSSAI among Allowed NSSAI to request a PDU session. In short, the UE is in control of selection of S-NSSAI during SM procedure based on the additional information provided by the network. |
| AT&T | YES |  |

Question 2) In addition to the current Rel-15/16 support in the network, whether the UE should be additionally provided with network slice incompatible information so the UE can efficiently use them to determine the Requested NSSAI. If the answer is YES, please indicate how it is done

| Company Name | Company View (Yes/No) | Notes(Justifications) If the answer is YES, please provide whether the network slice incompatible information is provided together with the Configured NSSAI, or together with the Allowed NSSAI, or per SUPI/GPSI |
| --- | --- | --- |
| Nokia | YES | The UE gets a simultaneous USE calls that is in the UDM for the slices it subscribes to when it registers with the network. |
| NEC | YES | The UE is provided with the network slice incompatibility for simultaneous usage attribute per network slice and the UE considers it when it needs to trigger a new PDU session (i.e. the UE does not trigger a PDU session on network slice that is incompatible for simultaneous usage with a network slice with an already active PDU session). |
| Ericsson | See comments | Providing more information to the UE would only be beneficial if there are many UEs that have many subscribed S-NSSAIs that are mutually exclusive from each other and the S-NSSAIs are dedicated to some application that the network cannot derive or if there is also a need to separate the handling in the UE. If there will be such UEs, then we prefer the SUPI approach. This approach is preferred when simultaneous network slice usage is subscriber based. It does not require UE to declare what it supports to the network nor requires any coordination between VPLMN and HPLMN for upgrades since it is backward compatible with existing rel15/Rel16 procedures and mechanism for allowed/configured/subscribed slices. What is not understood is just ignored. The solution #40 also allows the UE to separate the handling and resources, e.g. user data, inside the UE for S-NSSAIs that are incompatible. |
| LGE | NO |  |
| MediaTek | No | Not necessary. Rejection cause is sufficient. Other procedures ought to remain unaffected. |
| Samsung | No, but conditionally Yes only if slice coexistence needs to be ensured during MM procedure. | We think slice coexistence can be ensured during SM procedure. In such case, our view is “No”. But, if slice coexistence needs to be ensured during MM procedure, additional information can be provided to the UE, so that the UE can manage to use a subset of Configured NSSAI (i.e. compatible slices only) when generating Requested NSSAI. In short, the UE is in control of selection of S-NSSAI during MM procedure based on the additional information provided by the network. |
| AT&T | YES | It could provide additional flexibility to the UE in managing sessions from applications on incompatible slices. |

Question 3): How do the home and serving networks determine the network slice incomptible information, Option A) based on SLA; Option B) based on UE subscription; C) based on both SLA and UE subscription

| Company Name | Company View (Option A/Option B/Option C) | Notes(Justifications) |
| --- | --- | --- |
| Nokia | OPTION B | This is a per UE policy hence this is something based on subscription. Different UEs in same slice should be able to recive different constraints. This is also simplert than by SLA which nees update (roaming agreement update!) if ther ei a change in policy in HPLMN. |
| NEC | Option B | We agree with Nokia that the incompatibility attribute is per UE which allowes different UEs to have different incopatibillity attribute for the same network slice. This actually is one of the aims of this incopatibility attribute to allow different levels of isolation/security not only per network slice but per UE as well. So, it should be a subscription parameter. |
| Ericsson | Option A | Based on SLA |
| LGE | Option C | For more flexible way |
| MediaTek | Option A | We fail to see why this would be a subscription matter. In our understanding, slice incompatible information, if any, is an SLA aspect only. |
| Samsung | Option A | In our view, slice incompatibility is operator policy due to e.g. the network deployment or SLA between operator and 3rd party service provider. The network slicing operation based on SLA is already done for mapping of NSSAI. Mapping of NSSAI is configured in NSSF of VPLMN. We think similar mechanism can be applied for slice incompatibility. |
| AT&T | Option C |  |

### 1.3.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.3.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.4	Key Issue #7: Support of 5GC assisted cell selection to access network slice

### 1.4.1	Issue Description

For this key issue several UE based solutions(#29,#30) propose that UE is provided with frequency band information per network slice in the Configured NSSAI so the UE can efficiently select proper cell before access the network.

For network based solutions, sol#44 has been supported in Rel-16 and has no impact on the system. But whether it is sufficient for KI#7 depends on RAN WG feedback.

For other network based solution, Sol#17 and Sol#46 propose to steer the UE to prefered frequency band during the Registration procedure, and Sol#31 proposes to steer the UE to prefered frequency band UE during the PDU Session procedure. Sol#45 propose to generate Allowed NSSAI by considering the UE radio capability.

### 1.4.2	Companies View

Question 1) Whether the UE based solutions should be supported for KI#7:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Nokia | YES | This is specially useful for cell selection (before the UE has contacted the network and received priorities |
| NEC | Yes | This can allow the UE to reselect before accessing the network. |
| OPPO | Yes | Neither the solution#29 nor the solution #30 is supported RAN2 is also discussing the AS based solution (e.g. the supported slice information is broadcasted in the SIB). This can also be used for the cell selection. We believe that frequency band information is AS impact and should avoid the NAS impact as less as possible. |
| Ericsson | See comments in Notes | The existing 5GS already support the ability to steer UEs to preferred frequencies and also to partition resources, e.g. in NG-RAN, such that some resources are dedicated to a certain S-NSSAI. The scenario of reserving a specific frequency for an S-NSSAI and not letting other S-NSSAI be used on the same frequency would most likely not be a normal usage for multiple S-NSSAIs as it also makes an inefficient use of radio spectrum. A UE based solution impacting the UEs and also completely changing the principles and network planning without the ability to control non-supporting UEs is not realistic. Therefore, at minimum a network-based solution without UE impacts would anyway be required, if reserved frequencies for specific S-NSSAIs is to be supported. |
| LGE | Yes | Considering both “UE based” and “Netwrok based” |
| MediaTek | No | “Proper cell” is misleading in the above. We see no reason nor requirements for changing cell selection that could also lead to undue increased interference in the network. The network can direct the UE to appropriate spectrum if it sees fit. This is required to handle legacy Rel-15/16 UEs in any case. |
| Samsung | Yes | A UE based solution can be the most efficient way of achieving this. |
| AT&T | YES |  |

Question 2) Whether the network based solution(#17, #31,#45,#46) should be supported for KI#7

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| Nokia | YES | It is useful to enable per UE and across UE input in cell reselection, and also to allow the network to steer the UE to the right band if this is feasible. |
| NEC | YES | To allow the network to steer the UE to a cell from different FB or to trigger dual connectivity with a secondary NoteB on another FB. |
| OPPO | Yes | It can be used for the legacy UEs to steer the UE to the right FB or establish the DC with other gNB in a different FB. |
| Ericsson | Yes, see comments | If deployments with reserved frequencies for specific S-NSSAIs is to be supported then at minimum a network-based solution without UE impacts is required and solution #17 is the only available solution with no UE impacts. Regarding solution #31, the principle of preferred frequencies for S-NSSAIs is good. However, what is essentially proposed by solution #31 is also provided by solution #44 without any impacts to the system i.e. it is a matter of appropriate RRM strategy applied by NG-RAN. |
| LGE | Yes | Considering both “UE based” and “Netwrok based” |
| MediaTek | Yes | Compatibility with Rel-15/16 UEs is necessary. This implies network-based solution without UE impact is the only acceptable way forward. |
| Samsung | Yes | A network based solution is needed to support legacy UEs. We think solution #17 can be considered for normative work. Other UE based solutions that require DC capability can’t be the general solution to this key issue since the DC is optional capability. |
| AT&T | YES |  |
| NTT DOCOMO | Yes |  |

### 1.4.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.4.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.