Pre SA2#143E e-meeting Email Discussion

Source: 	<Jinguo Zhu/ZTE>

Title: 	<Email discussion on FS_eNS_Ph2>

# 1.	Issues for FS_eNS_Ph2

## 1.1	Key Issue #3: limitation of data rate per network slice in UL and DL per UE

### 1.1.1	Issue Description

For key issue 3 we have categorized the solutions into 3 categories

-	Category A1: Those enforcing the Slice-MBR in the UPF, in CN i.e. solution #13.

-	Category A2: Enforcing SMBR in the RAN and also admitting GFBR aggregate for the slice only up to the SMBR at the admission control time in the RAN, i.e. solution #22,

-	Category B: Those ensuring that the Slice-MBR limits the aggregated MBR and GBR for QoS flows of established PDU sessions and related QoS flows, i.e. solution #20, #21 and #37. Enforcement is done using the existing QoS parameter

### 1.1.2	Companies View

Question 1) Whether UPF based solution (Category A1) should be supported for KI#3。

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| T-Mobile USA | No | See ques 2 answer |

Question 2) Whether RAN based solution (Category A2) should be supported for KI#3:

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| T-Mobile USA | Yes | RAN already enforces UE-AMBR. No restriction on using same PCF/SMF/UPF for all PDU sessions in a slice. |

Question 3) Whether PCF based solution (Category B) should be supported for KI#3:

| Company Name | Company View (Yes/No) / (Option A/Option B) | Notes(Justifications) |
| --- | --- | --- |
| T-Mobile USA | No | See ques 2 answer |

### 1.1.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.1.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.2	Key Issue #5: Dynamic adjustment to meet the limitation of data rate per network slice in UL and DL

### 1.2.1	Issue Description

For key issue 5 we have categorized the solutions into 3 categories

-	Category A with enforcement of Slice max bit rate for each UE in RAN (#14,#25).

-	Category B with enforcement of Slice max bit rate in control plan function to control that the accumulate bit rate for all PDU sessions within the Slice do not exceed the Slice max bit rate.(#12,#18, #19, #20, #24).

-	Category C with enforcement of slice max bit rate in the user plane by distributing a quota to UPF for enforcement.(#16).

### 1.2.2	Companies View

Question 1) Whether RAN based solution (Category A) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| T-Mobile USA | No | See answer to ques 2 |

Question 2) Whether PCF based solution (Category B) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| T-Mobile USA | Yes | Prefer a PCF based (solution 20) or new NF based solution (solution 12, 18, or 24). |

Question 3) Whether UPF based solution (Category C) should be supported for KI#5:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| T-Mobile USA | No | See answer to ques 2 |

### 1.2.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.2.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.3	Key Issue #6: Constraints on simultaneous use of the network slice

### 1.3.1	Issue Description

For this key issue several solutions(#26,#28,#39) propose that UE is provided with a new rejection cause value of the S-NSSAI, to indicate that it is mutually exclusive to one or more of the S-NSSAIs in the Allowed NSSAI.

Serveral solutions(#27,#28, #41,#42) proposes that the UE is provided with network slice incompatible information per slice so the UE can efficiently use them to determine the Requested NSSAI. The network slice incompatible information per slice is provided together with Configured NSSAI or together with the Allowed NSSAI

Solution#40 proposes that the UE is provided with network slice incomptible information per SUPI/GPSI.

Some solutions proposes that the slice incompatible information is determined based on SLA, or on UE subscription. There is need to decide  how this slice incompatible information is determined.

### 1.3.2	Companies View

Question 1) In addition to the current Rel-15/16 support in the network,whether the UE should additionally be provided with a rejection cause value of the S-NSSAI, to indicate that it is mutually exclusive to the Allowed NSSAI?

| Company Name | Company View (Yes/No) | Notes(Justifications) |
| --- | --- | --- |
| T-Mobile USA | No | Prefer solution where network does not send any new information to UE. |

Question 2) In addition to the current Rel-15/16 support in the network, whether the UE should be additionally provided with network slice incompatible information so the UE can efficiently use them to determine the Requested NSSAI. If the answer is YES, please indicate how it is done

| Company Name | Company View (Yes/No) | Notes(Justifications) If the answer is YES, please provide whether the network slice incompatible information is provided together with the Configured NSSAI, or together with the Allowed NSSAI, or per SUPI/GPSI |
| --- | --- | --- |
| T-Mobile USA | No | Prefer solution where network does not send any new information to UE. |

Question 3): How do the home and serving networks determine the network slice incomptible information, Option A) based on SLA; Option B) based on UE subscription; C) based on both SLA and UE subscription

| Company Name | Company View (Option A/Option B/Option C) | Notes(Justifications) |
| --- | --- | --- |
| T-Mobile USA | Option C |  |

### 1.3.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.3.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.

## 1.4	Key Issue #7: Support of 5GC assisted cell selection to access network slice

### 1.4.1	Issue Description

For this key issue several UE based solutions(#29,#30) propose that UE is provided with frequency band information per network slice in the Configured NSSAI so the UE can efficiently select proper cell before access the network.

For network based solutions, sol#44 has been supported in Rel-16 and has no impact on the system. But whether it is sufficient for KI#7 depends on RAN WG feedback.

For other network based solution, Sol#17 and Sol#46 propose to steer the UE to prefered frequency band during the Registration procedure, and Sol#31 proposes to steer the UE to prefered frequency band UE during the PDU Session procedure. Sol#45 propose to generate Allowed NSSAI by considering the UE radio capability.

### 1.4.2	Companies View

Question 1) Whether the UE based solutions should be supported for KI#7:

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| T-Mobile USA | No | See question 2 answer |

Question 2) Whether the network based solution(#17, #31,#45,#46) should be supported for KI#7

| Company Name | Company View (Yes/No) | Notes(Justifications) If Yes please identify which solutions are prefered |
| --- | --- | --- |
| T-Mobile USA | Yes | Support solutions where RAN steers UE to proper slice and do not support solutions where Core Network sends any new freq band information to UE. Prefer solutions 17, 44, 45, 46 |

### 1.4.3	Summary

Editor’s Note: This clause should contain the brief summary of companies view e.g. n# of companies prefer to go with option A vs. m# of companies prefer to go with option B.

### 1.4.4	Proposed Way Forward

Editor’s Note: This clause should contain propose a way forward. For e.g. Given that majority of companies prefer to go with option A, it is proposed that Option A is agreed as way forward.